## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)‏
Submission Title: [Comment Resolution Palm Springs – MAC and Frames]
Date Submitted: [May 2011]
Source: [Ben Rolfe]
Company [BCA]
Address [n]
Voice: [], FAX: [], E-Mail: [ben @ blindcreek . com]
Re: [Comment Resolution]
Abstract: [This document intends to resolve comments received in LB70]
Purpose: [This document provides a list of the editing staff that will be working on 802.15.4g.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: LB 70 Comment Resolutions: CID # 151, 221,
15-11-0392-00-004g

## Slide 3: CID # 151
Commenter points out that the relevance of the enhanced ACK with respect to the 4g PHYs. We lost the rational
Initial suggestion was to provide an explanation of the relevance of discussing EA in 4g….
I couldn’t….

## Slide 4: CID # 151
What we had said before:
  In Draft 2, we provided an indication in the capabilities exchange that a device may require the timing of the enhanced acknowledgement (which we called “delayed acknowledgement” in D2) and that if so signaled a device will respond to that device with only with the appropriate acknowledgement.
  In Draft 3 we changed the indication to signal that the device supports the enhanced acknowledgement, and don’t say how a devices should use this information
Question: is there still anything we need to say?
  Short answer: probably not!

## Slide 5: CID # 151
Why did we need this (why was this relevant to the new PHYs)?
  The original issue: A device implementing some SUN PHYs may require more than aTurnaroundTime symbol periods (as specified in 802.15.4-2006) to generate an acknowledgement do to additional processing required by some PHY modes.
But now…
  The previous ACK timing spec (2006) did not consider PHY differnces as it was before addition of 3 new PHYs
  As part of the roll-up (4i), this was changed so that there is a PHY dependence introduced
  In the current 4g draft (D3), the ACK response time is adjusted to be appropriate (in a PHY dependent way) to all SUN PHYs.
So….
  Conclusion: use of enhanced ACK to accommodate PHY timing differences is no longer necessary. It is still available (as part of the 15.4 MAC per amendment 4e) but we don’t need to explicitly say so.
  We can accept the comment and remove the references to enhanced ACK

## Slide 6: CID # 151
Alternative (as initially suggested):
  Provide a paragraph explaining why we are calling out enhanced ACK, i.e. specifically why the revised ACK timing as specified in 15.4i-D9 isn’t enough, and figure out where to put it.
  I don’t have enough information to write that paragraph yet.

## Slide 7: CID #221
Comment notes that the Eqn. for macAckWaitDuration for MR-QPSK PHY (Page 30, Line 35) is confusing, and questions the meaning of the variable ‘K’. Upon review several issues exist with the equation:
“K” is almost “LENGTH” in the OFDM version.
“phyPSDUDuration as a function of K is given in 16.3.2.14” is not completely obvious following the link
The actual length of the PSDU for an ACK may be variable. This affects the maximum wait duration

## Slide 8: CID #221
“K” isn’t quite the same here as “LENGTH” in the OFDM version:
  In this case, this was specifically the length of an ACK frame, which is assumed to be a legacy ACK which has no MAC Payload)
  LENGTH is more generally PSDU length.
The actual length of the PSDU for an ACK may be variable. This affects the maximum wait duration
  So the assumption that an ACK is fixed size is not true. This would also affect the determination of macAckWaitDuration in all cases (based on the addition of enhanced ACK).

## Slide 9: CID #221
macAckWaitDuration =
aUnitBackoffPeriod + aTurnaroundTime + phySHRDuration + phyPHRDuration + phyPSDUDuration(LENGTH)
Option A (always corret):
where LENGTH is the maximum number of octets in an Acknowledge frame, and phyPSDUDuration(LENGTH) is given in 16.3.2.14.
Option B (just as wrong as everywhere else):
where LENGTH = 5 when macFCSType = 1 and LENGTH = 7 when macFCSType = 0, and phyPSDUDuration(LENGTH) is given in 16.3.2.14.

## Slide 10: Ripple
macAckWaitDuration in all other places is also valid only for a legacy (15.4-2006) Acknowledge frame.
Options:
  Fix it everywhere as in “A” on prior slide;
  Assume only legacy ACK for now (comment on 4e sponsor to ripple as part of new ACK)
  Leave it for the next roll-up (since it is going to be also wrong for all other PHYs)