## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title:[Fragmentation Ideas for Discussion]
Date Submitted: [May 11, 2011]
Source:[Ben Rolfe]
Company [BCA]
Address []
Voice: [+4.408.395.7207], FAX: [None], E-Mail: [ben @ blindcreek.com]
Re:[]
Abstract:[Fragmentation Ideas for group discussion ]
Purpose:[Stimulate thought in the task group]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Summary
Why Fragment
MSDU to multiple MSDU overhead examples
Ideas for optimization

## Slide 3: Why Fragment?
Inspired by 15-11-0348
  Burst packet: Fragmentation and reassembly with fragment level retry
  Substantial improvement in real world reliability
  Reduction in use of air time
    Smaller chunk less vulnerable to interference and changing channel conditions
    Retransmit smaller increments = less retry overhead
    Reduce interference foot print (we breath between chunks in a burst)

## Slide 4: Why Fragment? (Restatement of the Obvious)
When over the air data rate goes down, time on the air goes up
Longer transmission time -> more time for things to go wrong
Longer transmission time blocks other channel uses longer

## Slide 5: Why Fragment? (Restatement of the Obvious)
Examples:
Example | PSDU, Octets | Time @ 1kbps
802.15.4 thru 2010 | 127 | 1016ms
Ethernet MTU | 1518 | 12144
802.15.4g | 2047 | 16376
802.11 | 4095 | 32760

## Slide 6: MSDU -> multiple MPDUs MAC Frame Overhead
802.15.4 (pre 802.15.4e) (some examples):
  Min: FCTL[2] + Seq#[1] + MinAddr[2] +FCS[2] = 7
  Nominal: Min + Long Src [4] + Long Dest [4] = 15
  Secure: Nominal + 14 = 29 octets
14 fragments * 14 overhead = 196 = 14%

## Slide 7: MSDU -> multiple MPDUs MAC Frame Overhead
802.15.4e
  Min: FCTL[2] + FCS[2] = 4
  Nominal: Min + Short Address [2] = 6
13 fragments * 6 overhead = 78= 6%

## Slide 8: What if…
Can compress MHR?
  Addressing map to short address (2)
  Control information suppression
State vs Stateless?
  Explicit stateless: everything in every packet
  Stateful: keep track of all things
  Inferred state: known rules or characteristics that make state known

## Slide 9: Conceptual Example
Leverage existing MAC features
  Lots of implementations
  Flexible
  Adaptable to multiple PHYs already
Even Lower Data Rate (ELDR) PHY
  OTA packet resolution < 20ms @ 1kbps (< 200 bits)

## Slide 11: Closing
Fragmentation is a good thing for ELDR PHYs
Think about fragmentation in the MAC
  Optimized for the ELDR PHY(s)
  Compatible with existing MAC concepts

## Slide 12: Thanks for your Attention!