## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [IEEE 802.15.4-2011 and TG4e Overview]
Date Submitted: [18 July 2011]
Source: [Patrick Kinney] Company [Kinney Consulting LLC]
Address [Chicago area, IL, USA]
Voice:[+1.847.960.3715], E-Mail:[pat.kinney@ieee.org]
Re: [Information on TG4e and TG4i for July 2011 Session]
Abstract: [Information on TG4e and TG4i for July 2011 Session]
Purpose: [To assist TG4k group in drafting LECIM amendment]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: TG4i/802.15.4-2011
Revision of 802.15.4-2006 to include TG4a, TG4c, and TG4d
Included corrigenda items from TG4h
Substantial editorial changes for clarity and future amendments
MAC amendment to 802.15.4
Originally intended to amend 802.15.4-2006 to
  better support the industrial markets, and
  permit compatibility with modifications proposed within the Chinese WPAN
Now amends TG4i/802.15.4-2011 and also includes changes to address TG4f and TG4g application needs
TG4e

## Slide 3: 802.15.4-2011 Major Changes
Rolled TG4a, TG4c, and TG4d into 802.15.4
Includes corrigenda (d1P802-15-4-2006_Cor1.pdf)
Merged definitions and acronyms into clause 3
Reversed PHY/MAC order, now starts with MAC
Split MAC/Security clause into 3 clauses: MAC protocol, MAC services, and Security
Eliminated MAC enumeration values
Security has been rewritten for accuracy and clarity
Split PHY clause into 8 clauses (general requirements, services, and 6 specific PHYs)
Eliminated Coexistence Assurance Annex E

## Slide 4: TG4e major changes
Deterministic & Synchronous Multi-channel Extension mode
Time Slotted Channel Hopping mode
Low Latency Deterministic Network mode
Additional Frame Formats
Low Energy mode
Enhanced Beacon behavior
Information Elements
Miscellaneous

## Slide 5: Deterministic & Synchronous Multichannel Extension (DSME)
Support of industrial applications and commercial applications which need deterministic latency and higher link reliability
Operation
  DSME-enabled network runs on beacon-enabled PAN. All devices synchronize multi-superframe via beacon frame.
  Multi-superframe enhances GTS operation in 15.4-2006 by grouping multiple superframes, and also extends single channel operation during CFP to multi-channel operation either by adapting (switching) channels or by hopping channels.
  A pair of peer devices wakes up at a reserved GTS slot(s) to exchange a data frame and an ACK frame.

## Slide 6: Time Slotted Channel Hopping (TSCH)
Process Automation applications with a particular focus on equipment and process monitoring
Operation
  All devices in the same network synchronize slotframes
  All timeslots are contained within a slotframe cycle
  Timeslots repeat in time: the slotframe period
  Device-to-device communication within a timeslot includes packet Tx/Rx & ACK Tx/Rx

## Slide 7: Low Latency Deterministic Network (LLDN)
Support of factory automation and process automation e.g. automotive robots/suspension tracks, machine tools milling/turning/robot revolver
Uses beacon and assigned time slots to provide determinism
Designed for small networks and small frames
Substantial reduction in MAC overhead to allow very small superframes, hence reduced device latencies
Includes a Group ACK function to reduce bandwidth needs

## Slide 8: Additional Frame Formats
New frame type to accommodate LLDN networks
  Reduced overhead
Added multipurpose frame that:
  Accommodates TG4f (Tx only devices), Low Energy mode, etc.
  Reduce overhead, e.g. MAC overhead for an TG4f type frame can be as low as 4 octets (MAC overhead was 11 octets with the previous frame type)
  Provides configurability and extensibility

## Slide 9: Low Energy
IP-centric Sensor Networks
  Creates illusion of Always On, Low Latency, Multicast Capable, Synchronous Acks
Coordinated Sampled Listening (CSL)
  Receiver periodically performs channel sampling for radio traffic
    Every macCSLPeriod (ms)
  Sender transmits wakeup frame sequence prior to payload frame
    Full wakeup sequence (macCSLMaxPeriod) if unsynchronized with receiver, i.e., first time to send to the receiver
    Short wakeup sequence for guard time if synchronized with receiver
  Tradeoff between latency and energy consumption
Receiver Initiated Transmission (RIT)
  Receiver periodically broadcasts datareq frames and listen for a short amount of time (macRitDataWaitPeriod) for incoming transmissions every macRitPeriod
  Sender waits until receiving datareq frame from receiver then immediately transmit payload frame
  Works better when higher latency can be tolerated and works with regulations which limit continuous transmission duration (e.g., Japan)

## Slide 10: Enhanced Beacon & Enhanced Beacon Requests
Enhanced beacon includes ability to carry additional information in beacons (IEs).
Enhanced beacon request includes respondent filters and generalized information query capability

## Slide 11: Information Elements (IEs)
Simple, extensible, flexible information container
Allows adding information to existing frame format without adding new frame type
Managed and unmanaged ID spaces allows flexibility
Already being utilized by TG4g and TG4f

## Slide 12: Miscellaneous
Fast Association
  This mode allows a device to send and association response in direct communication eliminating a delay in the current indirect communication association response command
Network Metrics
  Added attributes macRetryCount, macMultipleRetryCount, macTXFailCount, macTXSuccessCount relate to data frame transmission
  Added attributes macFCSErrorCount, macSecurityFailure, macDuplicateFrameCount, macRXSuccessCount relate to data frame reception
Enhanced Acknowledgement Frames
  Allow ACKs be secured, include payloads, and a configurable delay to allow devices sufficient time to decrypt, etc
Channel Diversity
  Provides support for Channel Hopping via Hopping Sequence PIB and a default hopping sequence

## Slide 13: Summary
Transformed 802.15.4 into an easier to read, more extensible standard
Substantial additions to enable “managed” networks (such as DSME, TSCH, LLDN) to exhibit deterministic behavior, accommodate a large number of devices, better manage network behaviors
Additional protocol behaviors that can facilitate longer battery life, faster response times, etc