## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Preliminary Proposal for FHSS PHY for 802.15.4k]
Date Submitted: [18 July 2011 ]
Source: [Matt Johnson] Company [Itron]
Address [2111 N Molter RD, Liberty Lake, WA 99019, USA]
Voice:[+1 509-891-3364], FAX: [+1 509-891-3896], E-Mail:[matt.johnson@itron.com]
Re: [ Response to CFP issued 10 May 2011, document 15-11-0147-02-004k]
Abstract: [This document describes a FHSS PHY that addresses the requirements of the 802.15.4k PAR]
Purpose: [Preliminary proposal for consideration of inclusion into 802.15.4k PHY.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Agenda
Background
FHSS System
  Channel Coherence
  Coexistence
Link Budget
MAC Considerations

## Slide 3: Background: AMI Performance Expectations
20+ Year Endpoint Battery Life
  All the electronics, not just the radio
  Single Lithium-thionyl chloride A Cell (3.6 Ah)
Relatively Low Latency
  5 minutes
99% Hourly Read Reliability
High link budget to support up to 100k endpoints/concentrator
Support for worldwide deployment

## Slide 4: Background: Battery Considerations
Relatively Higher data rate = less TX & RX Time
  Relative to the PAR guidance
  Longer endpoint battery life
Optional unacknowledged uplink TX
  Endpoint RX larger consumer of battery than TX

## Slide 5: Two Ways to get to a High Link Budget
Broadband Spread Spectrum Systems
  Robust against interference through processing gain
Narrowband Systems
  Higher link through minimizing noise and interference
  Simpler to implement for low cost devices

## Slide 6: Why FHSS?
Frequency Diversity
  Effective for diversity reception
  Provides greater degrees of freedom in concentrator receiver design for high capacity systems
  Greater concentrator deployment flexibility
    Single antenna on tower – lower cost
    No tower-mounted electronics – high reliability
Narrow-band FHSS has proven to have a high degree of interference immunity

## Slide 7: Example Parameters
Narrowband FHSS System
  ≥ 100 Channels (915 ISM)
Channel BW of 100 to 200 kHz
Data Rate (based on 915 MHz ISM band)
  Uplink 35 to 40 kbps
  Downlink 10 to 40 kbps
FSK/GFSK Modulation

## Slide 8: Channel Coherence
Based on measured PSR (in the real world):
  In the 915 MHz band, we estimate channel coherence at 18 to 20 mSec
Interference
  In 915 ISM there are a wide variety of non-standards-based systems
Ricean fading environment

## Slide 9: Data Rate
Asymmetric data rates
  Relatively higher uplink rate
    Maximize payload for given channel coherence
  Lower downlink rate
    Lighten the load on limited endpoint computing resources
    Typical download payloads are significant smaller and less frequent in AMI and sensor networks
    Enable narrow bandwidth for improved interference immunity

## Slide 10: Coexistence
By low duty cycle
Energy Detection impacts battery life
Follow the ETSI philosophy from the SRD rules:
  LBT or Duty Cycle Limits if LBT not implemented

## Slide 11: Bands
915 MHz
868 MHz
2.4 GHz
Perhaps other regional bands?
  Will be defined in September Proposal

## Slide 12: 915 MHz Link Budget
Based on multiple network deployments
No single number can adequately describe penetration loss:
further discussion in the link budget session.

## Slide 13: 868 MHz Link Budget
Non Specific Use, 25 mW, ≤100 kHz Channels (ETSI )., 1 km range
Non Specific Use, 500 mW, ≤ 25 kHz Channels(ETSI ), 2 km range

## Slide 14: MAC Considerations
Chart: Histogram of Packet Payload Length
| 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60 | 64 | 68 | 72 | 76 | 80 | 84 | 88 | 92 | 96 | 100
Uplink | 0 | 0 | 7 | 14 | 20 | 5 | 6 | 3 | 1 | 0 | 0 | 2 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Downlink | 1 | 0 | 22 | 20 | 6 | 2 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Typical Operational Payloads are Relatively Small

## Slide 15: Conclusion
PAR can be met with both narrowband and broadband approaches
Expect to present a full proposal in September
  Welcome the opportunity merge with other narrowband proposals