## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: 802.15.4k Channel Model Proposal
Date Submitted: July 19, 2011
Source: Sourav Dey, On-Ramp Wireless
Re: 802.15.4k
Abstract: This presentation summarizes the discussions of channel model subgroup since the April, 2011 802.15.4k meeting in Palm Springs. It addresses various channel characteristics that should be addressed by LECIM PHY proposals. In addition, it proposes a potential RF path loss model.
Purpose: Propose a LECIM channel model for use in evaluating PHY proposals.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 802.15.4k LECIM Channel Model Update
7/19/2011

## Slide 3: Purpose
Summarize current state of channel model
  Identify key characteristics of LECIM channel
  Ideas shared on TG4k conference calls
  Ideas shared on TG4k Reflector
References
  DCN-802.15-11-0464-00-004k
  DCN-802.15-11-0465-00-004k
  DCN-802.15-11-0507-00-004k

## Slide 4: Basic Assumptions
Focus on star topology, e.g. endpoint <-> collector
Focus on outdoor propagation with (optional) additional loss due to penetration into underground vaults, etc.

## Slide 5: RF Path Loss Model
    Range is king!
      Coverage into difficult locations is stated goal of LECIM PHY.
      PHY proposals will be evaluated in part on the coverage they can get which still supporting the desired bit-rate (< 40 kbps)
    Possible Scenarios
      Underground vault from utility-pole height antenna
      Pad mount transformer from a cell-tower antenna
      Backcountry sensor from mountaintop antenna farm

## Slide 6: RF Path Loss Model
Frequency
  Dependent on PHY proposal
Transmit Power
  Dependent on regional regulations for frequency band
Antenna Gain
  Dependent on regional regulations for frequency band
    Uplink and Downlink
      Separate path loss calculations for each direction
      Potentially different impairments, antennas, etc.

## Slide 7: RF Path Loss Line Items
Penetration Loss
  Underground Vaults = ~40 dB
  Indoor Sensor Locations = ~20 dB
Shadowing Margin
  Nominal margin of 2s = 16 dB to account for clutter variation
  See DCH 15-11.0375-00-004k for more info
Propagation Loss
  Okamura-Hata Model for 150-1500 MHz
  Cost 231-Hata Model for 1500-2400 MHz
Interference
  Due to out of system interference at advantaged collector
  See DCN 15-11-0074-00-004k for more info

## Slide 8: RF Path Loss Excel Spreadsheet
Channel Model Parameters |  | Notes
Frequency (MHz) | 2400 | Valid Range 150-2400 MHz
Collector Antenna Height (m) | 30 | Valid Range 30-200 m, including terrain.
Endpoint Antenna Height (m) | 1 | Valid Range 1-10 m
Distance (km) | 4 | Valid Range 1-20 km
Downlink Path Loss Calculation |  | Notes
Collector Tx Power (dBm) | 30 | Subject to Tx Power Regulations
Collector Tx Antenna Gain (dBi) | 6 | Subject to Tx Power Regulations
Hata Path Loss (dB) | -162.99 | Must reference the right path loss from the next worksheet
Shadowing Margin (dB) | -16 | To buffer against variable shadowing loss
Penetration Loss (dB) | -10 | For underground vaults, etc.
Endpoint Rx Antenna Gain (dBi) | 2 | If using same antenna for Tx, must be same as in Uplink Table
Endpoint Interference (dB) | 1 | Rise over Thermal Interference
Rx Power at Endpoint (dBm) | -149.99 | Compare against Rx sensitivity
Uplink Path Loss Calculation |  | Notes
Endpoint Tx Power (dBm) | 20 | Subject to Tx Power Regulations. Can be dif from Collector
Endpoint Tx Antenna Gain (dBi) | 2 | Subject to Tx Power Regulations
Penetration Loss (dB) | -10 | For underground vaults, etc.
Hata Path Loss (dB) | -162.99 | Same as Downlink
Shadowing Margin (dB) | -16 | Same as Downlink
Collector Rx Antenna Gain (dBi) | 2 | If using same antenna for Tx, must be same as Downlink
Collector Interference (dB) | 10 | Rise over Thermal Interference
Rx Power at Collector (dBm) | -154.99 | Compare against Rx sensitivity

## Slide 9: Okamura-Hata Propagation Model
Frequencies: 150-1500 MHz
Terrain: Urban, Suburban, Rural
Valid Collector Antenna Height: 30-200m
Valid Endpoint Antenna Height: 1-10m
Distance: 1-20 km
  Equations courtesy of DCN-802.15-11-0507-00-004k

## Slide 10: Cost 231-Hata Model
Frequencies: 1500-2400 MHz
Terrain: Urban, Suburban
Valid Collector Antenna Height: 30-200m
Valid Endpoint Antenna Height: 1-10m
Distance: 1-20 km
  Equations courtesy of DCN-802.15-11-0507-00-004k

## Slide 11: RF Path Loss Excel Spreadsheet
 | City |  |  |  | Suburban |  |  | Open Space |  | 
 | Hata Medium City (150-1500 MHz) | Hata Large City (150-200 MHz) | Hata Large City (200-1500 MHz) | COST Hata Large City (1500-2400 MHz) | Hata Suburban (150-200 MHz) | Hata Suburban (200-1500 MHz) | COST Hata Medium City/Suburban (1500-2400 MHz) | Hata Open Space (150-200 MHz) | Hata Open Space (200-1500 MHz) | Free Space
Antenna Height Correction Factor | -1.45 | -0.81 | -1.31 | -1.31 | x | x | -1.31 | x | x | x
Cost Correction Factor | x | x | x | 3.00 | x | x | 0.00 | x | x | x
Hata Path Loss | 160.22 | 159.58 | 160.08 | 165.99 | 146.71 | 147.20 | 162.99 | 125.98 | 126.48 | 93.58

## Slide 12: Channel Power Delay Profile
  Multipath exists in any wireless system, but low data rate means long symbols which means delay spread << symbol duration
  From analysis in DCN-802.15-11-0507-00-004k propose that PHYs need to be robust to delay spread up to 5 usec
    Robustness can be left qualitative
    E.g. long symbol times for narrowband modulation
    E.g. RAKE receiver for DSSS

## Slide 13: Channel Coherence Time
Coherence time is defined as the time over which the channel auto-correlation is non-zero, i.e. measures time-varying nature of channel
  A robust PHY with low data rate will have long symbols, so it will not be expected that the channel is stationary over a PHY packet.
    Symbol times should be < coherence time
    Each packet should have some protection for this channel variation
    It will be assumed that packets will be lost due to deep fades
    There should be mechanisms at the MAC (or adaptation) layer to mitigate the loss of packets
  Need to characterize the channel coherence times for the bands of interest, e.g. 900 MHz, 2.4 MHz, etc.
    Coherence times for the LECIM channel are similar to stationary cellular channels.

## Slide 14: Interference
  Interference is problem at both the endpoint and collector sites (especially if elevated).
  Interference is mostly caused from other closely located transmitters in or near the same band.
    This is particularly true in unlicensed bands.
    See DCN 15-11-0074-00-004k for more details for the US 2.4 GHz band
    Proposals should consider the rejection of co-channel, adjacent channel, and broadband interference sources.
    Potential Models
      1 MHz broadband noise source with 10 dB Rise over thermal
      100 KHz noise source with 10 dB rise over thermal
      10 KHz noise source with 10 dB rise over thermal
      Pulse jammers with a 250 usec duty cycle

## Slide 15: Changing Link Conditions
  The wireless conditions change over time and this needs to be communicated between the collector and the endpoint.
    Channel characteristics
    Interference conditions
  PHY proposals should be robust to dynamic wireless conditions
    That robustness can be left qualitative
    e.g. adaptation of modulation to changing link conditions, etc.

## Slide 16: Varied Path Loss Between Endpoints
  LECIM devices scattered over a large area
    Possible loss range up to 80 dB between devices
    Difference between devices close to the collector and the disadvantaged devices far from the collector
  Proposals must be robust to large range of path losses
    Robustness can be left qualitative
    Robustness includes dealing with the near-far problem and potential hidden node problems

## Slide 17: Conclusions
Identified Key Characteristics of LECIM Channel
Quantitative where necessary, qualitative where possible
Next Steps
  Need to better understand power delay profiles for longer ranges and particular environments
  Need to better understand channel coherence time
  PHY proposals should address these characteristics for their particular design