## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [FSPL]
Date Submitted: [22 July 2011]
Source: [Ed Callaway] Company [Sunrise Micro Devices/Sensus]
Address [9181 Glades Road, Suite 125, Boca Raton, FL 33434-3941, USA
Voice:[+1-561-608-7537], E-Mail:[ed@sunrisemicro.com]
Re: [4k proposals]
Abstract: [Propagation loss is independent of frequency.]
Purpose: [To improve 4k proposal evaluation.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 802. 15-11-0540-00-004k

## Slide 2: Propagation Loss is Independent of Frequency
Ed Callaway
ed@sunrisemicro.com
doc.: IEEE 802. 15-11-0540-00-004k
Why 2.4 GHz is Just as Good as VHF1
– or –
1 In this regard

## Slide 3: Free Space Path Loss Formula
But free space propagation loss is independent of frequency! How can both be true?
FSPL = (propagation loss)×(receiving antenna aperture)
The receiving antenna assumed in the FSPL is an isotropic antenna. The aperture of an isotropic antenna is frequency-dependent.
Frequency independent
Frequency dependent
doc.: IEEE 802. 15-11-0540-00-004k

## Slide 4: FSPL Formula vs. Propagation Loss
Tx
Rx
Propagation loss
FSPL
Isotropic
Isotropic
FSPL is “coax-to-coax”;
Propagation loss is “antenna-to-antenna”
doc.: IEEE 802. 15-11-0540-00-004k

## Slide 5: Transmitted Power Density
Tx
d
Rx
At a distance d from an isotropic transmitting antenna, the available power per unit area S is
,
(the “inverse square law”).
This is the true “free-space propagation loss.”
doc.: IEEE 802. 15-11-0540-00-004k

## Slide 6: Received Power
Tx
d
Rx
But
due to the frequency-dependent aperture of the isotropic Rx antenna.
doc.: IEEE 802. 15-11-0540-00-004k
,
The aperture of a resonant dipole is also frequency-dependent. Its aperture goes as its length squared and, as the frequency goes up, the dipole gets physically shorter

## Slide 7: Anything You Want. . .
http://en.wikipedia.org/wiki/Free-space_path_loss
doc.: IEEE 802. 15-11-0540-00-004k
Tx
Rx
FSPL goes up with frequency:
Dipole
Dipole
Tx
Rx
FSPL goes down with frequency:
Parabolic dish
Parabolic dish
Tx
Rx
FSPL constant over frequency:
Dipole
Parabolic dish