## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: PSC PAR and 5C subgroup activities
Date Submitted: Aug. 2011
Source: Soo-Young Chang, CSUS
Address:
Contact Information: 530 574 2741 [sychang@ecs.csus.edu]
Re:
Abstract: This contribution is prepared to list activities of PSC PAR and 5C subgroup.
Purpose:
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1

## Slide 2: INTRODUCTION
  This PSC PAR and 5C subgroup was formed in the first teleconference held on Aug. 9, 2011 to prepare the initial PAR and 5C draft.
    Members of this group: Soo-Young Chang (CSUS, leader), Seung Hoon Park (Samsung), Paul (Beom Jin) Jeon (LG), and Sunggeun Jin (ETRI)
  After the first teleconference on Aug. 9, 2011, the following issues are addressed:
    Samsung’s position on a new standard or amendment to 15.3: a new standard
    Samsung’s reasons for a new standard listed
    LG and ETRI’s comments on Samsung’s reasons
Slide 2

## Slide 3: SAMSUNG’S BRIEF REASONS WHY A NEW STANDARD
Major use cases of interest
  Social network service, gaming and advertisement service which require exchanges of discovery messages among many devices in a range of larger than 500m
  Basically all the devices exchanges these messages without a master.
  Hundreds of devices in an area of 500 m range should be discovered with exchanges of relatively short messages.
  Distributed coordination rather than centralized coordination
 With 15.3c’s PNC which is for synchronization and resource control, high scalability can not be achieved to apply to numerous devices in a vast area.
 A new standard is required for proposed use cases.
Slide 3

## Slide 4: LG’S POSITION FOR A NEW STANDARD
LG's position is very clear.
  It does NOT object to going to totally new 15.8
  But it strongly believes 15.3d is enough to support all use cases it suggested.
  So, if we cannot find compelling reasons to make totally new 15.8 in time (but when?), then we should turn back to 15.3d approach.
The key question is "Are there any use cases (i.e. finding friends in a big stadium) which CAN NOT be supported with existing 15.3 MAC or PHY and their minor enhancements?"
Slide 4

## Slide 5: TECHNICAL FEATURES FOR PSC - SAMSUNG
Flat structure (no hierarchy)
  all device can be a broadcast source
  all device should listen the broadcasted discovery message
  no centralized coordination for resource management (e.g. cellular BS, 15.3 PNC)
Scalability
  long range of discovery &amp; short data transmission: 500m to 1km
  # of discovering devices: a thousands
  # of connected devices: a hundreds
  no single point of synchronization source (e.g. cellular BS, Wi-Fi AP, 15.3 PNC)
Slide 5

## Slide 6: TECHNICAL FEATURES FOR PSC - ETRI
Data rate should be supported up to 500 Mbps
High precision localization is required.
Coverage extension should be supported with multi-hop approach.
Fast association need to be realized.
Slide 6

## Slide 7: COMMENTS FROM BUM JIN JEON FOR TECHNICAL FEATURES FOR PSC - SAMSUNG
Flat structure (no hierarchy)
  all device can be a broadcast source
   It can be done with existing15.3. (using Broadcasting address as the target address)
  all device should listen the broadcasted discovery message
   It can be done with existing 15.3. (If the Target address is set as Broadcasting address, they will listen.)
  no centralized coordination for resource management (e.g. cellular BS, 15.3 PNC)
   It can NOT be done with 15.3. There should be a coordinator, but it is NOT designated. The role itself is distributed. So, if the reason for bullet number 3 is compelling, then we might be able to create 15.8. The key question is “Why there should be NO centralized coordination in which use cases?” If such use cases “never” be supported with centralized coordination, then the reason for 15.8 will be really compelling.
Slide 7

## Slide 8: RESPONSE FROM SEUNG HOON PARK FOR BUM JIN JEON’S BASIC QUESTION
The key question
  “Why there should be NO centralized coordination in which use cases?”
There are several reasons of requirement for NO centralized coordination.
  Topology aspect
    data sends through coordinator(master) node
      if there is installed infrastructure for coordinator -> cost problem
      else if user device do as coordinator -> why should I deliver another user's data?
      privacy problem at both case : it is better to send my private information directly to the target.
  Capacity aspect
    if coordinator collects data and send to recipients
      resource is wasted twice compared to direct transmission case
      single point of failure
    if coordinator just schedule resource and use direct link
      coordinator should know channel information of all managed links : scalability and scheduling delay problem
      a kind of cell boundary by coordinator : not optimized resource reuse
      single point of failure In summary, I think that only decentralized network and protocol can support Samsung use-cases involving hundreds or thousands devices.
Slide 8

## Slide 9: BUM JIN JEON’S COMMENTS FOR SEUNG HOON PARK’S RESPONSE (1)
The key question:
  “Why there should be NO centralized coordination in which use cases?”
There are several reasons of requirement for NO centralized coordination.
  Topology aspect
    data sends through coordinator(master) node
    => In 15.3, 1) There is no designated or installed coordinator. Each station may acts as coordinator.2) The coordinator does NOT serve as data bridge (transfer other’s data).3) It just manages the network resources (mainly scheduling the channel time by sending out beacons.)
      if there is installed infrastructure for coordinator -> cost problem
      => No issue. There can be NO installed infrastructure for coordinator.
      else if user device do as coordinator -> why should I deliver another user's data?
      => NO issue. The PAN coordinator does NOT deliver other’s data.
      privacy problem at both case : it is better to send my private information directly to the target.
      => NO issue. Two stations can talk to each other directly.But if we can prove that the burden of simple 15.3 coordinator is tooheavy for mobile device, then we can insist our “NO coordinator” policy.
Slide 9

## Slide 10: BUM JIN JEON’S COMMENTS FOR SEUNG HOON PARK’S RESPONSE (2)
The key question is “Why there should be NO centralized coordination in which use cases?”
There are several reasons of requirement for NO centralized coordination.
  2. Capacity aspect
    if coordinator collects data and send to recipients
      resource is wasted twice compared to direct transmission case
      single point of failure
      => The coordinator does NOT collects data and send to others. No issue. But there are always possibility of missing beacons or coordinators.
    if coordinator just schedule resource and use direct link
      coordinator should know channel information of all managed links : scalability and scheduling delay problem
      Well, I am NOT sure the coordinator should know the channel information. It just receives association message and channel time requests for reserved channel time blocks for quality services and sends out beacons. But if two stations want to use unreserved time blocks (CSMA/CA mode),it can find such time blocks also. (In a super frame, there are both reserved time blocks and unreserved time blocks.)
      a kind of cell boundary by coordinator : not optimized resource reuse
      single point of failure
      => Yes. There are always such issues and there are some solutions also(NOT perfect though).Like multi hopping, neighboring piconets, secondary coordinator, ….So, I am afraid that if we bring these issues up, they might ask us to enhance existing MAC & PHY to solve these issues. What will be our logic to answer such comments?
Slide 10

## Slide 11: SUNGGEUN JIN’S COMMENTS FOR SEUNG HOON PARK’S RESPONSE
The key question is “Why there should be NO centralized coordination in which use cases?”
There are several reasons of requirement for NO centralized coordination.
  2. Capacity aspect
    if coordinator just schedule resource and use direct link
      coordinator should know channel information of all managed links : scalability and scheduling delay problem
      Well, I am NOT sure the coordinator should know the channel information. It just receives association message and channel time requests for reserved channel time blocks for quality services and sends out beacons. But if two stations want to use unreserved time blocks (CSMA/CA mode),it can find such time blocks also. (In a super frame, there are both reserved time blocks and unreserved time blocks.)
      Sunggeun: I don’t think coordinator should know channel information of all managed links for proper scheduling. A device can determine its transmission rates by itself.
      a kind of cell boundary by coordinator : not optimized resource reuse
      Sunggeun: standard does not deal with optimization issue. It’s up to individual research.
Slide 11

## Slide 12: SOME OBSERVATIONS
Samsung came to a conclusion that a new standard is inevitable for their use cases after careful deliberation.
  Samsung’s reasons are not reasonable?
  If these reasons are reasonable, we have to pursue a new standard.
Bum Jin’s recommendation is ...
  Once Seung Hoon send those reasons in firm text, we immediately forward them to Bob Heile and ask his advice as early as possible. If he says "Yes", then we go in 15.8 approach. If he says "No", then we go in 15.3d approach.
  Seung Hoon’s response to this recommendation
    our confidence is more important than outside's agreement.
    we need deep discussion on this issue, before deciding the group's way officially.
Slide 12

## Slide 13: SOME ISSUES RAISED
How to integrate different types of technology bases in one standard (e.g. omni and mmWave)? – Seung Hoon Park
Slide 13