## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [LECIM Positive Train Control preliminary proposal]
Date Submitted: [20 September 2011]
Source: [Jon Adams, Shuzo Kato, JiaRu Li] Company [Independent, REIC/Tohuku University, Lilee Systems]
Address [12023 N 62nd St, Scottsdale AZ 85254; REIC Tohuku University; 2905 Stender Way Suite 78, Santa Clara, CA 95054]
Voice:[+1(415) 683-0213], FAX: [+1 FAX], E-Mail:[jonadams@ieee.org, shukato@reic.tohuku.ac.jp, jiaruli@lileesystems.com]
Re: [LECIM Call For Proposals, DCN: 0147-02]
Abstract: [Response to LECIM Call For Proposals, DCN: 0147-02]
Purpose: [Positive Train Control Considerations for LECIM]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 802.15.4k PHY Proposal
September 2011

## Slide 3: Summary
Review of Positive Train Control requirements
PHY Considerations
  Frequency band
  Channelization
  Data rates
  Transmitter and Receiver Characteristics
MAC Considerations
  Time Slotting
Path Loss and Propagation Considerations

## Slide 4: What is Positive Train Control?
PTC
  Keeps trains from hitting trains
  Keeps trains from hitting other on-rail equipment
  Keeps trains operating within their authority
  Provides protection for workers on or around the track within their work zones
  Keeps trains from traveling thru misaligned switches or other track elements
Jon Adams, Shuzo Kato, Jia-Ru Li

## Slide 5: Why IEEE 802.15?
PTC overview at July 2011 IEEE 802.11 WNG and 802.15 WNG sessions
  Entitled: PTC Radio and System Architecture (11-11-1032-00-0wng-positive-train-control-radio-and-system-architecture.ppt), Jia-Ru Li, Lilee Systems
802.15 voted to approve formation of an interest group to explore further
First step to explore alignment with 15.4k LECIM

## Slide 6: Challenging Propagation Environment
In the US, PTC allocated 220 – 222 MHz band (λ = 1.36 m)
High speed mobility environment
  500 km/h locomotive to trackside (1000 km/h closing speed)
“Collector” atop locomotive
  Antenna on locomotive “roof”, 5m height above railtop
  Roof 15 – 25 m long, 2.5 m wide, potentially 2km of metal-roofed cars ahead or behind
Endpoints (Wayside Equipment)
  Fixed equipment along the track, antennas may only a few meters high or pole-mounted up to 8-10 m
Base Station
  Network-connected base stations
  Antennas may be on towers, buildings or other structures
Track environment – extreme in every direction
  Mountainous terrain, tunnels, open cuts, viaduct with sound walls
  All of above but with horizontal curvature and rain sheeting down walls
  Dead flat straight track, technically line-of-sight between collector/endpoint but very strong Rayleigh fading due to strong reflection from rail/ground surface
  Dense urban, non-line of sight, extreme multipath
Distributed Power Unit (DPU)
  Remote controlled locomotive(s) separated from the crewed lead locomotive, separation up to 3 km

## Slide 7: PTC Aspects Relevant to LECIM 1
Train-centric communications (locomotive/train is “center of universe”)
High reliability PHY link, fault-tolerant, error-correcting or at least error-detecting
Intention that data carried may be “vital” (life/safety critical)
Strong link layer security features (flexible encryption, unique identity)
Data rates relatively low, depending on function (9.6k to 100’s of kbps)
Data communication speeds may be asymmetric
Propagation generally non-line of sight or close to ground, fade environment often Rayleigh, exponents 2.6 (fixed to fixed) to 3.2 (fixed to mobile)
Range to 2x braking distance (3 - 15 km) in typical urban/suburban/rural environments
Equivalent Radiated Power (ERP) (depending on antenna height, channel #, region)
Operation in licensed US 220 – 222 MHz band (but not excluding others)
  Channel spacing 5 kHz, may be aggregated (by license)
  Can support separate uplink and downlink bands (base and mobile)
  Potential for adjacent/alternate channel interferers
  Frequency agility may be useful

## Slide 8: PTC Aspects Relevant to LECIM 2
Absolute need for high-speed node mobility
  Speeds up to 500km/h, closing speeds to 1000 km/h
Latencies determined by stopping distance, order of 1 second sufficient
Payloads from a few bytes for control/command to ability to transfer larger files with fragmentation for remote upgrade/maintenance
Selectable QoS or communications priority may be useful
Wayside devices likely extremely power constrained (battery, vibration, pressure, solar, other scavenging)
Current requirements up to 24 locomotives and 30 waysides on one base station, but concept scales to dozens of devices per km of track
Flexible enough to handle very rapidly changing network membership
Time slotted and contention access periods necessary
Slide 8
Notes: doc.: IEEE 802.15-<doc#>
<month year>
        <author>, <company>
Page 8

## Slide 9: Other Potential Future Rail Environment Applications of LECIM
Track and track infrastructure
  Switch/turnout operation and position
  Block occupancy
  Damage to rails
  Right of Way fouling
  Perimeter monitoring
  Bridge, viaduct, tunnel, culvert, etc.
  Highway / Rail grade crossing
Rolling Stock Defects
  Defect detection (hot box, dragging equipment, high/wide, etc.)
Signals
  Signal indication
  Signal function
  Grade crossing signaling and warning equipment
Maintenance of Way Vehicle
  On/off rail status
  Position, direction, speed
  Positive control?
Maintenance workers
Rest-of-train car-to-car communication networks
  Hot box, brake line pressure, end of train marker, etc.

## Slide 10: FCC Allocation – Adjacent TV station

## Slide 11: FCC: 220-222 MHz Channel Summary
Summary : 200 kHz (TX ) + 200 kHz (RX)
Total Spectrum nationwide (= 25+25+25+50+75)
Two Nationwide Commercial 5 Channel blocks, (five 5kHz channels)
  Block 1 = 25 kHz + 25 kHz Block 2 = 25 kHz + 25 kHz
AAR (American Association of Railroads) = 25khz + 25khz
NWA255 (US FCC NationWide Area) - U.S. and Possessions = 50 kHz + 50 kHz
ALL EAGs (US FCC Economic Area Grouping) in Channel BLOCK J = 75 kHz + 75 kHz

## Slide 12: 220 MHz Channelization Proposal 1
Band governed under US CFR 47 Part 90 (T), sections 90.715 – 90.717
Channels on 5 kHz centers, but contiguous channels may be aggregated (FCC part 90.733(d))
Frequencies assigned in pairs
  Base channels: 220.0025 – 220.9975 MHz
  Mobile and control channels: 221.0025 – 221.9975 MHz

## Slide 13: Channelization Proposal 2
Channel designations set by rule
  E.g., channel 1 = 220.0025 MHz
  Fc (MHz) = 220.0025 + 0.005 * (Channel# - 1)
    Channel 1 = 220.0025 MHz
    Channel 201 = 221.0025 MHz
Assumption is that sufficient 5kHz channels may be aggregated to allow 12.5kHz channel separation

## Slide 14: Useful Guidance: American Association of Railways S-5904
Specs for “Remote Control Locomotive” Systems operating at 220MHz
May be a useful guideline for general requirements for a PTC communications radio in same band
  Modulation types GMSK, QPSK
  Forward Error Correction (FEC)
  Different channel spacings, different carrier frequencies
  64 time slot/sec (optional to support 128 slots/sec)
  Supports priority-based association (high priority/low priority contention slots)

## Slide 15: S-5904 Transceiver General Specifications and Traceability to ETSI Regs
Receiver Attribute | Spec | ETS-300-113 v1 Reference
Maximum useable sensitivity (normal) at BER <= 10-4 | -104dBm | 5.2.1
Co-Channel Rejection | -12dB to 0dB | 5.2.4
Adjacent Channel Selectivity (depends on channel spacing) | 60 dBc | 5.2.5
Blocking Desensitization Channel 13 (@ 211 MHz) | 95 dBc | 5.2.8
Spurious Radiation | -57dBm | 5.2.9
Transmitter Attribute |  | 
Max Carrier Power vs. Rated (normal conditions) | +/- 1.5dB | 5.1.2
Adjacent Channel Power (vs. Rated) (Note: ETSI standard is more restrictive than FCC by about 5 dB) | -60 dBc | 5.1.4
Spurious Emissions (Transmitting) | -36 dBm | 5.1.5
Intermodulation Attenuation | -40 dBc | 5.1.6
Intermodulation Attenuation at Locations Where Multiple Transmitters are in Service | -70 dBc | 5.1.6

## Slide 16: Extended Superframe Proposal
Frame beacon
  64 equal slot times
  62 full communication slots including 4 CAP (slots 60, 61, 62, 63)
  CAP slots 60, 61 are high priority access, may only be used on a pre-approved basis
  Option to support 128 CFP slots per frame (depends on licensed channel bandwidth and over the air data rate
  Slots may be concatenated for longer messages or slower channel rates
  Slot 32 optional extended beacon may be used for improved time synchronization or provide additional network information
Frame Beacon
Frame Beacon
t
Optional Extended Beacon
September 2011
Contention Access Period
(CAP)
Contention Free Period (CFP)

## Slide 17: Propagation Considerations
20dB fade margin
Propagation exponents vary with environment
  2.6 for fixed-to-fixed (base station to wayside)
  3.2 for fixed-to-mobile (locomotive to wayside, locomotive to base station)
Typical antenna heights and TX power levels
  Locomotive: 5 m / 44 dBm
  Wayside: 3-18 m (assume average 6 m) / 44 dBm
  Base station: 18 m / 44 – 48 dBm
Ranges
  Locomotive to wayside: 7 – 20 km
      Note that stopping distance for a HSR passenger train at 300 km/h can be 7200 m (http://www.railway-technical.com/Infopaper%203%20High%20Speed%20Line%20Capacity%20v3.pdf)
      Stopping distance for a 10000 ton freight train may be 10-12 km
  Locomotive to base station: 10 – 50 km
  Wayside to base station: 10 – 50 km
Future work
The channel modeling for high speed trains and longer transmission range peculiar to PTC is further work to be done

## Slide 18: Scenario 1: Locomotive to Wayside (using 15-11-0464-01)
Channel Model Parameters |  | Notes
Frequency (MHz) | 220 | Valid Range 150-2400 MHz
Locomotive Antenna Height (m) | 5 | Hata Valid Range 30-200 m, including terrain. Erceg Valid Range 10-80m, including terrain
Wayside Antenna Height (m) | 6 | Hata Valid Range 1-10 m, Erceg Fixed to 2m.
Distance (km) | 20 | Valid Range 1-20 km
Downlink Path Loss Calculation |  | Notes
Locomotive Tx Power (dBm) | 44 | Subject to Tx Power Regulations
Locomotive Tx Antenna Gain (dBi) | 3 | Subject to Tx Power Regulations
Path Loss (dB) | -159.99 | Must reference the right path loss from the Hata or Erceg worksheet
Shadowing Margin (dB) | -12 | To buffer against variable shadowing loss
Penetration Loss (dB) | 0 | For underground vaults, etc.
Wayside Rx Antenna Gain (dBi) | 6 | If using same antenna for Tx, must be same as in Uplink Table
Wayside Interference (dB) | 1 | Rise over Thermal Interference
Rx Power at Wayside (dBm) | -117.99 | Compare against Rx sensitivity
Uplink Path Loss Calculation |  | Notes
Wayside Tx Power (dBm) | 44 | Subject to Tx Power Regulations. Can be different from Collector
Wayside Tx Antenna Gain (dBi) | 6 | Subject to Tx Power Regulations
Penetration Loss (dB) | 0 | For underground vaults, etc.
Path Loss (dB) | -159.99 | Same as Downlink
Shadowing Margin (dB) | -12 | Same as Downlink
Locomotive Rx Antenna Gain (dBi) | 3 | If using same antenna for Tx, must be same as in Downlink Table
Locomotive Interference (dB) | 2 | Rise over Thermal Interference
Rx Power at Locomotive (dBm) | -116.99 | Compare against Rx sensitivity
Note that locomotive antenna height is not valid for Hata model, need further investigation

## Slide 19: Scenario 2: Base Station to Wayside, 20 km range
Channel Model Parameters |  | Notes
Frequency (MHz) | 220 | Valid Range 150-2400 MHz
Base Station Antenna Height (m) | 18 | Hata Valid Range 30-200 m, including terrain. Erceg Valid Range 10-80m, including terrain
Wayside Antenna Height (m) | 6 | Hata Valid Range 1-10 m, Erceg Fixed to 2m.
Distance (km) | 20 | Valid Range 1-20 km
Downlink Path Loss Calculation |  | Notes
Base Station Tx Power (dBm) | 44 | Subject to Tx Power Regulations
Base Station Tx Antenna Gain (dBi) | 3 | Subject to Tx Power Regulations
Path Loss (dB) | -147.57 | Must reference the right path loss from the Hata or Erceg worksheet
Shadowing Margin (dB) | -12 | To buffer against variable shadowing loss
Penetration Loss (dB) | 0 | For underground vaults, etc.
Wayside Rx Antenna Gain (dBi) | 6 | If using same antenna for Tx, must be same as in Uplink Table
Wayside Interference (dB) | 1 | Rise over Thermal Interference
Rx Power at Wayside (dBm) | -105.57 | Compare against Rx sensitivity
Uplink Path Loss Calculation |  | Notes
Wayside Tx Power (dBm) | 44 | Subject to Tx Power Regulations. Can be different from Collector
Wayside Tx Antenna Gain (dBi) | 6 | Subject to Tx Power Regulations
Penetration Loss (dB) | 0 | For underground vaults, etc.
Path Loss (dB) | -147.57 | Same as Downlink
Shadowing Margin (dB) | -12 | Same as Downlink
Base Station Rx Antenna Gain (dBi) | 3 | If using same antenna for Tx, must be same as in Downlink Table
Base Station Interference (dB) | 2 | Rise over Thermal Interference
Rx Power at Base Station (dBm) | -104.57 | Compare against Rx sensitivity

## Slide 20: Scenario 3: Locomotive to Base Station, 20 km range
Channel Model Parameters |  | Notes
Frequency (MHz) | 220 | Valid Range 150-2400 MHz
Base Station Antenna Height (m) | 18 | Hata Valid Range 30-200 m, including terrain. Erceg Valid Range 10-80m, including terrain
Locomotive Antenna Height (m) | 6 | Hata Valid Range 1-10 m, Erceg Fixed to 2m.
Distance (km) | 20 | Valid Range 1-20 km
Downlink Path Loss Calculation |  | Notes
Base Station Tx Power (dBm) | 44 | Subject to Tx Power Regulations
Base Station Tx Antenna Gain (dBi) | 3 | Subject to Tx Power Regulations
Path Loss (dB) | -147.57 | Must reference the right path loss from the Hata or Erceg worksheet
Shadowing Margin (dB) | -12 | To buffer against variable shadowing loss
Penetration Loss (dB) | 0 | For underground vaults, etc.
Locomotive Rx Antenna Gain (dBi) | 6 | If using same antenna for Tx, must be same as in Uplink Table
Locomotive Interference (dB) | 1 | Rise over Thermal Interference
Rx Power at Locomotive (dBm) | -105.57 | Compare against Rx sensitivity
Uplink Path Loss Calculation |  | Notes
Locomotive Tx Power (dBm) | 44 | Subject to Tx Power Regulations. Can be different from Collector
Locomotive Tx Antenna Gain (dBi) | 6 | Subject to Tx Power Regulations
Penetration Loss (dB) | 0 | For underground vaults, etc.
Path Loss (dB) | -147.57 | Same as Downlink
Shadowing Margin (dB) | -12 | Same as Downlink
Base Station Rx Antenna Gain (dBi) | 3 | If using same antenna for Tx, must be same as in Downlink Table
Base Station Interference (dB) | 2 | Rise over Thermal Interference
Rx Power at Base Station (dBm) | -104.57 | Compare against Rx sensitivity

## Slide 21: Questions?