## Slide 1
Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: WNG Closing Report for Atlanta November 2011
Date Submitted: 9 Nov 2011
Source: Pat Kinney, Kinney Consulting LLC
Contact: Pat Kinney, Kinney Consulting LLC
Voice: +1 847 960-3715, E-Mail: pat.kinney@ieee.org
Re: WNG Closing Report for Nov 2011 Session
Abstract: WNG Closing Report for Atlanta
Purpose: Information to 802.15 WG
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Interpretation Request
The following interpretation request concerns IEEE 802.15.4-2006, subclauses 6.8.2.5 and 6.8.3.2:
While the BPSK PHY and the ASK PHY of the 868 MHz specifications use raised-cosine and root-raised-cosine pulse shape filtering to represent the baseband chips, the O-QPSK PHY uses half-sine pulse shaping for baseband-chip representation (see 6.8.2.5). Furthermore, subclause 6.8.3.2 specifies that, using the 868 MHz band, "the signal shall be filtered" with a raised-cosine filter. Does this mean that the baseband chips are first half-sine filtered and then additionally raised-cosine filtered? Or is the raised-cosine filtering optional?

## Slide 3: Interpretation Request Resolution
Does this mean that the baseband chips are first half-sine filtered and then additionally raised-cosine filtered?
  “Yes”. This filtering is for pulse shaping purposes.
Or is the raised-cosine filtering optional?
  “No, this is mandatory”. This filtering is for spectral emissions purposes.

## Slide 4: Interpretation Request Resolution
SCWNG Motion: move to approve slide 3 of 15-11-0773-01 as resolution to the request for interpretation as stated on slide 2.
Moved by James Gilb , seconded by Phil Beecher
Following neither discussion nor opposition, the motion carries

## Slide 5: Interpretation Request Resolution
Motion: move to approve 15-11-0837-00 as the IEEE 802.15 WG resolution to the request for interpretation.
Moved by Pat Kinney, seconded by Phil Beecher
Following discussion, the vote was taken with the results of / / .

## Slide 6: Challenges on Chinese Wireless Medical Monitoring networking Applications by Liang Li (15-11-766-01)
Question: does the 402-425 MHz band have other uses that could conflict with this application?
  Reply: Yes, coexistence would need to be analyzed
Do the other bands have uses that could conflict with this application? Yes
Straw poll of attendees supporting the formation of an MBAN Chinese Study Group yielded a result of 30/0/10.

## Slide 7: Challenges on Chinese Wireless Medical Monitoring networking Applications by Liang Li
Motion: that the 802.15 Working Group seeks approval from the 802 EC to form a study group to develop the PAR and 5c documents for a PHY amendment to 802.15.4 to take advantage of newly available unlicensed spectrum for medical applications in China.
Moved by
Seconded by
Vote was taken with the result of / /