## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Positive Train Control Mandate and Technology]
Date Submitted: [08 Nov 2011]
Source: [Kevin Nichter] Company [Lilee Systems]
Address [2905 Stender Way, Suite 78, Santa Clara, CA, 95054 USA]
Voice:[+1 502-438-6950], E-Mail:[kevin.nichter@lileesystems.com]
Re: [PTC-IG November 2011 Session]
Abstract: [Overview of PTC technology and US mandate]
Purpose: [Informative presentation for the Positive Train Control Interest Group]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Positive Train Control Mandate and Technology
Kevin Nichter
Lilee Systems

## Slide 3
Background on the emergence of PTC
PTC technology
Interoperability
PTC systems in use today
A standards-based approach using the ERTMS example
Emerging issues
Agenda

## Slide 4
On September 12, 2008, a Metrolink passenger train collided with a Union Pacific freight train in Chatsworth, Los Angeles
Texting by Metrolink engineer
25 killed, 135 injured
September 12, 2008

## Slide 5
Rail Safety Improvement Act signed by President Bush on October 16, 2008 (“RSIA08”)
The bill mandates the implementation of Positive Train Control systems by December 31, 2015, on all
  Tracks with passenger service
  Tracks carrying hazardous materials which are poison or toxic by inhalation (PIH or TIH)
  Tracks carrying 5 million gross tons of freight or more per year
Requires submission of plans to FRA
  PTC Implementation Plan (PTCIP)
  PTC Safety Plan (PTCSP)
  PTC Development Plan (PTCDP)
Government Action

## Slide 6
Planning to Adopt Positive Train Control
PTC Implementation Plan (PTCIP) is the written plan that defines the specific details of how and when the railroad will implement the PTC system.
PTC Development Plan (PTCDP) provides a detailed discussion of specific elements of the proposed technology and product that will be used to implement PTC as required by RSIA08.
PTC Safety Plan (PTCSP) provides the railroad specific elements demonstrating that the system, as installed, meets the required safety performance objectives. Approval of the PTCSP comes in the form of a PTC System Certification.

## Slide 7
About Positive Train Control
Positive Train Control systems designed to prevent:
  Train-to-train collisions
  Overspeed derailments
  Incursions into work zones
  Movement through improperly configured switch
PTC systems are designed to override mistakes by human operators
Comprised of four subsystems
  Locomotive segment
  Wayside segment
  Communications segment
  Back office segment
Communications Segment
Locomotive
Wayside
Office

## Slide 8
PTC Communications Segments
Network Control Center
Network control centers communicate track warrants, database downloads, and other information to the locomotive
Can be performed through the interoperable 220 MHz network, or through other mediums as available

## Slide 9
PTC Segments
Network Control Center
Work orders, track
authorities, and databases
Wayside locations communicate signal status and switch point indications to train in signaled territory
Communicates switch position in dark territory
Communications links between wayside and office via base stations.

## Slide 10
BNSF, CSX, NS, and UP form ITC (Interoperable Train Control) to support PTC
  Working, steering, and executive committees
  Radio system using 220 MHZ frequency with TDMA
  Railroads are actively acquiring spectrum
Communications protocols and messaging formats
  AMQP, EMP, ITCM, Class C & D,
Interoperability Requirements
Radio type usage
  220 MHZ required for interoperability (across boundaries)
  802.11 WiFi for use in yards
  Satellite and cellular may be used where interoperability is not an issue (where it exists or is available today)

## Slide 11
Interoperable and Confined Systems
Interoperability between Class Is
  Locomotives must receive wayside status on home or foreign road
  Back offices configured to communicate between roads
Interoperability between Class I s and transit systems
Railroad A
Back Office
Railroad A
Wayside
Railroad A Locomotive
Railroad B
Back Office
Railroad B
Wayside
Geographical boundaries
  ITC (GPS-based) and ACSES (transponder-based)
  Collaborative effort between Class I and Northeast Corridor stakeholders
Standalone, confined systems
  Railroads without overlap with other systems
  Interoperable 220 MHZ is therefore not a requirement

## Slide 12
PTC in the United States
Project | Customer
ACSES (Advanced Civil Speed Enforcement System) | Amtrak (Northeast Corridor)
ASES (Advanced Speed Enforcement System) | New Jersey Transit
CAS (Collision Avoidance System) | Alaska Railroad
NAJPTC (North American Joint Positive Train Control) | IDOT (now TTCI)
ITCS (Incremental Train Control System( | Amtrak (Michigan)
ETMS (Electronic Train Management System) | BNSF
CBTM (Communications Based Train Management) | CSX
OTC (Optimized Train Control) | OTC
VTMS (Vital Train Management System) | UP
Train Sentinel | Ohio Central
Interoperable
Positive Train Control

## Slide 13
PTC (Positive Train Control)
  Primarily focused on United States freight and transit systems
  Affects Canadian railroads with tracks in U.S. (by mandate)
  Useful as a “lower cost” option to traditional ERTMS applications
CBTC (Communications-Based Train Control)
  Performance and functional specifications defined in IEEE 1474
  Worldwide applications in transit markets
  Frequency-agnostic (typically ISM band)
ATCS (Advanced Train Control System)
  Not fully implemented
  Successfully deployed as radio codeline standard in North America
ERTMS (European Rail Traffic Management System)
  Comprised of ETCS and GSM-R
Some “Train Control” Systems of Note

## Slide 14
Not all “PTC” systems can meet all four requirements
  For example, incursions into work zones
Systems vary in complexity and level of proprietary communications technology
PTC Technology
PTC System Requirements
Train-to-train collisions
Overspeed derailments
Incursions into work zones
Movement through improperly configured switch
  GSM-R interoperability standard (Europe)
  900 MHZ ATCS data radios, FEPs, and protocols for ACSES II
  Proprietary, but transparent, data radio
PTC as designed can be used in an overlay environment (i.e. dark territory, non-signaled applications)
PTC as vital (i.e. ACSES) or non-vital (i.e. Train Sentinel)

## Slide 15
Looking at ERTMS for a Moment…
ERTMS European Rail Traffic Management System | 
ETCS European Train Control System | GSM-R Global System for Mobile (Communications) - Railway
Can be a useful guide as to how a standards-based approach could work
Government and supplier support
  European Union
  UNIFE / UNISIG support ensures interoperability across vendors
Interoperable across geographical borders
Voice & data

## Slide 16
Looking at ERTMS for a Moment…
ERTMS European Rail Traffic Management System | 
Level | Characteristics
1 | Wayside signals; overlay; central office issues movement authorities
2 | Wayside signals optional; track characteristics are pre-loaded; radio-based communications
3 | Moving block; train detection equipment at wayside unnecessary; vital train integrity capability
Positive Train Control elements exist here

## Slide 17
The Emergence of the GSM-R Standard
UIC
Industry body
48 country representation
Negotiations
4 MHz
GSM
Proven track record
Recommendation
CEPT
Decision
Frequency
allocation
EIRENE
European Integrated Radio Enhanced Network
Railways
UIC
EC
Functional requirements
Technical requirements
MORANE
Mobile Oriented Radio Network
Vendors
GSM-R bearer

## Slide 18
Other Systems in Use…
AEI (Automatic Equipment Identification)
HBD (Hot Box Detector)
Crossing alarm and asset management
DTMF-Based Crossing Activation

## Slide 19
Immediate and Emerging Issues
Interoperability between ACSES and ITC
Are there other IEEE efforts that can address centralized management or other facets of PTC systems?
How will evolving needs and requirements be captured and implemented?
What else can be “absorbed” into the PTC communications system?
  Advanced crossing starts
  Codeline (controls / indications)
  EOT / HOT, AEI, HBDs, and more
  Motes?