## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Scanning issue for TG4m
Date Submitted: November 2011
Source: Suhwook Kim (LG Electronics)
Address: LG R&D Complex 533, Hogye-1dong, Dongan-gu, Anyang-shi, Kyungki-do, Korea
Voice: +82-31-450-1936, FAX: +82-31-450-4049, E-Mail: suhwook.kim@lge.com
Re: Call for Contributions(TG4m)
Abstract:
Purpose:
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1

## Slide 2: WPAN in TVWS
Slide 2
In this submission, we point out the scanning issue for WPAN operation in TWVS

## Slide 3: WPAN in TVWS
FCC regulation
  “In U.S. personal/portable devices may only transmit on available channels in the frequency bands 512-608 MHz (TV channels 21-36) and 614-698 MHz (TV channels 38-51)“
Scanning in 802.15.4-2011
  ED scanning
  Active scanning
  Passive scanning: suitable for TVBD
  Orphan scanning
Slide 3

## Slide 4: WPAN in TVWS
Channelization assumption
  180 MHz (30 TV channels)
  802.15.4g channel BW (0.2 MHz, 0.4 MHz, 0.8 MHz, 1.2 MHz, 2 MHz)
Number of TG4m channels in TVWS
  900 (0.2 MHz BW)
  450 (0.4 MHz BW)
  225 (0.8 MHz BW)
  150 (1.2 MHz BW)
  90 (2 MHz BW)
Slide 3

## Slide 5: WPAN in TVWS
Large initial access delay of passive scanning
  Number of candidate channels x Beacon Interval
  Scanning time might be around several minutes
  Power consumption depends on the number of scanning channels
Slide 3

## Slide 6: WPAN in TVWS
General solution to reduce initial scanning time
  Active scanning (802.15.4)
  Common pilot channel (802.15.4g-Enhanced Beacon)
  Set primary channel (802.11ac)
Slide 3

## Slide 7: WPAN in TVWS
Conclusion
  Scanning issue should be considered when we design the channel plan in TVWS band and develop MAC feature
  Some general solutions can be starting point for resolving scanning issue
Slide 3