## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [802.15 PTCsg Presentation]
Date Submitted: [16 Nov 2011]
Source: [Jon Adams] Company [Lilee Systems, Ltd]
Address [2905 Stender Way, Suite 78, Santa Clara, CA, 95054 USA]
Voice:[+1.480-628-6686], E-Mail:[jonadams@ieee.org]
Re: []
Abstract: [We’re a Study Group, so now what?]
Purpose: [Potential PHY Amendment to IEEE 802.15.4 or new standard under IEEE 802.15]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Motion at 802.15 Closing Plenary
Motion: The 802.15 Working Group seeks approval from the 802 EC to form a Study Group to develop the PAR and 5C documents for a wireless communications standard supporting US-mandated Positive Train Control systems.
Moved by Clint Chaplin
Seconded by Clint Powell
Approved 49Y/0N/0A

## Slide 3: Motion at Friday’s 802 EC Meeting
To approve the recommendation of the 802.15 Working Group for the formation of the IEEE 802.15 Positive Train Control Study Group
Vote was unanimous (numbers to follow later)

## Slide 4: PTC-SG Officers (Interim)
Chair: Jon Adams (Lilee Systems)
Vice Chair: Dr Mark Hartong (Federal Railroad Administration)
Secretary: TBD
Technical Editor TBD (Not needed until in editing phase)
Slide 4

## Slide 5: PTC-SG Schedule
Interest Group
  Establish group, discuss process Aug 2011
  Establish regular meeting schedule Oct 2011
  Request promotion to Study Group Nov 2011
Study Group
  Call for Applications/Contributions Nov 2011
  Draft Project Authorization Request and 5C Nov 2011
  Request PAR/5C approval Jan 2012
  Request promotion to Task Group Mar 2012
Task Group
  Proposal Effort
    Technical Guidance Document May 2012
    Call for Proposals May 2012
    Preliminary Proposals July 2012
    Final Proposals Sep 2012
    Adopt Baseline Nov 2012
  Drafting
    Preliminary draft May 2013
    Final draft (ready for WG Letter Ballot) July 2013
  Balloting
    Letter ballot Sep 2013
    Recirculation I Jan 2014
    Recirculation II Mar 2014
    Recirculation III May 2014
    Sponsor Ballot July 2014

## Slide 6: PTC-SG Goals and Intentions
This standard may be a new IEEE 802.15 standard or an amendment to IEEE 802.15.4. The intention is to standardize the over-the-air radio link for the mandated US Positive Train Control law established in 2008:
Enables operation in a variety of radio frequency bands including the US-licensed 216-222MHz spectrum
Supports typical data rates from 9.6 to 200 kbits per second
Support for multiple simultaneous networks
Provides for mobility up to 500km/h (1000km/h closing speeds, train to train)
Supports radio ranges up to 70km
Shall operate in not-necessarily contiguous channel sizes as small as 5kHz but generally up to 50kHz
Requires flexible and robust QoS with attention to connection time, transfer delay, registration delay, and handover time
Allows for rapidly changing (several per second) network membership
Realizes optimal and power efficient device command and control applications for energy-scavenged end devices
Slide 6
Notes: November 11
Page 6

## Slide 7: Goals and Intentions 2
Propagation path loss of approximately 140 dB
Potential for dozens of simultaneous wayside and network connections per locomotive
Asymmetric application data flow
Extreme difference in capabilities and performance between wayside, network access points, and locomotives
  Locomotive and Network Access Points may support all standardized modulations (MCS) and data rates
  May be requirements to support antenna diversity or antenna beam steering
  Wayside equipment may be required to conserve energy
Reliable operation in dramatically changing environments (no control over environment)
This amendment also provides mechanisms that enable coexistence with other systems in the same band(s) including IEEE 802.11, 802.15, and 802.16 systems, assuming those networks exist in set of bands
Because of its nature, the standard developed here may be broadly applicable to other monitoring and control Intelligent Transportation System (ITS) functions.

## Slide 8: PAR (Project Authorization Request) 1
The important bits:
5.2 Scope: This amendment specifies a physical layer for 802.15.nn US Positive Train Control regulatory requirements and also any necessary MAC changes needed to support this physical layer. The standard: enables operation in a variety of radio frequency bands including the US-licensed 216-222MHz spectrum, supporting typical data rates from 9.6 to 200 kbits per second; provides for mobility up to 1000km/h (closing speeds, train to train); supports radio ranges up to 50km; shall operate in not-necessarily continguous channel sizes as small as 5kHz; requires flexible and robust QoS with attention to connection time, transfer delay, registration delay, and handover time; allows for rapidly changing network membership which may or may not require association; realizes optimal and power efficient device command and control applications for energy-scavenged end devices. Because of its nature, the standard developed here may be broadly applicable to other monitoring and control Intelligent Transportation System (ITS) functions.

## Slide 9: PAR (Project Authorization Request) 2
5.4 Purpose: The purpose of this amendment/standard is to enable 802.15 wireless networks to address large scale Positive Train Control device command and control applications.

## Slide 10: Five Criteria, Section 1
1. Broad Market Potential
  a) Broad sets of applicability
  b) Multiple vendors and numerous users
  c) Balanced costs (LAN versus attached stations)

## Slide 11: Five Criteria, Section 2
2. Compatibility
  IEEE 802 defines a family of standards. All standards shall be in conformance with the IEEE 802.1 Architecture, Management, and Interworking documents as follows: 802 Overview and Architecture, 802.1D, 802.1Q, and parts of 802.1f. If any variances in conformance emerge, they shall be thoroughly disclosed and reviewed with 802.1.
  Each standard in the IEEE 802 family of standards shall include a definition of managed objects which are compatible with systems management standards.
  This standard will be compatible with the IEEE 802 requirements of Architecture, Management, and Inter-networking documents as required. There is no specific technology feature anticipated in the standard that could preclude this compliance.

## Slide 12: Five Criteria, Section 3
3. Distinct Identity
  a) Substantially different from other IEEE 802 standards
  b) One unique solution per problem (not two solutions to a problem)
  c) Easy for the document reader to select the relevant specification

## Slide 13: Five Criteria, Section 4
4. Technical Feasibility
  a) Demonstrated system feasibility
  b) Proven technology, reasonable testing
  c) Confidence in reliability
  d) Coexistence of 802 wireless standards specifying devices for unlicensed operation

## Slide 14: Five Criteria, Section 5
5. Economic Feasibility
  a) Known cost factors, reliable data
  b) Reasonable cost for performance
  c) Consideration of installation costs

## Slide 15: Logistics from Atlanta to Jacksonville
Conference Calls
Near weekly calls
  Wednesday at 1600 EDT
  November 30; December 7, 14, 21; January 4, 11
Call details are: +1.530.881.1000, participant access code: 646359#
Topics
  Further work to finalize PAR and 5Cs
  Call for contributions and applications
  Continue to increase industry participation