## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title:[MPDU Fragmentation Format Refinement Ideas]
Date Submitted: [Nov 16, 2011]
Source:[Benjamin Rolfe]
Company [Blind Creek Associates]
Address []
Voice: [+1.408.395.7207], FAX: [None], E-Mail: [ben @ blindcreek.com]
Re:[MPDU Fragmentation drafting]
Abstract:[Ideas for the details of the MPDU fragment format, compiled from comments received and discussions on the presentations in Atlanta]
Purpose:[Support drafting of MPDU Fragmentation text]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Summary
Much good input was received during and after the Atlanta session (in hallways, coffee breaks, lunch time, etc). A common and obvious goal is to minimize per-fragment overhead. The following slides aggregate and summarize the discussions.

## Slide 3: Overview
Consolidate control fields:
  Some flags only make sense with some fragment types
  Trade-off individual control flags vs enumerating via sub-type each valid combination
Efficient per-fragment Ack: sliding window bit map
Roll CID and CRC together to save bits

## Slide 4: Control Flag Conditions
Now: 3 bit subtype + 4 flag bits (7 control bits)
ACK request - used to indicate when to I-ACK.
  May be used with any fragment, or not a fragment
  Not used for I-ACK
Chan open only used when
  Not last fragment in sequence
  Or “not a fragment” (single frame)
  Might be used w/I-ACK, but only when last frag?
Last fragment – only set on last fragment in sequence
CID present can be used anytime
3 Flags that aren’t always meaningful

## Slide 5: Fragment Info Enumeration
List all the possibilities subframes
  Fragment (part of fragment sequence), not last, Ack later (defer Ack)
  Fragment (part of fragment sequence), not last, Ack now
  Last fragment, defer Ack [or should last always result in I-ACK?
  Last fragment, defer Ack, chan open (more data to follow)
  Last fragment, I-ACK now
  Last fragment, I-ACK, chan open
  Not a fragment (no I-ACK needed – MPDU Ack)
  Not a fragment, chan open
  I-ACK
= 4 bits w/ spares [2 bits saved w/CID flag retained]

## Slide 6: Fragment Structure
FHR |  |  | Payload | FFR
Octets: 2 | 0/1 | 0/2 | [7-10, 15-18 or 23-26] | 4
Fragment Descriptor | Ext. Descriptor | CID | Fragment Data | Frag CRC
16, 24 or 32 octets
Bits: 4 | 3 | 1 | 1 | 2 | 5
Sub-type | LQI | CID Present | SDU # | ?? | Fragment #
Only need when subtype is fragment
Saved 2-bits need not be transmitted
Can CID flag also roll into subtype?

## Slide 7: Efficient I-ACK: Sliding bit-map window
Take advantage if “incremental” nature of I-ACK
Status is obvious for fragments not yet sent
If fragments always sent in order (or mostly in order) can request only what is needed.
Instead of always sending full bit-map for every possible fragment, send a sub-set
  Sliding window (stateless)
  Incrementally growing map (stateless)
  Combination (stateful)

## Slide 8: bit-map (simplest)
With 5-bit Fragment #, max fragments = 32
Need 4 octets of flags
If fragment # grows, I-ACK grows
Always send 4 octets no mater how many fragments received so far (or total)
Octets: 4 |  |  | 
Status 0-7 | Status 8-15 | Status 15-23 | Status 23-32

## Slide 9: Sliding bit-map
Bit-mapped ACK content: [index][8-bit flags]
Sliding window into the bit-map of all fragments status.
Octets: 1 | 1
Window Index | Status flags (8 fragments)
Bit # 0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23
+ + +
^ ^
| |
Index 0, Flags 0 to 7 Index 2, flag 16-23
Could optimize window index  window size
  3 bit index, 5 bit status flags = 1 octet

## Slide 10: Incrementally growing
When fragment sequence > 7 only 1 octet
When fragment sequence > 14, 2 octets
etc
Octets: 1 |  | 0 to 3
Bits: 2 | 6 | Flags 5 to 31
# flags | Flags 0 to 5 | 

## Slide 11: Fragment Validation
CRC-32 is over-over kill, CRC-16 not enough, CRC-24 not already in standard
If we combine CRC with CID?
  CID always present [can remove CID flag in descr.]
  CID must match to be valid
  CRC must match to be valid
  [Still half-baked, need more input]

## Slide 12: Fragment Validation
MIC as CRC (secure FCS)
  Feasible: properly implemented CMM* MIC undetected error rate ~ same as CRC-32 [J. Simon]
  MIC implementation is common (15.4 security)
  Requires a nonce (non-repeating counter synchronized between sender and receiver
    Can be assumed if reliable contet (ex: TSCH)
    In 15.4-2011, always included in secured frame (not good for fragments)
  Implementation complexity?
Need input on what could be used as nonce