## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title:[Sliding Window I-ACK]
Date Submitted: [Nov 21, 2011]
Source:[Jussi Haapola]
Company [Centre for Wireless Communications / University of Oulu]
Address [P.O. Box 4500 FI-90014 University of Oulu, Finland]
Voice: [+358-40-8363-018], FAX: [], E-Mail: [jhaapola@ee.oulu.fi]
Re:[MPDU Fragmentation drafting]
Abstract:[Ideas for using a sliding window acknowledging method for sub-MAC fragmented frames]
Purpose:[Support drafting of MPDU Fragmentation text]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Summary
Three different methods for acknowledging multiple MPDU fragments using a sliding window approach.

## Slide 3: Simple, but limited
Bit 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Fragm 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Reserve a fixed one octet for acking
Sliding by moving to next 8 fragments after current 8-fragment block finished.
Limits maximum transmitted fragments to 8 before request for I-ACK.
Cannot advance to next 8 fragments before all 8 prior have been ACKed correctly.

## Slide 4: Simple Sliding window
Len: length of sliding window (0->1 octet, 1->2 octets)
If less than 9 fragments have been transmitted before I-ACK, len = 0 and only first octet present
If more than 8 fragments have been transmitted before I-ACK, len = 1 and both octets are present.
When fragments 1 to 8 have been successfully ACKed, their ACK fields are omitted, len = 0 and bits 0-7 now ACK fragments 9 to 16. (Hence the term Sliding)
Len | … | Bit 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1 bit | … | Frag 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Bit 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Frag 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16

## Slide 5: Sliding Window Over All Fragments
Len | … | Bit 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
4 bits | … | Frag 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Bit 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Frag 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Bit 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Frag 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Bit 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Frag 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32

## Slide 6: Sliding Window Over All Fragments
Define MaxMPDUFragments (32 in this case)
4 bit Len field in header to indicate which Fragment ACK octets are present
  Len 0001: only first octet present
  Len 0011: first and second octet present
  Len 0101: first and third octet present
  0: absent, 1: present
Up to MaxMPDUFragments fragments can be transmitted before ACK request.
Only the octets having MPDU fragments to ACK are present.
Once a complete octet has been ACKed, it will be omitted by setting the appropriate Len bit to 0.
Len 0000 is effectively NACK for all incomplete 8-block fragments.
We could extend Len field for smaller ACK fragment blocks.