## Slide 1
Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: 802.15.4k Fragmentation Concept Proposal
Date Submitted: 25 Nov 2011
Source: Pat Kinney, Kinney Consulting LLC
Contact: Pat Kinney, Kinney Consulting LLC
Voice: +1 847 960-3715, E-Mail: pat.kinney@ieee.org
Re: In response to MAC subgroup call for concepts/proposals
Abstract: 802.15.4k Fragmentation Concept Proposal
Purpose: Fragmentation Concept Proposal
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Fragmentation Concept Overview
The following presentation is the overview of a concept that could be used to implement fragmentation for TG4k.
This concept leverages TSCH concepts of setting up dedicated links with predetermined originations and destinations and also the timing of these links. For beacon-enabled modes it also leverages many concepts of DSME.
This concept is based upon a “stateful” method, i.e. both devices share information necessary to properly execute fragmentation

## Slide 3: Fragmentation Overview
The coordinator sets up the fragmentation operation by sending a packet, using standard 802.15.4 formatting, to the end device containing an Information Element (IE) dedicated to fragmentation with the following configuration information:
Destination address (typically the end point)
Origination address (typically the coordinator, but not necessarily)
Fragmentation link ID (identifying this fragmentation operation, this ID will be closed when the operation is terminated)
Length of total message in octets
Number of fragments to be sent (thus defining each fragment length)
Acknowledgment protocol (e.g. individual or group, fixed or sliding window)
Slot times & Channel/channel hopping information (e.g. when the fragments will be sent-slot number and on what channel/channel sequence)
Synchronization information (to accommodate the timing element)
Fragmentation time out period (after this period the fragmentation link will be cleared and any received fragments will be purged)

## Slide 4: Fragmentation Scenario
IE Description | Value | Notes
Dest Addr | 0x1EA8 | Endpoint’s short address
Orig Addr | 0x0000 | Coordinator’s short address
Frag Link ID | 0xEA | Number is assigned by Coordinator
Msg Length | 80 | octets
# of Fragments | 5 | 16 octets + overhead (9 octets) = 25 octets per fragment
Ack protocol | I-ACK/fixed window | 1 I-ACK since it can accommodate up to 8 fragments
Slot#/Chan# | S0/C3:S8/C1:S16/C7:S24/C2:S32/C5 | Where network sets slot durations at 50 ms and channel page to 9
Synch info | TBD | 
TimeOutPeriod | 0x3C | => 60 slots or 3 seconds (0xFF = no period defined)
To illustrate this fragmentation concept let’s take the scenario of a coordinator (0x0000) wishing to send a data message to an endpoint (0x1EA8) that will be fragmented. The MPDU is 80 octets, and the data rate is 4800 b/s.

## Slide 5: Fragmentation Scenario
The coordinator sets up the fragmentation operation by sending the configuration packet containing the Fragment IE as per the previous slide
The endpoint device will respond with to the fragmentation IE with an ACK or a NACK with a reason why it cannot accept or agree with this message
Since the timing, channel, destination, and origination are defined by the fragment link ID, each fragment need only contain the PHY header, fragment link ID, a sequence value, and FCS in addition to the fragment

## Slide 6: Fragmentation Scenario
The coordinator starts sending the sequence of fragments as per the “agreed-upon” schedule
The endpoint device acknowledges receipt of these fragments as per the “agreed-upon” method
Upon successful receipt of all fragments, the endpoint MAC reconstructs the “whole” message, processes it as a “normal” 802.15.4 frame, and passes the payload to the next higher layer
The coordinator clears out all fragments and configuration settings from the fragmentation link and releases the Fragment Link ID to be used for another fragmentation link

## Slide 7: Fragmentation Concept Details
The Fragment link ID is one octet and is assigned by the coordinator
The sequence value is one octet
The FCS is two octets
For beacon-enabled modes, the fragmentation slots will be marked as “special” to disallow another device from sensing them “empty” and trying to use them to send a message to the coordinator
For nonbeacon-enabled modes, the coordinator may send out messages to all other devices that certain times have been reserved for this fragment link

## Slide 8: Fragmentation Concept Details
If an end device wishes to send a fragmented message to another device (and is able to do so), the coordinator will set up this link
The PHY will use a Start Frame Delimiter (SFD) unique to a fragmentation link allowing 15.4k devices to sense and decode the fragment, i.e. an SFD-F
The PHY will not include the frame length field since it is determined at configuration
Non 15.4k devices will not recognize these fragments due to the unique SFD, and the non-conformal MAC Header

## Slide 9: Fragmentation Concept Details
If security is desired, the current version of frame security will be placed on the original, non-fragmented message, not on each fragment
In addition to the time slots dedicated to transmission of fragments, the coordinator should also set up “management” time slots to allow both devices to communicate management information such as “terminate this fragmentation link now” or “suspend this operation for a defined time”

## Slide 10: Fragmentation Concept TBDs
Initial fragment configuration IE (see slide 3) needn’t contain all future slot times & channels, allow management time slots (see slide 8) to contain fragment configuration IEs that contain continuation slot times & channels?
The size of the initial fragment configuration frame could easily be too long; the IE size could be reduced using:
  Defaults declared within the standard
  Preconfiguration at commissioning via out-of-band mechanisms
  Extension of the 15.4 definition of an RFD, to sufficiently restrict its operation such that the number of configuration parameters is reduced
Configuration frame sent to end point, should it be Data, Beacon, or Command?

## Slide 11: Fragmentation Concept TBDs
Fragment security could be implemented if a suitable mechanism could supplant the 2-octet FCS
Limit # of fragment links to ~64 and leave 2 bits of fragment link ID as reserved?
Limit # of fragments to ~64 and leave 2 bits of sequence value as reserved?
For very low data rates (<1 kb/s) consider:
  merging Fragment Link ID and Sequence Number into one octet (reducing the number of fragment links and the number of fragments)
  Unique SFD to this low data rate fragmentation link, i.e. SFD-LDRF
  use of an 8-bit CRC (such as CRC-8-WCDMA)

## Slide 12: Fragment Packet
Total Overhead: 4+1+1+1+2= 9 octets
Link ID
PHY Preamble 4-octet
SFD -F
FCS 16-bit
PPDU
Total Overhead: 3+1+1+1= 6 octets
Link ID/Seq #
PHY Preamble 3-octet
SFD -LDRF
FCS 8-bit
PPDU
Seq #
Baseline Fragment
Low Data Rate Fragment