## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [PAC Introduction]
Date Submitted: [05 January 2012]
Source: Myung-Jong Lee7
Company [Samsung Electronics ]1, [ETRI]2, [LG]3, [Huawei]4, [NICT]5, [CSEM]6 , [CUNY]7
Address [] Voice:[], FAX: [],
E-Mail:[shannon.park@samsung.com]1, [ ]2, [ ]3, [ ]4, [ ]5, [ ]6, [mjlee999@gmail.com]7
Re: [.]
Abstract: [Introduction for Peer Aware Communication (PAC) to support local and dynamic traffic service nearby a user and expected market potential]
Purpose: [To show use cases and market potential and to clarify the scope of PAR & 5C]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Introduction to Peer Aware Communications (PAC):
A Study Group of IEEE 802.15 WG

## Slide 3: ToC
Introduction
Target Use-cases
  Social Networking
  Advertisement
  Gaming
  CE
  Emergency
  Key Requirements
Key Technical Features
  Infrastructure-less peer-aware communication
  Fully distributed coordination
Summary
  Why a new TG?

## Slide 4: Introduction
Application driven
  Primarily to support burgeoning social networking, peer-to-peer applications, and emergency communications for mobile devices
Requirements
  Peer awareness in a close proximity
  Low signaling overhead
  Scalability
  Group management
Need for a New TG

## Slide 5: Target Use-cases

## Slide 6: Location-based Service Trend
Geo-social networking
  Who’s here
Location-based Game
  ‘check-in’ game:
  over 25 various games from Wikipedia
Location-based Search
Around Me
Map Attack

## Slide 7: Target Use-cases
Urban/Crowded
  SNS, Advertisements, Gaming,
  Broadcasting/Multicasting
  Service/Contents discovery
Rural/Isolated
  SNS, Advertisements
  Broadcasting/Multicasting
Public safety
  Back-up network at emergency
Social Networking
Gaming
Public Safety
Notes:   The fully distributed network without infrastructure is not only useful for crowded places such as mall, stadium, campus, amusement park etc. but also isolated places not supported by infrastructure. It is also useful for emergency situations such as flooding, earthquake, fire, and etc.

## Slide 8: Use-case 1: Social Networking
Friends
Company
Food Truck
Geo-social networking
  Relevant to situation/context
  Local group chatting
Proximal filtering
  Avoid too many info from SNS
Proximal search
  Suitable for dynamically changing proximal info
  Proximal answering engine
  Proximal profile matching
Augmented society
  Complementing real world
Personal broadcast
  By relevant information
Neighbors

## Slide 9: Use-case 2: Advertisements
John
Broadcast Ad for McDonald’s Hamburger
1
Receive Ad from near-by shop when hitting the score
2
Retailer
Ads in Game
Advertising platform
  By user interaction/context
  Personalized promotions
  Precision marketing
Related services
  Advertisements with personalized information (coupon, brochure, mileage, etc)
  Product information broadcastings
  Experience of sample video or audio clips
  Automatic narration/guide
  Mobile group buying
  Mall navigator

## Slide 10: Use-case 3: User-centric Service Platform
Distributed SW platform
  For user-centric applications that should be scalable and efficient
  Gaming, streaming, contents distribution
Augmented Reality
  Game based on real location + virtual scene, e.g. MyTown
Personal DJ
User-centric Game Model
PAC link
PAC link

## Slide 11: Use-case 4: CE (Consumer Electronics)
Personal environment setup
  1. Notify user’s activity to each device and setup it
  2. Each device adjust automatically its status and feedback to other devices
Device can automatically establish multi-hop wireless links forwarding data frames

## Slide 12: Use-case 5: Alarm & Emergency Service
Accident alarm
  Fast notification in near-by area
  E.g. car accident alarm
Emergency platform
  Robust link to infrastructure or public officer, or among distant peoples
  Coverage enhancement
  E.g. finding a injury
Hazard sensing
  Monitoring hazard syndrome and inform to people in the area
  E.g. chemical effusion, air pollution, water contamination
Car Accident Alarm
Public Officer
Finding people
Connecting people

## Slide 14: Key Features

## Slide 15: Key Features
Optimized design of PHY and MAC to support Target use cases
    Peer awareness in a close proximity
    Low signaling overhead
    Scalability
    Low power consumption
    Group management
    Security
Infrastructure-less peer-aware communication
Peer-to-peer network with fully distributed coordination

## Slide 16: Peer Awareness
Relevant Time
Relevant People
Relevant Location
Relevant Message

## Slide 17: Location-based Service
Positioning
  attaining the current absolute geographic coordinates
  legacy: GPS, Cellular, Base-station
Matching
  geo-location matching: determine the location information from the coordinates value
    matching my location / matching the location what I want to know
    local info in server may not be updated timely
  proximity matching
    matching the location of someone/something in my proximity

## Slide 18: Positioning
Legacy (GPS/A-GPS/Base station)
  inaccurate indoor position
  need support of operator’s network
  local info in server may not be updated timely
  high power consumption
   Not good user experience
Alternative?
  relative positioning may be sufficient  especially, for proximal discovery
  independent from operator’s network  easy to implement

## Slide 19: Matching
Server-based geo-location matching is going well
Current proximity matching for mobile devices
  built on top of existing physical network infrastructures that focuses on matching among wireless devices in close proximity
different proprietary network infrastructures
Wi-Fi AP
Cellular BS
Logically same to application
server

## Slide 20: Limitation of Existing Matching
High control overhead
  due to periodic report from Apps and updates from server
    sending position value or discovery request from nodes
    retrieving matching result from server
    frequent update is inevitable due to the device mobility
  10s of protocol steps for link setup
Long latency
  the communication path between devices is long even though two devices are geographically close in the same segment
Peer-awareness
by direct communication in close proximity

## Slide 21: Comparison
 |  | GPS | A-GPS | BS | PAC
Positioning | Method | Absolute positioning |  |  | Relative positioning
 | Outdoor | High accuracy | High accuracy | Low accuracy | Moderate accuracy
 | Indoor /Urban | Low accuracy | Low accuracy | Low accuracy | Moderate accuracy
 | Latency | 10s of seconds | Several seconds | Several seconds | ?
Matching | Geo-location | Through remote server |  |  | P2P, conditionally
 | Proximity | Through remote server |  |  | P2P
Power consumption |  | High | Medium | Medium | Low

## Slide 22: Infrastructure-less Peer-aware Communication
No BS, no AP
  No cost for deployment or maintenance
  No network control overhead
No LBS server
  Low cost to implement proximal search
  Avoid tracking and storing personal geo-location
  No single point of hazard from cracking

## Slide 23: Infrastructure-less Peer-aware Communication
Peer-awareness based communication
  Discovery with service/contents information
    without association
    relative positioning
  Group management
    link management for nodes in the same group
    multicasting, routing, data dissemination
  Key challenge: How to realize/facilitate normally higher layer functions such as discovery and group communication?

## Slide 24: Fully Distributed Coordination
No coordinator node
  Direct link for user-centric operation
  Low latency / low signaling overhead
  Efficient resource usage
  Simple & Scalable
Distributed protocol
  Synchronization
    enables low duty cycling for discovery
  Resource management
    distributed multiple access
    distributed scheduling
    distributed interference management

## Slide 25: Distinctive Features
  Discovery for peer information without association
    Discovery signaling rate -typically 100 kbps
    Number of peers >100
  Efficient data transmission by distributed coordination
    Data transmission rate -typically 10 Mbps
  Group communications: n to m
  Multi-hop support -typically 2 hops
  Relative positioning -typically 10 m
  Security
  Globally available unlicensed/licensed bands

## Slide 26: Potential Spectrum Bands
Unlicensed
  No need for licensees, fast adoptions
Licensed
  Easier to find Biz model (compared to unlicensed)
Potential spectrum bands
  Unlicensed : TV White Space, WLAN(2.4GHz, 5GHz), local license-exempt band
  Licensed: under utilized existing bands
Globally available unlicensed/licensed bands

## Slide 27: Why a new TG?
Existing centralized architecture incurs substantial signaling overhead and communication latency when to support hundreds of devices in the proximity.
In view of IEEE 802 standard, current MAC and PHY are not optimized to support those applications.
Parts of the features can be supported by existing standards, but no single standard can support all features

## Slide 28: Thank You
Any Questions?