## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: PANA over 802.15.9 Proposal (DCN 15-12-0109-00-0009)
Date Submitted: March 2, 2012
Source: Yoshihiro Ohba, Toshiba
Address 1 Komukai Toshiba-cho, Saiwai-ku, Kawasaki, 212-8582, Japan
Voice:+81 (44) 549-2127, FAX: +81 (44) 520 1806, E-Mail:yoshihiro.ohba@toshiba.co.jp
Re: IEEE P802.15.9 CFP
Abstract: Proposal for PANA over 802.15.9
Purpose: To add PANA KMP support for 802.15.9
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PANA KMP Support for 802.15.9
Yoshihiro Ohba and
Yasuyuki Tanaka (Toshiba),
Stephen Chasko (Landis+Gyr),
Subir Das (ACS)
March 2, 2012

## Slide 3: PANA (RFC 5191) [Informative]
PANA carries EAP between PaC (PANA Client) and PAA (PANA Authentication Agent) over UDP
PaC
PAA
PANA message
EAP Peer
EAP Authenticator
PaC |  | PAA | Message (when a 4-message EAP authentication method is used)
 |  |  | PCI
 |  |  | PAR[PRF-Algorithm, Integrity-Algorithm, Encryption-Algorithm*, EAP(msg#1)]
 |  |  | PAN[PRF-Algorithm, Integrity-Algorithm, Encryption-Algorithm*, EAP(msg#2)]
 |  |  | PAR[Nonce, EAP(msg#3)]
 |  |  | PAN[Nonce, EAP(msg#4)]
 |  |  | PAR[Result-Code, Key-Id, Session-Lifetime, EAP(Success), Encr-Encap*, AUTH]
 |  |  | PAN[Key-Id, AUTH]
(*) Encryption feature enabled by a PANA encryption extension (draft-yegin-pana-encr-avp)
PCI: PANA-Client-Initiation
PAR: PANA-Auth-Request
PAN: PANA-Auth-Answer

## Slide 4: PANA Relay (RFC 6345) [Informative]
PANA Relay Element (PRE) is used when PaC and PAA are not able to directly communicate
PANA-Relay (PRY) message is used for forwarding a PANA message in between
PaC
PAA
EAP Peer
EAP Authenticator
PRE
PANA message
PANA message
PRY message
PaC |  | PRE |  | PAA | Message
 |  |  |  |  | PCI
 |  |  |  |  | PRY[PaC-Info., Relayed-Message{PCI}]
 |  |  |  |  | PRY[PaC-Info., Relayed-Message{PAR}]
 |  |  |  |  | PAR
 |  |  |  |  | PAN
 |  |  |  |  | PRY[Pac-Info., Relayed-Message{PAN}]
 | … |  | … |  | …
PCI: PANA-Client-Initiation
PAR: PANA-Auth-Request
PAN: PANA-Auth-Answer
PRY: PANA-Relay

## Slide 5: PANA over 802.15.9 Overview
PANA PDU (w/o IP and UDP headers) is carried in KMP Payload between PaC and its parent node
  Parent node is PAA (for single hop case) or PRE (for multi-hop case)
  PANA PDU is carried over UDP/IP between PRE and PAA (out of the scope of 802.15.9)
    This guideline uses IPv6 due to straightforward mapping between EUI-64 address and IP address
PAA performs network access authentication and authorization for PaC
  PANA serves as a bootstrapping KMP
  PAA may communicate with AAA server located outside the mesh network using AAA protocol (out of the scope of 802.15.9)
Upon successful network access auth/authz, Link-Layer Credentials (LLCs) are securely distributed from PAA to PaC
  Using PANA payload encryption mech. (draft-yegin-pana-encr-avp)
Example of LLCs:
  Group PSK credentials
  Short-term public key credentials
LLCs are used for establishing link-layer transient session keys (TSKs) between neighboring nodes to protect link-layer frames using a link establishment KMP
  TSKs: Unicast TSKs and Multicast TSKs

## Slide 6: Call Flow (w/o Relay)
PaC
PAA
Joining Node
Parent Node
PANA over 802.15.9
(bootstrapping KMP)
(2) Link Establishment KMP
over 802.15.9
LLCs
LLCs (encrypted in PANA payload)
PaC : PANA Client
PAA: PANA Authentication Agent

## Slide 7: Call Flow (w/ Relay)
PaC
PRE
PAA
Joining Node
Parent Node
(1’) PANA Relay over UDP
PANA over 802.15.9
(bootstrapping KMP)
LLCs
Out of scope of 802.15.9
(2)Link Establishment KMP
over 802.15.9
LLCs encrypted in PANA payload)
PaC : PANA Client
PAA: PANA Authentication Agent
PRE: PANA Relay

## Slide 8: Message Format for 802.15.4e
802.15.4e MAC Frame
Frame Control (1 octet) +
PANA PDU fragment (variable)
‘device control’ IE
PANA PDU

## Slide 9: Message Mapping for PANA-Relay
802.15.4e MAC Frame
PANA-Relay (PRY) Message
16-bit Port Number
PaC-Information AVP
Frame Control (1 octet) +
PANA PDU fragment (variable)
IPv6 Address
64-bit Prefix
64-bit Interface
Identifier
Relayed-Message AVP
Downlink
messaging
Uplink
messaging
‘device control’ IE

## Slide 10: PANA Session Management for 802.15.9
Single-hop case
  In both PaC and PAA, PANA session is associated with MAC addresses of PaC and PAA
Multi-hop case
  In PaC, PANA session is associated with MAC addresses of PaC and PRE
  In PAA, PANA session is associated with IP addresses and port numbers of PaC, PAA and PRE (same as RFC 6345)

## Slide 11: Link Establishment KMP
  If a child node already has valid LLCs, it can skip Bootstrapping KMP and do Link Establishment KMP only
Link Establishment KMP depends on type of LLCs
    For PSK-based LLCs, use SAE, etc
    For pubkey-based LLCs, use HIP, etc