## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title:[Updated on MAC work for TG4k]
Date Submitted: [Sept 16, 2011]
Source:[Benjamin Rolfe]
Company [Blind Creek Associates]
Address []
Voice: [+1.408.395.7207], FAX: [None], E-Mail: [ben @ blindcreek.com]
Re:[Progress and MAC work]
Abstract:[Status and discussion points for MAC work on TG4k]
Purpose:[Final proposal presentation for Sept 2011 meeting]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Progress since January
Draft text merged and integrated with draft
Technical work identified in January discussed and resolved on TCs and emails
Several additional work items identified during TC and email discussions

## Slide 3: To do
Continue work to complete technical content
  Missing content in fragment cell and/or transaction context
  TBDs in draft
  Other gaps
Refine text
  Identify the normative changes/additions to base standard (all contributors)
  Re-organize informative content to correct sections (BR and MB)

## Slide 4: Fragmentation
In January, decided to move to more stateful – move as much as possible to transaction context and out of fragment cell
  Minimize recurring overhead
Some stuff got left out of both!
  Identified during TCs

## Slide 5: Fragment Cell Additions
LQI in I-ACK and fragment cells
  Intent was allow for PHY adjustments between cells
May be more than 32 fragments (oops)
  Extend fragment number and # fragments fields to 6 bits
How to tell a fragment cell from a PPDU that is not a fragment cell
  Need to tell an I-ACK from a fragment cell and from an PPDU containing unfragmented/compressed MPDU
  The “cell type” field (2-bits) could do it

## Slide 6: Transaction setup ACK
Transaction setup ACK format thoughts:
Setup ACK can include data pending - when your done I have stuff for you to.
Acknowledge that I heard you, but I have nothing to say (for TID zero to coordinator)
Acknowledge that I heard you but can’t accept a transaction

## Slide 7: Review TBDs
Transaction (link) context completion
RSLN Synchronization
Other synchronization
Reception and rejection (filtering, retransmission, validation) when MPDUF used.
I-ACK details
RSLN ack details
GTS allocation and management for RSLN
Some fragment fields descriptions
PHY dependent transaction context parameters
HWSL wakeup command and request details
RSLN link request and response commands details
CRC length for fragment cells
Details for service parameters
Primitives for RSLN
Fragment timeout considerations
PID details