## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Channel Hopping for DSME MAC Fragments]
Date Submitted: [March 13, 2012]
Source: [Wun-Cheol Jeong, Chang-Sub Shin]
Address []
Voice:[+82-42-860-5104], FAX: [], E-Mail:[wjeong@etri.re.kr]
Re: [IEEE P802.15.4k]
Abstract: [channel hopping method for DSME MAC fragments]
Purpose: [provides channel hopping method for DSME MAC Fragments]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Channel Hopping for DSME MAC Fragments
Slot ID 0
Channels
11
12
13
14
15
16
17
Slot ID 1
Slot ID 2
Slot ID 3
Slot ID 4
Hopping Sequence ID | Description
0x00 | a default hopping sequence
0x01 | a hopping sequence generated by PANCoord
0x02-0x0f | a hopping sequence set by higher layer
  Hopping Sequence List = {12, 15, 13, 17, 11, …}
Notes: doc.: IEEE 802.15-<doc#>
<11 January, 2008r>
        <author>, <company>
Page 2
doc.: IEEE 802.15-<doc#>
<11 January, 2008r>
        <author>, <company>
Page 2

## Slide 3: Channel Hopping for DSME MAC Fragments
Slot ID 0
Channels
11
12
13
14
15
16
17
Sub Slot n
Sub Slot n-1
Sub Slot n-2
Sub Slot n+1
Sub Slot n+2
Channels
11
12
13
14
15
16
17
MPDU
Slot ID 1
Slot ID 2
Slot ID 3
Slot ID 4
Fragmented MPDU
PHR
Notes: doc.: IEEE 802.15-<doc#>
<11 January, 2008r>
        <author>, <company>
Page 3
doc.: IEEE 802.15-<doc#>
<11 January, 2008r>
        <author>, <company>
Page 3

## Slide 4: Channel Hopping for DSME MAC Fragments
Example:
  Hopping Sequence List = {1, 2, 3, 4}
DSME-GTS Slot ID | PHY Hopping Sequence
0 | {1, 2, 3, 4}
1 | {2, 3, 4,1}
2 | {3, 4, 1, 2}
3 | {4, 1, 2, 3}
… | 

## Slide 5: Channel Hopping for DSME MAC Fragments
Example:
  Hopping Sequence List = {1, 2, 3, 4}
PHY Hopping Sequence | Logical Channel
{1, 3, 5 7} | 1
{2, 4, 6, 8} | 2
{9,11,13,15} | 3
{10,12,14,16} | 4

## Slide 6: Channel Hopping for DSME MAC Fragments
Example:
  Hopping Sequence List = {1, 2, 3, 4}
DSME-GTS Slot ID | PHY Hopping Sequence
0 | {1, 3, 5, 7}
1 | {2, 4, 6, 8}
2 | {9,11,13,15}
3 | {10,12,14,16}
4 | {1, 3, 5, 7}
… | …