## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [PAC Requirements]
Date Submitted: [14 March 2012]
Source: [Seung-Hoon Park, Chiwoo Lim, Pil-Yong Hwang, Kyungkyu Kim, Daegyun Kim, Won-il Roh] Company [Samsung Electronics]
Address [416, Maetan-3Dong, Yeongtong-Gu, Suwon-Si, Gyeonggi-Do, 443-742, Korea]
Voice:[+82-10-9349-9845], FAX: [+82-31-279-2441], E-Mail:[shannon.park@samsung.com]
Re: [.]
Abstract: [Initial exemplary baseline draft of application and technical requirements of PAC]
Purpose: [To discuss application/technical requirements and PAC design approach]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PAC Use-Cases (1/4)
SNS (Social Networking Service)
  User A and User B activate the same SNS application
  SNS application enables the interface to PAC module to broadcast PDI(Peer Discovery Information) including application ID, SNS user ID, profile or interest
  A’s device listens PDI from B’s device in the proximity
  A’s application is notified and decides to make a connection to B’s device
    B may be already known person to A in the SNS
    A may like B’s interest or profile
  A and B exchange text, voice, video, or etc each other

## Slide 3: PAC Use-Cases (2/4)
Advertising
  Retailer A is using an advertising application
  User B is playing a certain application which has a built-in push-based advertising component
  A’s device broadcasts PDI including application ID, coupon, sale, shop information, or etc
  B’s device does not broadcast, but listens and match the ad-related PDI
  B’s application is notified and show the ad through GUI when playing
  B’s application decides to make a connection to A’s device if more commercial information is required
  B is received more detail advertising information from A

## Slide 4: PAC Use-Cases (3/4)
Gaming
  User A activates a game application
  User B and User C who is playing the game application same as User A’s
  B and C is already connected and exchanging data
  A’s device broadcasts PDI including application ID, gamer ID, profile, ranking, or etc
  B’s or C’s application is notified by PDI from A’s device, and check whether to allow A’s entrance into the game or not
  B’s or C’s application makes a connection to A’s device
  A, B and C exchange data for game playing

## Slide 5: PAC Use-Cases (4/4)
Personal Broadcast
  User A activates a VJ(Video Jockey) application to broadcast the music video
  VJ application enables the interface to PAC module to broadcast PDI including application ID, VJ ID, genre, or etc
  Peer devices in the proximity listens PDI from B
  Some of peer devices playing the same VJ application can match PDI from B and notify to the application
  The application decides to make a connection to A’s device
  A’s application updates the audience list and responses to them with connection information
  A is broadcasting the streaming data

## Slide 6: PAC Application Requirements
 | Discovery Time | Data Rate | Latency | Range | Mobility
SNS text | < 10 s | 8~512 kbps1 | few seconds1 | < 1 km | < 8 km/h
SNS voip | < 10 s | 8~64 kbps2 | 100~200 ms2 | < 1 km | < 8 km/h
Advertising | < 10 s | 8~512 kbps1 | few seconds1 | < 3 km | < 60 km/h
Gaming | < 10 s | 64~512 kbps3 | 100~200 ms3 | < 1 km | < 8 km/h
Broadcasting | < 10 s | 2~5 Mbps1 | 100~200 ms1 | < 200 m | < 8 km/h
CE Convergence | < 1 s | 8~64 kbps2 | 20~100 ms2 | < 100 m | < 4 km/h
Emergency Service | < 10 s | 64~512 kbps4 | 100~200 ms4 | < 10 km | < 60 km/h
IST-4-027756 WINNER II D6.11.2 v1.0 Key Scenarios and Implications (WINNER II)
D1.1 Scenarios and Requirements Specification (Seventh Framework Program)
HyoJoo Park, TaeYong Kim, and SaJoong Kim "Network Traffic Analysis and Modeling for Games" in proc. WINE 2005.
Radio ommunication objectives and equirements for public protection and dsaster relief ITU-R M.2033

## Slide 7: PAR Scope
This standard defines PHY and MAC mechanism for Wireless Personal Area Networks (WPAN) Peer Aware Communications (PAC) optimized for peer to peer and infrastructureless communications with fully distributed coordination

## Slide 8: PAR Scope
Discovery for peer information without association
  discovery signaling rate, typically 100 kbps
  the number of devices in the discovery
Scalable data transmission rates, typically 10 Mbps
Group communications
  with simultaneous membership in multiple groups, typically up to 10
Relative positioning
Multihop relay
Security
Operational in selected globally available unlicensed/licensed bands below 11 GHz capable of supporting these requirements.

## Slide 9: PAC Technical Requirements (General Description)
Synchronization
  proximate nodes should be synchronized for other operation such as discovery, peer pairing, data transmission, to be efficient
  Synchronization should works in outdoor as well as indoor environment by interaction among proximate nodes
  Time to synchronized state at a certain area should be minimized
  Robustness to network dynamics

## Slide 10: PAC Technical Requirements (General Description)
Peer discovery
  PDI includes identifications presenting device, user, application, or etc
  PDI may include additional information for matching
  PDI may be broadcasted with a proper period according to application type
  Multi-hop peer discovery may be supported for a certain application
  Power consumption for peer discovery should be minimized to fulfill application requirements
  A certain type of PDI should be delivered securely

## Slide 11: PAC Technical Requirements (General Description)
Peer pairing
  Node A send request to the discovered node B for connection setup
  Node B response corresponding to the request from Node A
  Pair should be managed to be robust and scalable to network dynamics

## Slide 12: PAC Technical Requirements (General Description)
Data transmission
  Node in the proximal area join mutually with fully distributed manner to be efficient, scalable and robust
  The sum capacity of all PAC links in the certain area should be maximized
  Minimal control signaling overhead is preferred
  Each link should be managed considering QoS constraints