## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposed 900 MHz and 430 MHz Channelization in Japan for IEEE802.15.4k ]
Date Submitted: [15 March, 2012]
Source: [Shu Kato, Hirokazu Sawada, Hiroyuki Nakase] Company [ Tohoku University]
Address [2-1-1, Katahira, Aoba-ku, Sendai, Miyagi, Japan]
Voice:[+81-22-217-5506], FAX: [+81-22-217-5476], E-Mail:[shukato@riec.tohoku.ac.jp]
Re: [Channelization in Japan for 8082.15.4k]
Abstract: [900 MHz and 430 MHz Channelization for IEEE is proposed]
Purpose: [Presented to the IEEE802.15.4k LECIM task group for consideration]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Proposed 900 MHz and 430 MHz Channelization in Japan for IEEE802.15.4k
March 15, 2012
Shu Kato
RIEC Tohoku University

## Slide 3: 900 MHz and 430 MHz Japanese Regulations and Channelization Summary
900 MHz
The band, 915.9~929.7MHz is usable but need carefully to pay attention on complicated regulations
Need to coordinate USA 900 MHz channelization: starting with “0” frequency such as 902, 903, ..MHz (If it changes, need to follow)
Worked on 1024 kc/s, 512 kc/s, and 256 kc/s signal transmission
Some cases need relatively stringent filtering and high resolution D/A converters to meet out of band signal transmission power regulation
Worked on 250 mW, 1-20 mW, 1mW (or less) output power transmission
Came out with the workable numbers of channels for each bonded bandwidth, 400, 600, 1000 kHz
II. 430 MHz
Ten channels with 12.5 kHz spacing (8.5 kHz signal bandwidth) have been identified

## Slide 4: A New 900 MHz Spectrum Allocation in Japan : 13.8 MHz
Country | Tx power regulations
USA | Max e.r.p. <= 1 W
Korea | 3 mW or 10 mW (920.6~923.5MHz and six 200 KHz channels below 920.6 MHz)
Japan | 1mW , 20 mW or 250 mW (915.9~929.7MHz) Max BW = 1 MHz
902
928 MHz
917
923.5
929.7
26 MHz
6.5 MHz
US (max erp <=1 W)
Korea
Japan
(Max BW = 1MHz)
915.9
928 MHz
13.8 MHz

## Slide 5
900 MHz Available Channels in Japan (915.9~928.1MHz)(200 KHz BW/unit channel)
Tx Power= 1 mW or less

## Slide 6
900 MHz Available Channels in Japan (928.1~929.7MHz)(100 KHz BW/unit channel)
Tx Power: 1 mW or less

## Slide 7
Classification by Transmission Power
Case 1: Output power= 250 mW (ch. 24 - 38)
Case 2: Output power= 1 - 20 mW (Ch. 1-5, 54 – 61, 62 - 77 )
Case 3: Output power = less than 1 mW (Ch. 1-61, 62-77)
Power level at the occupied band edge: may decide usable
/ non-usable (may need signal bandwidth reduction,
“higher number of bits” in DAC) may be required)
2. Adjacent channel leakage power limitation

## Slide 8
Case 1 : Pout=250 mW
Radio Channel
Unit channel (Center/carrier frequency: from 920.6MHz to 923.4MHz, 200kHz step, ch 24 - 38）（Max boded unit channels: 5)

## Slide 9
400 kHz channels by bonding two unit channels (for 250 mW Transmission)

## Slide 10
600 kHz channels by bonding three unit channels (for 250 mW Transmission)
1 MHz channels by bonding five unit channels (for 250 mW Transmission)

## Slide 11
710
900
915
920.3
+200kHz
924.3
930
1000
1215
-36dBm/100kHz
-55dBm/1MHz
-55dBm/100kHz
-36dBm/100kHz
-29dBm/100kHz
-29dBm/100kHz
-36dBm/100kHz
-55dBm/100kHz
-45dBm/1MHz
-30dBm/1MHｚ
Adjacent channel
-5dBm/200kHz
Adjacent channel
-5dBm/200kHz
Out of band power regulation (920MHz band)
STD-108 Pout=250mW (24dBm)
Channel edge regulation
(In the case of using 920.0~922.3MHz)
+4dBm
-200kHz
Occupied
bandwidth
200kHz x N
Frequency
[MHz]
Pout=24dBm

## Slide 12
Case 1-1(Pout=250 mW) 922.5MHz~923.4MHz (Ch33~Ch38)
A. Power level limitation at the edge of occupied band: Not specified –
– possible to transmit 1 Mc/s signals
B. Adjacent channel leakage power : less than -5dBm/200 kHz
C. Further outer bands (shown in the following picture)
: -29 dBm/100 kHz (-53dBc from the peak power)

## Slide 13
Case 1-2 (Pout=250 mW), 920.6MHz~922.3MHz (Ch24~Ch32)
A. Power level limitation at the edge of occupied band
: less than +4 dBm (- 20 dBc from the peak power) - Not feasible to transmit 1Mc/s signals
B. Adjacent channel leakage power : less than -29dBm/200 kHz
C. Further outer bands (shown in the following picture)
: -29 dBm/100 kHz (-53dBc from the peak power)

## Slide 14
1MHz BW(5ch combined)
Available channels：1
(ch 33,34,35,36)
Channel starts from 922 MHz: good for USA coordination
600kHz BW(3ch combined)
Available channels：1
(ch 33,34,35)
400kHz BW(2ch combined)
Available channels：2
(ch 33,34 and Ch 36,37)
Channelization for Case 1-1 (Available channels: ch 33-38, guard band : one ch)

## Slide 15
Case 2: Output power = 1 – 20 mW
Radio channel
916 – 916.8 MHz, 920.6MHz - 928.0MHz
916.0MHz and 916.0MHz + N x 200kHz
920.6MHz and 920.6MHz + N x 200kHz
Unit channel bandwidth: 200 kHz, can be combined up to 5
2. 928.15MHz - 929.65MHz
928.15MHz and 928.15MHz + N x 100kHz
Unit channel bandwidth: 100 kHz, can be combined up to 5
Condition: Passive Systems have priority in these bands
Can not use the channels with center frequency of 920.6MHz to 922.2MHz (ch#24 – 32) and channels with center frequency of 922.4MHz or higher (ch#33~) simultaneously

## Slide 16
710
900
915
930
1000
1215
-36dBm/100kHz
-55dBm/1MHz
-55dBm/100kHz
-36dBm/100kHz
-36dBm/100kHz
-55dBm/100kHz
-45dBm/1MHz
-30dBm/1MHz
Out of band power regulation (920MHz band)
Pout=1mW～20mW
Frequency
[MHz]
Adjacent channel power leakage:
Pout=1～20mW: -15dBm/200kHz以下
Pout=1mW以下: -26dBm/200kHz以下
Pout=0 ~ 13dBm
+200kHz
-200kHz
Occupied
bandwidth
200kHz x N
Channel edge regulation
(In the case of using 915.9~922.3MHz)
-20dBm/100kHz @ Pout=0dBm
-7dBm/100kHz @ Pout=13dBm

## Slide 17
CASE 2-1(Pout=1-20 mW),
922.3MHz~928.1MHz (Ch 33~Ch 61)
Power level limitation at the edge of occupied band: Not specified
(Roll off filter (Alpha=0.6 ) may work)
B. Adjacent channel leakage power : less than -15dBm/200 kHz
C. Further outer bands (shown in the following picture)
: -36 dBm/100 kHz (-49dBc from the peak power)

## Slide 18
CASE 2-2 (Pout=1-20 mW),
920.5 MHz~922.3MHz (Ch 24~Ch 32)
A. Power level limitation at the edge of occupied band: -7dBm or less (20 dBc max), or -26 dBm or less (for 0 dBm Tx power output)
B. Adjacent channel leakage power : less than -15dBm/200 kHz, or -26 dBm or less (for 0 dBm Tx power output)
C. Further outer bands (shown in the following picture)
: -36 dBm/100 kHz (-49dBc from the peak power)

## Slide 19
Case 2-1
1MHz BW(5ch combined) (Ch 33~Ch 61)
Each channel to start at “0” MHz – 1.2 MHz for signal transmission bandwidth
(to coordinate USA frequency allocation)
(Roll off filter (Alpha= 0.17 ) may work)
Available channels：3 (ch. 33,34,5,36,37,ch. , ….)
1M
1M
1M

## Slide 20
Case 2-1 600 kHz BW(3ch combined) to transmit 512 kc/s signals (Ch 33~Ch 61)
Each channel needs: 0.8 MHz channel spacing for signal transmission (Roll off filter (Alpha= 0.6) may work)
Available channels：7 (ch. 33,34,35,ch , ….)
6K
6K
6K
6K
6K
6K
6K

## Slide 21
Case 2-1 400 kHz BW(2ch combined) to transmit 256 kc/s signals (Ch 33~Ch 61)
Each channel needs: 0.6 MHz channel spacing for signal transmission
Channels：10 (ch 33, 34 ….)
4K
4K
4K
4K
4K
4K
4K
4K
4K
4K

## Slide 22: Case 3: Output power= 1 mW or less
922.3MHz ~ 928.1MHz(Ch. 33～61)
Power level limitation at the edge of occupied band: Not specified
2. 915.9MHz ~ 916.9MHz (Ch. 1～5）
A. Power level limitation at the edge of occupied band:
- 20 dBm or less (20 dBc max)

## Slide 23
CASE 3-1 922.3MHz - 928.1MHz (Ch. 33～61)
A. Power level limitation at the edge of occupied band: Not specified – possible to transmit up to 1Mcps
B. Adjacent channel leakage power : less than -26 dBm/200 kHz
C. Further outer bands (shown in the following picture)
: -36 dBm/100 kHz (-36 dBc from the peak power)

## Slide 24
Case 3-2
A. Power level limitation at the edge of occupied band: -20 dBm or less –
not feasible to transmit 1Mc/s signals
B. Adjacent channel leakage power : less than -26 dBm/200 kHz
C. Further outer bands (shown in the following picture)
: -36 dBm/100 kHz (-36 dBc from the peak power)

## Slide 25
Channelization for Case 3-1 (Available channels: ch 33-61, guard band : one ch): 1 mW or less
1MHz BW x 3 channels ( by combining 5 unit channels )
Each channel starts with “0” (922, 924,..) to coordinate USA Spectrum

## Slide 26
600 kHz BW x 7 channels ( by combining 3 unit channels)
Each channel has 800 kHz channel spacing (Roll off filter (Alpha =0.5) may work
Channelization for Case 3-1 (Available channels: ch 33-61, guard band : one ch)

## Slide 27
400 kHz BW x 11channels ( by combining 2 unit channels)
Each channel has 600 kHz channel spacing (Roll off filter (Alpha =1.5) may work
Channelization for Case 3-1 (Available channels: ch. 33-61, guard band : one ch.)

## Slide 28: 400 MHz Frequency Availability in Japan
FDD channels for duplex communications only
Channel spacing: 12.5 kHz (8.5 kHz signal bandwidth) – spreading factor of 10
Frequency bands
: 429.8125 ~ 429.9250 MHz (ch. 1 ~ 10)
: 449.7125 ~ 449.8250 MHz (ch.1 ~ 10)

## Slide 29: 400 MHz Available channels in Japan : 12.5 kHz channel spacing (Occupied Bandwidth of 8.5 kHz or less) Channel No., Operating Frequency and Transmission Time restriction

## Slide 30: Conclusion
900 MHz Channelization
1. With Tx power of 250 mW
Channel starts from 922.1 MHz, Center: 922.8 MHz, 923.5 MHz ending,
Could be usable for USA
Available channels：1 ( ch. 33,34,35,36)
2. With Tx power of 1 -20 mW
1MHz BW(5ch combined) (Ch 33~Ch 61)
Each channel to start at “0” MHz – 1.2 MHz for signal transmission bandwidth (to coordinate USA frequency allocation)
(Roll off filter (Alpha= 0.17 ) may work)
Available channels：3 (ch. 33,34,5,36,37,ch. , ….)
3. With Tx power of 1 mW or less
1MHz BW (5ch combined) (Ch 33~Ch 61)
Each channel starts with “0” (922, 924,..) to coordinate USA Spectrum
Available channels：3 (ch. 33,34,5,36,37,ch. , ….)