## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title:[Refinements to Priority Access Text – discussion points
Date Submitted: [Sept 16, 2011]
Source:[Benjamin Rolfe]
Company [Blind Creek Associates]
Address []
Voice: [+1.408.395.7207], FAX: [None], E-Mail: [ben @ blindcreek.com]
Re:[Progress and MAC work]
Abstract:[Discussion slides for March 27 MAC subgroup conference call]
Purpose:[Refine and complete technical content of draft]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Specifying Priority Access in Beacon enabled PAN
Discussion and Refinement

## Slide 3: Basic Scheme in a nutshell
Reserve a time t the start of the Contention Access Period for priority access
Normal traffic waits until after this time to start slotted CSMA
Thus priority traffic has less contention and wins CSMA over normal traffic

## Slide 4: How we specify it
Reserve the first 2 slots of the CAP in every superframe
Which led to the observation that there has to be at least 2 slots in the CAP for this to work (actually there needs to be at least 3).
Which led to adding text that suggests the minimum CAP length has to consider “room” for priority slots and normal slots
Which led to….

## Slide 5: A problem?
Slot duration =
  2macSuperframeOrder × aBaseSlotDuration
  aBaseSlotDuration = 60
  macSuperframeOrder = 0 to 14
Slot duration =
(60, 120, 240, 480, 960, 1920, 3840, 7680,15360,30720, 61440 122880, 245760, 491520 983040) Symbols!
At a 1ms symbol … yikes?!?

## Slide 6: Proposal
What we really want is some period of time at the beginning of each CAP that is dedicated to priority traffic to avoid contention with normal traffic
Priority traffic events are infrequent (by definition) and probably short messages (to increase probability of reliable first-try delivery)
If we specify the priority period as a certain number of symbol periods we can achieve this
Suggest a multiple (possibly < 1) of aMinCAPLength (which is 440 symbol durations).

## Slide 7: Background

## Slide 8: Superframe Structure
802.15.4-2011
  SF consists of 16 slots;
  Slot 0 is defined as Beacon
  CAP is at least 440 Symbols duration
    Minimum CAP slots depends on slot duration
    Number of CAP slots = 15-# GTS slots
  CPF is up to 7 GTS slots
802.15.4e DSME
  More GTS slots achieved via multi-superframe,
  Each superframe
    The CAP is the first 9 slots
    CFP is the remaining 7 slots
  Number of SFs in a multi-superframes determined by macMultisuperframeOrder and macSuperframeOrder

## Slide 9: Beacon Order Vs Min CAP slots
aMinCAPLength = 440 symbols
macSuperframeOrder | Minimum CAP Slots | Slot Duration symbols
0 | 8 | 60
1 | 4 | 120
2 | 2 | 240
3 | 1 | 480
4..14 | 1 | 960.. 983040