## Slide 1: Summary of Latest Japanese 920MHz Rules and Conditions
Date: 2012-5-16
Authors:

## Slide 2: Purpose
The purpose of this document is to summarize the rules and conditions
with regard to upcoming Japanese 920MHz band, which is scheduled to
be opened up after July 24, 2012, following the consultation of Japanese
Telecommunication Council of MIC, of which summary was already
presented in TG-4g last July plenary (15-11/0510r04), and also to clarify
that the international standardization and VLSI design should be based
on the mandatory rules and conditions mentioned above.
Beside of mandatory rules and conditions, Japanese voluntary standard
defined by ARIB, called Std. T-108 (revised based on Std. T-96 in term
of 950MHz band) is also published, because this standard is expected to
be the factual deployment rules in Japanese 920MHz market, of which
summary is attached as Appendix of this submission.
* MIC : Ministry of internal affair and Communication

## Slide 3: Law ordinance and Voluntary ARIB Std. T-108
In the case of upcoming 920MHz band, the rules and conditions of Law
ordinance and ARIB Std. T-108 are not identical.
Every systems and devices operated in 920MHz band have to abide by
Law ordinance, so the device certification process and the test procedure
(TELEC Test procedure T-245/T-248) are based on Law ordinance , not
on ARIB Std. T-108.
Of course ARIB Std. T-108 is articulated to conform sufficiently with
Law ordinance, and is introducing additional rules, which are discussed
and arbitrated within open forum participated by several major industry
alliances and deployment entities. ARIB Std. T-108 recommends several
voluntary deployment rules including a boundary frequency (916.9MHz
and 922.3MHz, so far) in term of coexistence conditions, which is to be
re-examined in future and may be changed by ARIB.

## Slide 4: Law ordinance and Voluntary ARIB Std. T-108
Law ordinance
Radio law/Regulations for enforcement of radio law
Ordinance regulating radio equipment
Ordinance concerning technical regulations conformity certification
MIC (ministry)
Telecommunication
Council
Consultation
Specific
WGs
Parliament(House of representative)
TELEC
(Telecom Engineering Center )
ARIB
(Association of Radio Industries and Businesses)
ARIB Std.
(T-108)
Conformance
of
Product
Test Procedure (T-245/T-248)
Mandatory
Voluntary
Industrial
Alliances
System
Deploying entities

## Slide 5
Compulsory rules and conditions
Law ordinance

## Slide 6
<Frequency band and channelization>
Compulsory rules and conditions

## Slide 7: Entire 920MHz channelization
Frequency band usage
  Frequency band : 915.9MHz - 929.7MHz
  200kHz width element channel : 915.9 - 928.1MHz ( 61 channels )
  100kHz width element channel : 928.10 - 929.70 ( 16 channels )
  Shared portion with Passive RFID system : 915.9 - 923.5MHz
  Note: This boundary of 923.5MHz is supposed to be re-examined in future by MIC.
Limited channel usages depending on each Tx power level category
Eight categories of channel usage including passive RFID systems

## Slide 8
920MHz band and channelization for WSN and passive RFID systems
200kHz Element channel
100kHz Element channel
Passive RFID Systems |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Fixed Licensed （1W Licensed） |  |  |  |  |  |  |  |  | Fixed Light License （1W registered） |  |  |  |  |  |  |  |  | Specific Low Power （250ｍW） |  |  |  |  |  |  |  |  | Specific Low Power （10ｍW) |  |  |  |  |  |  |  |  | Data Return Ch. of Miller Sub-carrier Systems |  |  |  |  |  |  |  | 
Active Low Power or Convenience Radio Systems including Active RFID & WSN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Convenience Radio （250ｍW） |  |  |  |  |  |  |  |  | Specific Low Power （20ｍW) |  |  |  |  |  |  |  |  | Specific Low Power （1ｍW） |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
１W PassiveID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
１W・LBT PassiveID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
250mW PassiveID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10mW PassiveID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ch |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | # | # | # | # | # | # | # | # | # | # | # | # | # | # | # | #
Center Frequency | 915.8 | 916.0 | 916.2 | 916.4 | 916.6 | 916.8 | 917.0 | 917.2 | 917.4 | 917.6 | 917.8 | 918.0 | 918.2 | 918.4 | 918.6 | 918.8 | 919.0 | 919.2 | 919.4 | 919.6 | 919.8 | 920.0 | 920.2 | 920.4 | 920.6 | 920.8 | 921.0 | 921.2 | 921.4 | 921.6 | 921.8 | 922.0 | 922.2 | 922.4 | 922.6 | 922.8 | 923.0 | 923.2 | 923.4 | 923.6 | 923.8 | 924.0 | 924.2 | 924.4 | 924.6 | 924.8 | 925.0 | 925.2 | 925.4 | 925.6 | 925.8 | 926.0 | 926.2 | 926.4 | 926.6 | 926.8 | 927.0 | 927.2 | 927.4 | 927.6 | 927.8 | 928.0 | 928.15 | 928.25 | 928.35 | 928.45 | 928.55 | 928.65 | 928.75 | 928.85 | 928.95 | 929.05 | 929.15 | 929.25 | 929.35 | 929.45 | 929.55 | 929.65
1mW ActiveWSN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
20mW ActiveWSN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
250mW ActiveWSN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ○ | ○ | ○ | ○ | ○ | ◎ | ◎ | ◎ | ◎ | ◎ | ○ | ○ | ○ | ○ | ○ | ○ | ○ | ○ | ○ | ○ | ○ | ○ | ○ | ○ | ○ | ○

## Slide 9: 920MHz band channelization & usage rules in term of Active WSN
Category ( Based on maximum Tx Power ) | 
Specified Low Power 1mW (3dBm eirp) [License exempt] | 1mW or less Tx power: 915.9-928.1MHz, 61x 200kHz element channels
Specified Low Power 20mW (16dBm eirp) [License exempt] | 20mW or less Tx power: 920.5-928.1MHz, 38x 200kHz elementary channels
Convenient Radio 250mW (27dBm eirp) [Registration required] | 250mW or less Tx power: 920.5-923.5MHz, 15x 200kHz elementary channels
Data Transmission |  | 
Modulation Scheme | Not specified, i.e. any modulation can be used. | 
Bundled usage of Element channels ( ~ max. occupied signal width ) |  | 
Maximum number of Element channels |  | Up to 5 channels, (1MHzBWmax.)

## Slide 10
920MHz Band channel usage rule for WSN Systems
(Relating to 11ah)
ch | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61
Center Frequency | 916.0 | 916.2 | 916.4 | 916.6 | 916.8 | 917.0 | 917.2 | 917.4 | 917.6 | 917.8 | 918.0 | 918.2 | 918.4 | 918.6 | 918.8 | 919.0 | 919.2 | 919.4 | 919.6 | 919.8 | 920.0 | 920.2 | 920.4 | 920.6 | 920.8 | 921.0 | 921.2 | 921.4 | 921.6 | 921.8 | 922.0 | 922.2 | 922.4 | 922.6 | 922.8 | 923.0 | 923.2 | 923.4 | 923.6 | 923.8 | 924.0 | 924.2 | 924.4 | 924.6 | 924.8 | 925.0 | 925.2 | 925.4 | 925.6 | 925.8 | 926.0 | 926.2 | 926.4 | 926.6 | 926.8 | 927.0 | 927.2 | 927.4 | 927.6 | 927.8 | 928.0
1mW ActiveWSN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
20mW ActiveWSN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
250mW ActiveWSN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Active Low Power or Convenience Radio Systems including Active RFID & WSN |  |  |  |  |  |  | 
 | Convenience Radio （250ｍW） |  | Specific Low Power （20ｍW) |  | Specific Low Power （1ｍW） |  | 
[Registration Required]
(Light licensing scheme)
[License exempt]
[License exempt]

## Slide 11
<Transmission control requirements>
Compulsory rules and conditions

## Slide 12: Transmission control requirements for each system categories
LDC |  | 
1mW category | 3.6s per 1 hour | ( or Less than 0.1%)
20mW or 250mW Category | 360s per 1 hour | ( or Less than 10%)
 | not required (LBT>5ms) | within 4s max. Tx followed by 50ms idle at 920.5MHz-923.5MHz.
Max. Transmission Duration |  | 
1mW Category | 100ms | for 200KHz element channels, 50ms for 100KHz cases.
20mW or 250mW Category | 400ms (LBT>128us) | (ARIB T-96 recommends 200ms or 100ms in some conditions)
 | 4s (LBT>5ms) | 4s (LBT>5ms) is only permitted for 920.5MHz-923.5MHz.
Idle period after Transmission |  | 
1mW Category | 100ms | for 200KHz element channels, 50ms for 100KHz cases.
20mW or 250mW Category | 2ms (LBT>128us) | (not required if Tx duration was no more than 6ms)
 | 50ms (LBT > 5ms) | 50ms (LBT>5ms) is only valid for 920.5MHz-923.5MHz.
LBT requirement |  | 
1mW Category | not required | 
20mW or 250mW Category | listen more than 128us | -80dBm (ED Level) regardless of bundled number of channels.
 | listen more than 5ms | LBT>5ms is only valid for 920.5MHz-923.5MHz.

## Slide 13: Exception of LBT
Data/Request/Query
LBT
(Clear)
Response
(Ack)
Node A
Node B
Within 50ms
Exemption
of LBT
time
time
(Only in case of same frequency channel)
Short Response including Ack frame following Data, Request and
Query needs no LBT, if Tx completes within 50ms on same channel.
Short Response don't have to be taken account into LDC.
e.g. 360s per 1hour limit is not affected by Ack response.
( ARIB std. T-108 recommends a few additional conditions over law ordinance above. )

## Slide 14
<Adjacent leakage power & spurious emission>
Compulsory rules and conditions

## Slide 15
Adjacent leakage & spurious emission
Maximum Spurious Emission
710
917
919
921
930
940
(MHz)
-36
dBm/100kHz
-65(-55dBm/MHz)
-55
-39
-61
MCA
Cellular
LTE
-55
-36
-29 ( 20mW < P =< 250mW)
-65
(Antenna Gain must be less than 3dBi.)
電子タグシステム
WSN
Provision of Channel Mask
Spur
Emi dBm
/100kHz
fc
fc+(N+1)*100kHz
Adjacent Channel
Leakage
Category | Max. Leakage
200kHz adjacent element channel | 
(output power: P) | (dBm/200kHz)
P =< 250mW | -5dBm
P =< 20mW | -15dBm
P =< 1mW | -26dBm
Figure below
1215
-55
-45dBm/MHz
-36
920.3MHz
924.3MHz
Adjacent Channel Leakage
Right Table
-36
-36 ( P =< 20mW )
915
900
960

## Slide 16
Frequency ( level at Tx output to Antenna ) | Max. Spurious Emission (Average Power) | Reference Bandwidth
Lower than or equal to 710MHz | -36dBm | 100kHz
Higher than 710MHz and up to 900MHz | -55dBm | 1MHz
Higher than 900MHz and up to 915MHz | -55dBm | 100kHz
Higher than 915MHz and up to 920.3MHz * | -36dBm | 100kHz
Higher than 920.3MHz and up to 924.3MHz * (except for the region within (200+100 n) KHz; n=number of bundled element channels) | -29dBm : (Tx power >20mW) -36dBm : ( otherwise ) | 100kHz
Higher than 924.3MHz and up to 928.1MHz * (except for the region within (200+100 n) KHz; n=number of bundled element channels) | -36dBm | 100kHz
Higher than 928.1MHz and up to 930MHz (except for the region within (100+50 n) KHz; n=number of bundled element channels) | -36dBm | 100kHz
Higher than 930MHz and up to 1GHz | -55dBm | 100kHz
Higher than 1GHz and up to 1.215GHz | -45dBm | 1MHz
Beyond 1.215GHz | -30dBm | 1MHz
Spurious emission
Emission from enclosure has to be less than the corresponding EIRP value with above value. Max. Antenna Gain is 3dBi.

## Slide 17
Frequency ( level at Tx output to Antenna ) | Max. Spurious Emission (Average Power) | Reference Bandwidth
Lower than or equal to 710MHz | -54dBm | 100kHz
Higher than 710MHz and up to 900MHz | -55dBm | 1MHz
Higher than 900MHz and up to 915MHz | -55dBm | 100kHz
Higher than 915MHz and up to 930MHz | -54dBm | 100kHz
Higher than 930MHz and up to 1GHz | -55dBm | 100kHz
Beyond 1GHz | -47dBm | 1MHz
Parasitic emission of Rx
- Be measured at the condition that Rx operation has to be activated,
while Tx circuitry may be disabled.
- A measurement using temporal antenna terminal is allowed in both case of
measurements in term of Tx spurious emission and Rx parasitic emission,
provided that the loss difference between real antenna and temporal terminal
has to be compensated.

## Slide 18
<Spectrum masks>
Compulsory rules and conditions

## Slide 19
Spectrum mask
Center Frequency
200KHz
(200 n) KHz
200KHz
< 1mW Category (915.9 ~ 928.1MHz) >
-36dBm/100KHz
(915 ~ 930MHz)
Spurious Emission
-26dBm/200KHz(915.9-928.1MHz)
Upper Adjacent Leakage Emission
-26dBm/200KHz (915.9-928.1MHz)
Lower Adjacent Leakage Emission
0dBm/(200 n) KHz
Av. Signal Power

## Slide 20
Spectrum mask
Center Frequency
200KHz
(200 n) KHz
200KHz
< 20mW Category (920.5 ~ 928.1MHz) >
-36dBm/100KHz
(915 ~ 930MHz)
Spurious Emission
-15dBm/200KHz
Lower Adjacent Leakage Emission
13dBm/(200 n) KHz
Av. Signal Power
-15dBm/200KHz
Upper Adjacent Leakage Emission

## Slide 21
Spectrum mask
Center Frequency
200KHz
(200 n) KHz
200KHz
< 250mW Category (920.5 ~ 923.5MHz) >
-29dBm/100KHz
(915 ~ 930MHz)
Spurious Emission
-5dBm/200KHz
Lower Adjacent Leakage Emission
24dBm/(200 n) KHz
Av. Signal Power
-5dBm/200KHz
Upper Adjacent Leakage Emission

## Slide 22
<Miscellaneous >
Compulsory rules and conditions

## Slide 23: Frequency Tolerance
Within ±20 ppm
Tx power Tolerance
Between +20% and -80% of the designed power level
Antenna Gain
+3dBi max. with max. Tx power allowed.
Higher gain antenna is allowed to use, provided that
EIRP level is kept below than that with max. Tx power
using +3dBi antenna.
Permitted Communication
Simplex (with or without Rx), Duplex (FDD, CDD, etc.),
half Duplex (TDD), Broadcast and Multicast.

## Slide 24
< Reference >
- IEEE802.11 Doc:
11-11-0974-01-00ah-Consultation-Summary-of-Japanese-920MHzBand-Rules-and-Conditions
- Press Release of MIC ( written in Japanese )
< http://www.soumu.go.jp/menu_news/s-news/0kiban14_01000036.html >
- Summary Table of 920MHz RFID/WSN systems ( written in Japanese )
< http://www.soumu.go.jp/main_content/000119517.pdf >
- Consultation Report for public comments ( written in Japanese )
< http://www.soumu.go.jp/main_content/000113160.pdf >
- TELEC Test procedure document for radio certification (written in Japanese)
< http://www.telec.or.jp/book/files/h2405_kaitei_self07.pdf > (Purchase required)
- ARIB Std. T-108 ( written in Japanese )
< http://www.arib.or.jp/english/html/overview/doc/1-STD-T108v1_0.pdf >
English translation of ARIB Std. T-108
< http://www.arib.or.jp/english/html/overview/doc/5-STD-T108v1_0-E1.pdf >

## Slide 25
Appendix

## Slide 26
Voluntary deployment rules and conditions
Recommendation of ARIB Std. T-108

## Slide 27
<Frequency channelization and usage>
Additional rules recommended by ARIB Std. T-108

## Slide 28: Recommended channelization by ARIB Std. T-108
Further channel usage sub-categorization over MIC regulation
  Frequency band : 915.9MHz - 929.7MHz
  200kHz width element channel : 915.9 - 928.1MHz ( 61 channels )
  Introducing two additional frequency boundary at 916.9 & 922.3MHz
  Corresponding spectrum masks including band-edge notation
  Note: This band-edge notation is associated with no consistent
  measurement procedure so far. Both TELEC T-245 and 248
  include no performance requirement on this notation.
Further transmission control sub-categorization are introduced
  Sub-categorization in term of :
    Frequency portion of channel
    Transmission duration and pause duration
    Number of bundled channel, and so on

## Slide 29
920MHzBand Channel usage Plan of each RFID/WSN Systems
(Recommended by ARIB Std. T-108)
Additional boundary at 922.3MHz
Additional boundary at 916.9MHz

## Slide 30
<Spectrum masks>
Additional rules recommended by ARIB Std. T-108

## Slide 31
< 915.9~916.9MHz portion of 1mW Category(915.9~928.1MHz) >
Additional spectrum mask of ARIB Std. T-108

## Slide 32
< 920.5~922.3MHz portion of 20mW Category(920.5~928.1MHz) >
Additional spectrum mask of ARIB Std. T-108

## Slide 33
< 920.5~922.5MHz portion of 250mW Category(920.5~923.5MHz) >
Additional spectrum mask of ARIB Std. T-108

## Slide 34: <Transmission Control recommendation of ARIB Std. T-108>
Additional rules recommended by ARIB Std. T-108

## Slide 35
Transmission Control recommendation of ARIB Std. T-108

## Slide 36: Transmission Control recommendation of ARIB Std. T-108 (Continued)

## Slide 37
Transmission Control recommendation of ARIB Std. T-108 (Continued)

## Slide 38
End