## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Future Standardization Plan in IG-LED]
Date Submitted: [, 2012]
Source: [Yeong Min Jang, Vu Van Huynh]
[Kookmin University]
Address [Kookmin University, Seoul, Korea]
Voice:[82-2-910-5068], FAX: [82-2-910-5068], E-Mail:[yjang@kookmin.ac.kr]
Re: []
Abstract: []
Purpose: [Contribution to IEEE 802.15 IG-LED]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 15-12-0277-00-wng0
Notes: doc.: IEEE 802.15-09-0117-00-0007
<month year>

## Slide 2: Contents
Overview IEEE 802.15.7 VLC
  PHY layer
  MAC sub-layer
Key issues in LED Communications
Conclusion
doc.: IEEE 15-12-0277-00-wng0

## Slide 3: PHY layer
The PHY is responsible for the following tasks:
  Activation and deactivation of the VLC transceiver
  WQI (wavelength quality indicator) for received frames
  Channel selection
  Data transmission and reception
  Error correction
  Synchronization
doc.: IEEE 15-12-0277-00-wng0

## Slide 4: MAC Sub-layer
The MAC layer handles all access to the physical layer and is responsible for the following tasks:
  Generating network beacons if the device is a coordinator
  Synchronizing to network beacons
  Supporting VPAN association and disassociation
  Supporting color function
  Supporting visibility
  Supporting dimming
  Flicker removal scheme
  Supporting visual indication of device status and channel quality
  Supporting device security
  Providing a reliable link between two peer MAC entities
  Supporting mobility
doc.: IEEE 15-12-0277-00-wng0

## Slide 5: Super-frame Structure
Contention access period (CAP)
  The CAP shall start immediately following the beacon and complete before the beginning of the CFP on a super-frame slot boundary
Contention-free period (CFP)
  The CFP shall start on a slot boundary immediately following the CAP and it shall complete before the end of the active portion of the super-frame.
CAP
Beacon
CFP
doc.: IEEE 15-12-0277-00-wng0

## Slide 6: Multi-Frame Type
Proposed LED Communication for indoor LBS applications
  Data Frame: Data
  Control Frame: Beacon, Synchronization,
  Acknowledgement, Command, CVD, location information.
doc.: IEEE 15-12-0277-00-wng0

## Slide 7: Mobility and Link Switching Issues
Mobility includes two types: physical and logical
  Physical mobility occurs when the VLC
  device M1 changes its position due to the
  movement within the coverage area of
  infrastructure I1
  Logical mobility occurs when the device
  M1 changes its communication link from
  a link with infrastructure I2 to one with
  infrastructure I3
doc.: IEEE 15-12-0277-00-wng0

## Slide 8: Location-Aware Link Switching Scheme
Minimize the link switching delay.
Reduce the number of scanned neighbor tags
doc.: IEEE 15-12-0277-00-wng0

## Slide 9: Position Based Mobile Cleaning Robot
Based on LBS service, provide mobile cleaning robot control in the indoor LED environment.
doc.: IEEE 15-12-0277-00-wng0

## Slide 10: Interference Issues and Scenarios
Inter-application interference
Intra-application interference
Adjacent color interference
doc.: IEEE 15-12-0277-00-wng0

## Slide 11: Hidden Terminal Problem in LED Communications
Current IEEE802.15.7 VLC specification:
  Limited Field Of View (FOV)
  Inefficient CSMA/CA
C can not sense B’s signal when it tries to
access the channel.
A
FOV
C
B
doc.: IEEE 15-12-0277-00-wng0

## Slide 12: Dynamic FOV Adjustment
Dynamic FOV adjustment based on location information
  Reduce interference.
  Increase reliability.
doc.: IEEE 15-12-0277-00-wng0

## Slide 13: Cooperative and Relay Networks
Direct communication
  Less delay
  High packet loss
Multi-hop communication
  More delay
  Low packet loss
LED
Reader #3
Reader #2
Multi-hop
Reader
LED
Direct
doc.: IEEE 15-12-0277-00-wng0

## Slide 14: Cooperative and Relay Network
Performance improvement of LED-ID network
  Delay
  Throughput
  Loss probability
Increase coverage
Reader #3
Reader #2
LED
doc.: IEEE 15-12-0277-00-wng0

## Slide 15: Visible RFID
RFID system
Visible RFID system
Reader
Tags
Reader
Tags
RF
doc.: IEEE 15-12-0277-00-wng0
Visible light

## Slide 16: Visible RFID
Property | RF |  | VLC | Visible RFID
 | Active | Passive |  | 
PHY | RF | RF | VLC | VLC & RF
Sensing ability | Yes | No | FOV restriction | Utilizing the FOV characteristics
Collision | High | High | High | Low
VLC receiver
VLC transmitter
RF module
RF module
Tag
Reader
Communication interfaces
  Identification process by VLC interface
  Data transmission by RF interface
Advantage
  Interference reduction
    SNR improvement
    Ranging selective tag
  Efficient bandwidth utilization
doc.: IEEE 15-12-0277-00-wng0

## Slide 17: Conclusion
IEEE 802.15.7 defines a PHY and MAC for short-range optical wireless communications using visible light
IEEE 802.15.7 is capable of delivering data rates sufficient to support:
  Audio and video multimedia services.
  Mobility of the visible link.
  MAC layer that accommodates visible links.
Some key issues in current LED Communications and Positioning techniques: commercial services, implementation issues, support multi-frame type, fast link switching, LBS applications, interference management, hidden terminal problems, dynamic FOV, cooperative and relay network, visible RFID(RFID+VLC), spectrum relief issues, automobile applications, applications of smart phone .
doc.: IEEE 15-12-0277-00-wng0