## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Standardization Issues in LED-ID Techniques]
Date Submitted: [May 14, 2012]
Source: [Yeong Min Jang, Vu Van Huynh]
[Kookmin University]
Address [Kookmin University, Seoul, Korea]
Voice:[82-2-910-5068], FAX: [82-2-910-5068], E-Mail:[yjang@kookmin.ac.kr]
Re: []
Abstract: [] 15-12-0279-00-wng0
Purpose: [Contribution to IEEE 802.15 IG-LED]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 15-12-0279-00-wng0
Notes: doc.: IEEE 802.15-09-0117-00-0007
<month year>

## Slide 2: Contents
Introduction
Standardization issues in PHY
Standardization issues in MAC
Conclusion
doc.: IEEE 15-12-0279-00-wng0

## Slide 3: Network Architecture for LED-ID Application
1 | Wake Up | Tag wakes up when readers send request
2 | Beacon | Tag will be synchronized by superframe
3 | Request | Reader requests traffic
4 | Resource Allocation | Tag allocates slots based on reader’s request
5 | Data Transmission | Data transmission using allocated slot
doc.: IEEE 15-12-0279-00-wng0

## Slide 4: Comparison of ID Technologies
 | Bar Code | RFID (Passive) | LED-ID
Signal Format (Transmission medium) | Printed image | RF | LED light (Visible Light Infra-red Light Ultra Violet Light etc)
Reliability | Wrinkled or smeared labels will not be read | Nearly flawless read rate | Flawless read rate
Readable through objects | No, must be line of sight | Yes | Depend on FOV
Orientation dependence | Yes | No | 
Read speed | Slow | Fast | Variable Speed
Multiple tags | No | Yes (10-1000 tags per second) | Yes
Updateable | No | Yes | Yes
Data type | Non real-time | Non real-time | Non real-time and real-time
Tag and reader position | Scanner needs to see the bar code to read it | No need to bring the tag near the reader | Need to bring within the FOV
QoS | No need | Not support QoS | Support QoS
Communication | Half-duplex | Duplex | Duplex
Possibility to use Existing Infrastructure | No, New setup | No, New setup | Yes Existing infrastructure may be used
doc.: IEEE 15-12-0279-00-wng0

## Slide 5: Interference Management
Difference frequency using for difference FOV.
Interference avoidance and increasing the utilizing bandwidth
doc.: IEEE 15-12-0279-00-wng0

## Slide 6: MAC Approach
Processing state
Process of Tag
doc.: IEEE 15-12-0279-00-wng0

## Slide 7: MAC Approach
Process of Reader
doc.: IEEE 15-12-0279-00-wng0

## Slide 8: Link Recovery
Unreliable LED-ID link for obstacles.
Recover the link ASAP
Link Recovery Scheme using Cooperative Communication
Sender
Receiver
Relay node
doc.: IEEE 15-12-0279-00-wng0

## Slide 9: Location-Aware Fast Link Switching Scheme
Tag#1
Tag#2
Tag#3
Tag#4
Tag#5
Tag#6
Tag#7
Tag#8
Tag#9
Direction
Serving Tag
Multi-tags scenario of LED-ID system
doc.: IEEE 15-12-0279-00-wng0

## Slide 10: Location-Aware Fast Link Switching Scheme
Tag 2 (X2,Y2)
Past Position
Current Position
(X1,Y1)
(X2,Y2)
(X3,Y3)
α1
α2
α3
L1
L2
L3
Tag #4 (X4,Y4)
Tag #5 (X5,Y5)
Past Position | (X1, Y1)
Current Position | (X2, Y2)
Predicted Position | (X3, Y3)
Tag #1 | (X1, Y1)
Tag #4 | (X4, Y4)
Tag #5 | (X5, Y5)
Neighbor Position Table of Serving Tag
Tag #1 (X1,Y1)
α
Serving Tag
Reader Position Table of Serving Tag
doc.: IEEE 15-12-0279-00-wng0

## Slide 11: Cooperative and Relay Network
Increase the coverage
Reduce blocking probability
Applicable to a Link recovery scheme
Direct communication
Cooperative communication
Multi-hop communication
doc.: IEEE 15-12-0279-00-wng0

## Slide 12: Cooperative MAC Protocol for LED-ID
Why using Cooperative and Relay Network for LED-ID
  Interference from another light source
  Link disconnection from movement obstacle
  Limited of FOV
Applications
  Real-time service: QoS application
Advantages
  Reliable network
  Increasing the coverage
Disadvantages
  Working on dense mobile node ( discovery relay node)
  Large FOV
  Complexity
doc.: IEEE 15-12-0279-00-wng0

## Slide 13: Conclusion
LED-ID is one of the ID techniques and it has many advantages of using visible light.
The issues which are presented will be the important topics in future standardization about LED-ID.
FOV limitation is one of the most important issues in LED-ID techniques.
Contribute to IG-LED about the LED-ID issues starting July meeting.
doc.: IEEE 15-12-0279-00-wng0