## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Miscellaneous MAC work update
Date Submitted: [Sept 16, 2011]
Source:[Benjamin Rolfe]
Company [Blind Creek Associates]
Address []
Voice: [+1.408.395.7207], FAX: [None], E-Mail: [ben @ blindcreek.com]
Re:[Progress and MAC work]
Abstract:[Update on MAC related fixes and ]
Purpose:[Refine and complete technical content of draft]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Transaction ID Uniqueness
How do we determine the Transaction ID?
  In the context of a fragmentation transaction, the TID replaces addressing;
  Need to avoid unintended devices recogizing TID at the wrong time
Can it be done with sufficiently low probability of conflict over the duration of the transaction?
  YES, several methods discussed
  Depends on PHY (example: Code separation in DSSS)
  Want to avoid overhead in fragment
Should we specify the function for determining the TID?
  No, should be implementation specific
Should provide sufficient means for interoperability
  Possibly give an example in the informative annex?

## Slide 3: Transaction ID Uniqueness
Methods to provide:
  Provide parameters in the setup message:
    Offset for FVS location in the cell;
      Default is zero
      Support for non-zero optional
    FVS CRC initialization vector
      Default is same as FCS IV
      Support for non-zero optional
  Allow for optimally including addressing in fragment
    Makes sense for FSK and other PHYs in base standard
    Optional and only when makes sense (i.e. not in 16-octet fixed PPDU mode)

## Slide 4: Transaction Uniqueness
Probability of random conflict w/o addressing:
For devices on common logical channel:
  Transaction ID @ 10 bits 1/1024
    With 1000 active transactions 97%
  Offset location of CRC in fragment cell
    Fragment: > ~1/80 [DSSS 16 octet PSDU, better with longer PSDU]
    I-ACK: >~ 1/16 [shortest IACK]
  Variable CRC initialization vector:
    Approximately 1/216 or 1/232
At least 9.313368e-10 , as much as 2.842171e-15 of separation provided if all three used

## Slide 5: Transaction Uniqueness
PHY dependence?
  For LECIM DSSS, code separation can be used
  For UWB PHY, preamble codes provide separation
  For other PHYs when used with frequency hopping, randomization in hopping may be enough
  So…Minimize set-up overhead and add no fragment overhead

## Slide 6: Additional Parameters for Context
Add to 5.2.4.23 MPDU Fragment Sequence Context Description IE:
Change Reserved field in Figure 48no to TID Extension field. Show TID parameters before addressing, length is 0/24/40 bits;
Add description: TID extension: Indicates that a TID Parameters field is present.
Add description of TID Parameters Field:
  FVS Offset [7 bits]: indicates an octet offset from the last octet of the PSDU; A value of zero means the FVS follows last octet of PSDU (i.e. at the end); value must be bounded by PSDU length.
  CRC IV 16 or 32 bits depends on macFragmentCVSType value; provides initialization value to be used in the CRC calculation.

## Slide 7: Other misc issues
Fragment # value for “abort”
  In one place says use 0 to mean “quit” (Fragment)
  In another (IACK) says use 0 to mean “I-ACK”
Suggest fragment # of zero means “abort” both ways
Suggest in I-ACK fragment # is the last fragment recieved