## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed Approach for MAC changes for TVWS
Date Submitted: [July 2012]
Source:[Benjamin A. Rolfe1, Kunal Shah2]
Company [Blind Creek Associates1, Silver Spring Networks2]
Address []
Voice: [+1.408.395.7207], FAX: [None],
E-Mail: [ben @ blindcreek.com, kshah @ silverspringnet.com]
Re: Support 4tv PHY development
Abstract: Proposed approach to address MAC requirements for TVWS
Purpose: Contribution to draft development
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Proposed Approach for MAC changes for TVWS
Essential MAC capabilities to support 15.4 operation in TVWS

## Slide 3: Goals
Enable meeting known regulatory requirements for TVWS operation
Insulate 802.15.4m from new regulations and changes in regulations
Promote efficient development and approval of TVWS PHY Amendment
Align with other proposals in TG4m
Align with other work on 802.15.4
Take advantage of existing MAC capacities

## Slide 4: General Approach
Review requirements
Propose MAC operation to address required operation
Present appropriate over-the-air exchange format

## Slide 5: 802.15.4 differentiation
How is 802.15.4 different from other 802 services?
Ability to operate peer-to-peer (including Mode I) without a PAN coordinator involved in the transaction
Role of Coordinator, PAN Coordinator not tied to Mode I/Mode II device – Either Mode I/Mode II could be PAN coordinator or not.
Communicating peer device may get TVWS channel information from different sources
Source of TVWS channel availability is not tied to the role of PAN Coordinator: Any device with access to the database, either via direct out-of-band connection or other means can be the source
Ability of any device to share channel availability information with other devices
Ability of a device to autonomously determine if the channel information received is valid for its current geo-position and/or circumstances.

## Slide 6: Concurrent work
IETF Protocol to Access White Space database (PAWS)
  Database access over the internet
  IETF project (early stage)
  XML/HTTPS/SSL/TCP/IP (higher layers from 802 perspective)
  Provides a good model of the content of messages to/from TVWS database
  Message formats not compact
Other 802 projects
  802.22 includes spectrum manager function, specific formats
  802.11 provides MAC formats for WS related data
  Similar message content to PAWS, more compact representations

## Slide 7: Basic Terminology (for this discussion)
Based on FCC Part 15 Subpart H (most complete and well known at this time):
Fixed: Not moved after installation, assumed to have internet access to database
Mode II Device: Might move after installation, assumed to have internet access to database (directly or indirectly)
Mode I Device: Assumed does not have access to database, depends on Mode II or fixed device for which channels it can use

## Slide 8: TVWS Database Access
Basic operations to be supported
Discovery of database server(s)
Device registration
FCC ID Verification Request
White Space Channel Query
White Space Channel Update
Source: FCC, PAWS

## Slide 9: Database Access via IP
Logical approach for internet-connected devices
IP end to end advantages
  Transport and security well defined
  Agnostic to underlying NWK/MAC/PHY
  Seems like what regulatory bodies are expecting
IP end to end disadvantages
  Verbose encoding expensive for low data rate and low duty cycle systems
  Doesn’t give the full story for devices with TVWS only interface

## Slide 10: 802.15.4 TVWS Basic Needs
For a device with only TVWS interface
Ability for database connected fixed and/or Mode II devices to advertise a valid channel for initial contact (channel data source)
Means for device FCC ID verification, which requires 2-way communication via the contact channel between the Mode I device and valid channel data source
Means for sending the available channel information following validation of the device ID initially and to update the information when something changes
Means for periodic or on-demand contact verification signaling between the fixed/mode II device and the mode I device.
Ability to send channel data securely

## Slide 11: Scope considerations
Assume a higher layer spectrum management entity (SME) in the higher layer Device Management Entity (DME)
  Outside the scope of 802.15, requirements defined by applicable regulations (which will change)
Suggests how SME “might” operate using 15.4 MAC
  Could be information in the standard or external document
Define efficient information element (IE) encodings to support the required information exchange
  IEs can added to data, MP, beacons or MAC command frames
IEs may be defined in the MAC (?)
Could be defined outside the MAC (?)
  Examples: 802.15 RP, informative annex to 802.15.4
Could be shared outside 802.15 (?)
  Similar problem for all other802 standards that operate in TVWS
(?) indicates need for TG discussion

## Slide 12: Define IEs optimized for 802.15.4
Advantage:
  Can Optimized representation for 802.15.4 low data and duty cycles to reduce the on air overhead and interference footprint
Disadvantage:
  Content and requirements may change w/regulatory changes
  Content may be specific to region
  Adds overhead to representation
Optimization methods:
  Elide information based on context (MAC or HL)
  Elide information based on characteristics of the 802.15.4 protocol (MAC, RP or informative annex)
  Elide information based on the characteristics of the applications (higher layer)

## Slide 13: TVWS access with the 802.15.4 MAC

## Slide 14: 802.15.4 TVWS Basic Needs
For a device with only TVWS interface
Ability for database connected fixed and/or Mode II devices to advertise a valid channel for initial contact (channel data source)
Means for device FCC ID verification, which requires 2-way communication via the contact channel between the Mode I device and valid channel data source
Means for sending the available channel information following validation of the device ID initially and to update the information when something changes
Means for periodic or on-demand contact verification signaling between the fixed/mode II device and the mode I device.
Ability to send channel data securely

## Slide 15: Ability to send data securely
“TV bands devices shall incorporate adequate security measures … This requirement includes implementing security for communications between Mode I personal portable devices and fixed or Mode II devices for purposes of providing lists of available channels.”
Use of higher layer security on internet side
Existing security mechanisms in the MAC meet this requirement
How security mechanisms are used (authentication sources, key management, etc) are outside the scope of 802.15.4 (and we really want to keep it that way!).
Supported by existing MAC features

## Slide 16: Contact Channel Requirement
“To initiate contact with a fixed or Mode II device, a Mode I device may transmit on an available channel used by the fixed or Mode II TVBD or on a channel the fixed or Mode II TVBD indicates is available “
Provides a way for a device with only a TVWS interface to operate
Receiving a valid 802.15.4 frame on a channel meets requirement , and the device may use the channel for making initial request
Beacon-enabled PAN:
  Presence of beacon on channel signals channel is “used by” the device that sent the beacon (i.e. valid contact channel
Non-beacon PAN
  Beacon (or other) frame transmission initiated by higher layer
  May be semi-periodic or semi-randomly transmitted
MLME-SCAN supports passive detection and active query/response
MCPS-Data supports Data and/or MP frame generation w/IEs

## Slide 17: Channel Data Source Info IE
Octets: 1 | 16 | 0/8 | 0/4 | 0/1 | Variable
Source Info | Location | Address of Known source | Channel Description for Known source | Number of Contact Channels | Channel Descriptions
Used to advertise availability of channel data source
Source Info subfields (bit fields):
  Indication that this device is a channel info source, and thus channel description fields are present
  Indication of known Channel Info source address field included
  Indication that known Source Channel descriptions field present
Location format per RFC 6225 (described on following slide)
Address of Other Source field is EUI-64 of another device known to have channel data
Channel Description for other source field contains the channel description for contacting the other source.
Number contact channels indicates how many Chanel Descriptions follow
Channel Descriptions format same as Channel Info IE (following slide)

## Slide 18: Device Identification and Channel Info Request IE
“A fixed or Mode II device may provide a Mode I device with a list of available channels only after it contacts its database, provides the database the FCC Identifier (FCC ID) of the Mode I device requesting available channels, and receives verification that the FCC ID is valid for operation“
Request contains the regulatory device ID for verification
Response includes channel info (ID valid) or failure status (ID not valid)
Initiated by higher layer
  Can use MLME-SCAN to do Active query/response with device ID and to receive channel data
  Can send data/MP frames with request IE and channel data IE

## Slide 19: Device Identification and Channel Info Request IE
Regulator Domain ID set to operating region
  Determines the size of the Device ID
Regulatory ID is ID assigned by regulatory agency, length varies by region:
  FCC ID is 14 octets
  Industry Canada is 11 octets
  Other domains may be different.
  Regulations will change after publication of the standard.
Manufacturer’s Device serial number
  Different length for each manufacturer
ID known by the higher layer or is implementation/vendor specific
A device may support multiple regulatory domains
Octets: 1 | Variable | 1 | Variable
Regulator Domain ID | Device ID | SN Length | Device Serial Num

## Slide 20: Channel Info Response IE
Response to channel information request, contains
Channel map ID
  Incremented when channel map updated
Regulatory region identification
  Unique value for each known regulatory region
Location where channel map is valid (next slide)
Number of channel descriptions
Status
  Access not allowed to request
  No channel list updates to the request
Channel Descriptions list, for each channel (next slide)
  Channel identification
  Maximum power level
  Valid time of channel
Octets: 1 | 1 | 8 | 1 | 1 | Variable
Channel Map ID | Regulator Region ID | Location | Number of Channels | Status | Channel Descriptions List

## Slide 21: Channel Info Response IE
Location Format (RFC 6225 format without Option Code and Option Length)
0:5 | 6:39 | 40:45 | 46:79 | 80:83 | 84:89 | 90:119 | 120:121 | 122:124 | 125: 127
Latitude Uncertainty | Lat | Longitude Uncertainty | Lon | Altitude Type | Altitude Uncertainty | Altitude | Version | Res | Datum
Chanel description:
Channel number according to 8.1.2 [as appropriate for the TVWS channel(s) available]
Maximum TX power in dBm (or fractions of dBm ?)
Valid time in minutes that channel is available (0 means “until further notice” or contact verification)
2 | 1 | 2
Channel ID | Maximum TX Power | Valid time

## Slide 22: Contact Verification Requirement
“At least once every 60 seconds, except when in sleep mode, i.e., a mode in which the device is inactive but is not powered-down, a Mode I device must either receive a contact verification signal from the Mode II or fixed device that provided its current list of available channels …“
Transmit channel map verification
  Periodic in beacons (security?)
  Data or MP frame at least every 60 seconds OR when device “awake” (like when scheduled wake-up in use)
  Other frames as they happen (such as when RIT or CSL used)
Channel map verification IE:
Octets: 1 | 1
Channel Map ID | Valid time
  Channel map ID of the currently valid Channel availability map
  Valid time set to duration that map is expected to remain valid

## Slide 23: Other possible information
Channel schedule
  Provide more detailed info on what channels will be available when
  Cover 24 hour period (per FCC)
  Could help ‘sleepy’ devices
  Note required to meet FCC requirements
Additional channel constraints
  Spectral mask or other limits beyond max power
  Might be required in some regions (not FCC)
  Could be a way to deal with changes in regulations

## Slide 24: Other Considerations
Allow for multiple radio devices
  multiple radio device that can use non TVWS radio to get to database
  might use the same data formats (multi-band 802.15.4 device)
  Might use IP end-to-end (802.11, 802.16, 3G/4G etc)

## Slide 25: Scenarios
Beacon PAN, PAN coordinator is channel data source
Beacon PAN, PAN coordinator is not source of channel data
Device not a PAN coordinator is a channel data source (beacon or non-beacon PAN, no PAN)
Peer-to-peer M2M where each device finds a channel data source independently

## Slide 26: Beacon PAN: PAN Coordinator is channel data source
Beaconing device has valid channel data
  Via direct or indirect connection to database
Advertises that it is a data source in beacons
  Presence of beacon means channel is OK for contact
  Includes Channel Data Source IE to identify itself as source
New devices use passive scan to find beacons
  Detection of beacon indicates can query on that channel
Use active scan:
  Include Device Identification and Channel Info Request IE in beacon request
  PAN coordinator includes Channel Info IE in response
  Can be secured as required

## Slide 27: Beacon PAN: PAN coordinator is not the Channel data source
PAN coordinator has acquired a valid channel to use from a data source
PAN coordinator transmits beacon
  May include Channel Data Source IE indicating NOT data source, and
  Identity of the device it sourced data (a known source)
Device looking for valid channel
  Uses passive scan to find beacon
  Decodes from beacon address of channel data source
  Contacts data source using provided channel info

## Slide 28: Device not a PAN coordinator as channel data source
Device not the PAN coordinator has access to the database
Device with channel information:
  Will respond to beacon request with Device Identification and Channel Info Request IE
  Responds with beacon with Channel Info IE
  May ad-hoc advertises by transmitting beacon frame with Contact IE to broadcast address (a periodic or periodic depending on application)
Device seeking channel information:
  Passive scan for beacons or listens for traffic on channel
  Initiates query/response for channel data on channel it hears in use (using active scan)
  Validates based on it’s position and data valid position

## Slide 29: M2M: Peer devices independently find source
Direct peer-to-peer communication without master (PAN coordinator) control
Each device finds channel data source
  Passive scan for device advertising channel data source
  Exchanges query/response to get data
  Repeats scan as needed to meet regulatory requirements
Each device can use active scan to find neighbors once activity is detected

## Slide 30: IE to support ranging measurement exchange

## Slide 31: Ranging Measurement
To initiate a range measurement, include range request IE in any MAC frame
Response used with data known to initiator:
  TX Timestamp (MCPS-Data.confirm)
  RX Timestamp (MCPS-Data.indication)
Note: Based on ranging described in 15.4 – 2011: Annex E

## Slide 32: Ranging Measurement IEs
Bits: 7 | 1
Range message sequence # | Ranging Method
Range Request IE: Included to request a ranging measurement
Range message sequence #: assigned upon transmission, used in response
Ranging Method: indicates one way ranging or two way ranging
Bits: 7 | 1 | 32
Range message sequence # | Ranging Method = 0 | Response TX-Timestamp
Range Response IE: Included in any frame (example, ACK) in response to request
Range message sequence #: in the initiating request
Ranging Method = 0: for one way ranging
TX-Timestamp: Time in responders time reference when response packet was transmitted
One Way Ranging

## Slide 33: Ranging Measurement IEs
Bits: 7 | 1 | 32 | 32
Range message sequence # | Ranging Method = 1 | Request RX Timestamp | Response TX Timestamp
Range Response IE: Included in any frame (example, ACK) in response to request
Range message sequence # in the initiating request
Ranging Method = 1: for two way ranging
RX Timestamp: the time, in the responding device time reference, that the request was received
TX Timestamp: Time in responders time reference when response packet was transmitted
Two Way Ranging

## Slide 34: Supplemental information

## Slide 35: Device to Database interface architecture

## Slide 36: Interface Protocol Framework
Application protocol that can be carried over secure HTTP
The protocol operation is assumed in the document and not mandated
  “While the details of adapting the White space application protocol to
  the above protocol stack may vary, following protocol operation steps
  are assumed in this document.”

## Slide 37: White Space Device (WSD) Initialization
Establishing initial connection to the database
  Exchange messages (help device to obtain security parameters)
  Authentication (performed at the application layer)
Field | Description
Protocol version | Version used for this exchange
Message type | INT-REQ
Authority | US, UK, others
Device Type | Fixed, Mode I or Mode II device
Device Identity | FCC ID – for US, Device serial no
Field | Description
Protocol version | Version used for this exchange
Message type | INT-RESP
Authority | US, UK, others
Result Code | Success, Failure
Authentication Info | Info used to initiate the authentication
INT-REQ
INT-RESP

## Slide 38: WSD Registration
Establishing operational parameters with the database
  Device Identity, Device Type, Device Location (Latitude, Longitude, Antenna height and characteristics), Device owner info
Field | Description
Protocol version | Version used for this exchange
Message type | REG-REQ
Authority | US, UK, others
Device Type | Fixed, Mode I or Mode II device
Device Identity | FCC ID – for US, Device serial no
Device Location | Latitude, Longitude, Antenna height and characteristics
Device Owner | Device owner and operator info and address
Authentication Code | Info that authenticates the ownership
Field | Description
Protocol version | Version used for this exchange
Message type | REG-RESP
Authority | US, UK, others
Sequence Number | Message sequence number
Result Code | Success, Failure
Authentication Info | Info used to initiate the authentication
REG-REQ
REG-RESP

## Slide 39: Database Query
Obtain available channel information
  Device sends its location (geo-location) with other parameters to the DB
  DB returns set of channels

## Slide 40: Database Query Message Parameters
Field | Description
Protocol version | Version used for this exchange
Message type | AVAIL-CHAN-REQ
Authority | US, UK, others
Device Type | Fixed, Mode I or Mode II device
Device Identity | FCC ID – for US, Device serial no
Device Location | Latitude, Longitude, Antenna height and characteristics
Authentication Code | Info that authenticates the ownership
Field | Description
Protocol version | Version used for this exchange
Message type | AVAIL-CHAN-RESP
Authority | US, UK, others
Sequence Number | Message sequence number
Result Code | Success, Failure
Available Channel | Channel info with availability, max power, freq range and time until the channel is available
Authentication Code | Info used to authenticates the ownership
AVAIL-CHAN-REQ
AVAIL-CHAN-RESP
In the notification message, the device sends sequence no and selected channel info in addition to the request message
  selected channel info includes channel number, max power limit, and frequency

## Slide 41: WSD Validation
Process by which WSDs can be validated
  By US FCC rule, “the TVWS Fixed or Mode II device provides service to a Mode I device only after the Mode I is validated by the TVWS database”
Field | Description
Protocol version | Version used for this exchange
Message type | DEV-VALID-REQ
Authority | US, UK, others
Device Type | Fixed, Mode I or Mode II device
Device Identity | FCC ID – for US, Device serial no
Device Location | Latitude, Longitude, Antenna height and characteristics
Device List | List of devices that require validation
Authentication Code | Info that authenticates the ownership
Field | Description
Protocol version | Version used for this exchange
Message type | DEV-VALID-RESP
Authority | US, UK, others
Sequence Number | Message sequence number
Result Code | Success, Failure
Device List | List of valid devices with device type, identity , manufacturer serial no.
Authentication Info | Info used to initiate the authentication
DEV-VALID-REQ
DEV-VALID-RESP

## Slide 42: One of the use cases considered
Master/ AP powers up and register with the trusted database
Master acquires available channels
Slave/ user device scans TV bands and associate with AP
Slave queries for a channel list (provide attributes defined by the regulations – include device ID, geo-location info)
Periodically repeat the process to request a channel list
Technology used between WS device and master – TDD air interface, WS air interface