## Slide 1
Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks(WPANs)
Submission Title: ETRI OFDM PHY Proposal for TG4m
Date Submitted: July 2012
Source: Cheol-ho Shin , Mi-Kyung Oh and Sangsung Choi (ETRI), Soo-Young Chang (SYCA)
Contact: chshin@etri.re.kr
Voice: +82 42 860 6831, E-Mail: chshin@etri.re.kr
Re: Call for proposals
Abstract: This contribution presents a proposal for the TG4m
Purpose: Final proposal to 802.15m
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Contents
Requirements overview
Dual PHY for TVWS WPAN
OFDM PHY for TVWS
Summary

## Slide 3: Requirements Overview
Key requirements for TVWS WPAN
  Operations in TVWS frequency bands under regulatory constraints
  Data rate of typically 40Kbps to 2Mbps & optionally 10Mbps
  Optimal & power efficient device command & control applications
  Operating range of at least 1Km
  At least 1000 direct neighboring devices
  Opportunistic coexistence with primary users (TV broadcasting): not interfere with other primary users

## Slide 4: Dual PHY for TVWS WPAN
PHY data rate in TG4m PAR
  Typically 40Kbps~2Mbps, optionally ~10Mbps
Various applications in TGD (doc.11-0684-12)
  Single PHY cannot cover all the applications.
  FSK PHY: Low data rate & low complexity PHY
  OFDM PHY: High data rate & high reliability PHY
Application | Candidate PHY
Smart Utility Networks | FSK
Infrastructure Monitoring Networks | FSK
Intelligent Transportation System | OFDM
Surveillance Control & Monitoring Networks | OFDM

## Slide 5: OFDM PHY for TVWS

## Slide 6: OFDM PHY for TVWS WPAN (1)
Reference modulator diagram

## Slide 7
Slide 7
July, 2009
Channel spacing : 1,25MHz, Guard band : 0.5MHz
Can use 4 TVBD Channels per 1 TV Channel
OFDM PHY for TVWS WPAN (2)
Channel plan for TVWS OFDM

## Slide 8: OFDM PHY for TVWS WPAN (3)
Timing-related parameter
Parameter | Description | Value
fs | Sampling frequency | 1250 KHz
NFFT | FFT Size | 128
∆f | Subcarrier frequency spacing | 1250/128 KHz
TFFT | IFFT and FFT period | 102.4 us
NCP | Number of samples in cyclic prefix | 32
TCP | Cyclic prefix duration in time | 25.6 us
NSYM | Total Number of samples per symbol | 160
TSYM | Symbol Duration | 128 us

## Slide 9: OFDM PHY for TVWS WPAN (4)
Parameter | TVWS OFDM (Mandatory)
Approximate signal bandwidth (KHz) | 1060
DFT Size | 128
Pilot tones | 8
Data tones | 100
MCS0 (kb/s) (BPSK rate ½)) | 390.625
MCS1 (kb/s) (QPSK rate ½) | 781.250
MCS2 (kb/s) (16-QAM rate ½) | 1562.5
Mandatory modes for TVWS OFDM

## Slide 10: OFDM PHY for TVWS WPAN (5)
Optional modes for TVWS OFDM
- Using 4x over-clock of TVWS OFDM
Parameter | TVWS OFDM (Optional)
Approximate signal bandwidth (KHz) | 4240
DFT Size | 128
Pilot tones | 8
Data tones | 100
MCS0 (kb/s) (BPSK rate ½)) | 1562.5
MCS1 (kb/s) (QPSK rate ½) | 3125
MCS2 (kb/s) (16-QAM rate ½) | 6250

## Slide 11: OFDM PHY for TVWS WPAN (6)
Parameter | PSD limit (100KHz) | TVWS OFDM (Mandatory) | TVWS OFDM (Optional)
Nominal bandwidth (KHz) |  | 1060 | 4240
Fixed | 12.6 dBm | 22.85 dBm | 28.87 dBm
Personal/portable (adj. channel) | -1.4 dBm | 8.85 dBm | 14.87 dBm
Sensing only | -0.4 dBm | 9.85 dBm | 15.87 dBm
All other Personal/portable | 2.6 dBm | 12.85 dBm | 18.87 dBm
Available TX maximum power defined by FCC 12-36

## Slide 12: OFDM PHY for TVWS WPAN (7)
Format of the OFDM PPDU
  SHR
    STF : The repetition cycle is the same as that of the TG4g OFDM Option 1
    - Formulas
    LTF and PHR: TBD

## Slide 13: OFDM PHY for TVWS WPAN (8)
Bit-to-symbol mapping
  same as TG4g SUN
Forward error correction (FEC)
  same as TG4g SUN
Interleaver
  same as TG4g SUN
  Ncbps is defined as follows;
  100 bits for BPSK, 200 bits for QPSK , 400 bits for 16-QAM

## Slide 14
128 IFFT
Total of 128 tones:
  100 data tones
  (constellation: BPSK/QPSK/16-QAM).
  - 8 pilot tones
  - Remaining 20 tones including DC are NULL tones.
Slide 14
July, 2009
OFDM PHY for TVWS WPAN (9)

## Slide 15: OFDM PHY for TVWS WPAN (10)
Cyclic prefix (CP)
  same as TG4g SUN
Structure of OFDM Symbol

## Slide 16: OFDM PHY for TVWS WPAN (11)
PPDU Tail Bit field (TAIL)
  same as TG4g SUN
Pad bits (PAD)
  same as TG4g SUN
Scrambler
  same as TG4g SUN

## Slide 17: Summary of OFDM PHY for TVWS
OFDM PHY
  Proposes the OFDM PHY based on the OFDM Option 1 of TG4g SUN to support the duel PHY
  Adds optional modes using 4x over-clock of TVWS OFDM to achieve the optional data rate of 10 Mbps, and these modes are very useful to track the position of TVBDs.