## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Comments to DCN385-02 TGD Draft]
Date Submitted: [10 September 2012]
Source: [Seung-Hoon Park, Kyungkyu Kim, Chiwoo Lim, Hyunseok Ryu, Daegyun Kim and Won-il Roh] Company [Samsung Electronics]
Address [416, Maetan-3Dong, Yeongtong-Gu, Suwon-Si, Gyeonggi-Do, 443-742, Korea]
Voice:[+82-10-9349-9845], FAX: [+82-31-279-0813], E-Mail:[shannon.park@samsung.com]
Re: [.]
Abstract: [Comments to revise TGD draft document (based on DCN385-02)]
Purpose: [To present comments to several discussion items in TGD draft document]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comments to DCN385-02 TGD Draft
September 10, 2012
Samsung

## Slide 3: Comments to 4.1 Concepts and architecture
Replace
“802.15.8 PAC shall support a fully distributed, decentralized, data scalable, and self organized system.”
to
“802.15.8 PAC shall support a fully distributed, decentralized, and self organized system. 802.15.8 PAC shall be data scalable.”

## Slide 4: Defining Fully Distributed Coordination
What is ‘fully distributed coordination’?
  fully distributed, decentralized, self-organized, scalable are different aspects of same thing

## Slide 5: Centralized System*①
Definition
  A single point of control for a group of systems
C
S1
S2
S3
S4
permanent control
(fixed hierarchies)

## Slide 6: (Just) Distributed System*①
Definition
  A collection of independent subsystems that appears to the application as a single coherent system
C
S1
S3
S4
S2
temporary control
(dynamic organization)

## Slide 7: Fully Distributed System*①
Definition
  A system consists of subsystems which of each has a control capability to the own subsystem and the local interactions
C
C
C
C
S1
S3
S4
S2

## Slide 8: Decentralized System
Definition
  a system found which function without an organized center or authority

## Slide 9: Self-Organization*①
Definition
  a process where some form of global order or coordination arises out of the local interactions between the components of an initially disordered system
C
S3
C
S5
C
S1
C
S4
C
S2
Local interactions (environment, neighborhood)
Local system control
Simple local behavior
C
S6

## Slide 10: Why “Fully Distributed”?
To support
  User-centric operation
    PD shall discover other PDs in the proximal range from itself, not from other delegates.
  Network scalability
    Group leader (,even though being temporary,) means hierarchy. Hierarchy means the limited range of network due to control overhead (reporting and commanding).
  Low complexity
    Hierarchical system (e.g. tree) needs a bunch of management overhead.

## Slide 11: Comments to 4.1 Concepts and architecture
Clarify
  Define “selective exchange of data”
“Possibly aided by higher layers, PD shall support selective exchange of data with specific other PDs or groups of PDs.”

## Slide 12: Comments to 4.1 Concepts and architecture
Add
  discovery for peer information without association (from PAR)
    The term ‘association’ was replaced by ‘peering’.
“IEEE 802.15.8 PAC shall provide discovery for peer information without peering. Peering is a function to establish single link or multiple links. Discovery without peering is beneficial by reducing redundant procedures to setup links and to exchange data among non-peer PDs. So discovery after peering shall be avoided in the efficiency aspect and novelty of 802.15.8.”

## Slide 13: Comments to 4.2 Components
Replace
  There is no hierarchy within PDs.
  However, a PD can take a specific role according to event (e.g. peering)
The title “Components” to “Roles”.

## Slide 14: Comments to 4.4 Services
Replace
Add
“802.15.8 PAC shall support a PD ability to:”
to
“802.15.8 PAC shall provide a discovery service that user or application aware peers in the proximity.
802.15.8 PAC shall support a PD discovery ability to:”
“802.15.8 PAC shall provide traffic services such as best effort, non real-time, real-time, streaming, gaming or etc.”

## Slide 15: Comments to 6.1 Synchronization
Add
  Link-level synchronization to Tx-Rx pair shall be provided for low power consumption.
“A transmitting PD and a receiving PD shall be synchronized to support low duty cycling.”

## Slide 16: Comments to 6.1 Synchronization
Add
  System-level synchronization shall be provided to get higher throughput from synchronous channel access mechanism than one from asynchronous channel access mechanism.
“A multiple of proximal PDs shall be synchronized for efficient channel access.”

## Slide 17: Synchronization and Channel Access
Throughput vs. offered load
  Pure Aloha : max throughput 0.184, at G = 0.5, Sp = 1/(2e)
  Slotted Aloha : max throughput 0.368, at G = 1, Ss = 1/e
0.5
2

## Slide 18: Comments to 6.2 Discovery (PD discovery or Peer discovery)
Replace
  The “Peer” information can include
    Application, service, user (nick)name
    PAC Device type, and capability
the title
“Discovery (PD discovery or Peer discovery)”
to
“Peer discovery”

## Slide 19: Comments to 6.3 Peering (Link establishment, or association)
Replace
the title
“Peering (Link establishment, or association)”
to
“Peering”

## Slide 20: Comments to 6.3 Peering (Link establishment, or association)
Replace
“802.15.8 PAC shall support a quick peering between PDs that have already discovered each other.”
to
“802.15.8 PAC shall support a quick peering between PDs that have already peered each other.”

## Slide 21: Comments to 6.9 Multi-hop support
Add
  Only users in the same peer group can support relaying.
  How selfish user helps relaying for different group users?
  So it shall be decided by peer information.
“Only relay-enabled PD decided by peer information shall relay discovery messages or traffic data from PDs in the proximity.”

## Slide 22: References
“Self-Organization in Autonomous Sensor/Actuator Networks”, Palko Dressler, http://www7.informatik.uni-erlangen.de/~dressler/
WSN MAC Protocols, http://www.etcs.ipfw.edu/~lin/ECET581_CS590/lectures/Lin_Lect_11_WSN_MAC%20Protocols.html