## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal to Include 5 MHz of DSRC Band (5.850-5.855 GHz) in 802.15.4p]
Date Submitted: [18 September 2012]
Source: [Ibrahim Muftic] Company [Parsons Brinckerhoff]
Address [303 2nd Street, Suite 700N, San Francisco, CA 94121 USA]
Voice:[Add phone number], FAX: [Add FAX number], E-Mail:[ibrahim.muftic@ieee.org]
Re: [If this is a proposed revision, cite the original document.]
Abstract: [In the US, the Dedicated Short Range Communications (DSRC) band is a good candidate to provide the necessary spectrum and appropriate protection for deployment of radio communication systems to support positive train control systems.
Purpose: [Proposal to include this band in the standard amendment]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Contents
Introduction
Proposal for 802.15.4p in DSRC Band
Rules and Rulemaking

## Slide 3: Introduction

## Slide 4: Introduction
Intelligent transportation systems should include advanced rail transit vehicles and systems
Rail transit systems need protected bandwidth for reliable communications for train control
In the US, the Dedicated Short Range Communications (DSRC) band is a good candidate to provide the necessary spectrum and appropriate protection

## Slide 5: Why DSRC Band?
Railroads have shallow vertical and horizontal curves; especially high-speed rail
Right-of-way clearance is carefully maintained
Line of sight of several km are practical
Easy installation of regular base stations along the right of way

## Slide 6: DSRCS - Channel Allocation
Ch. Number | Frequency range (MHz) | Max EIRP1 (dBm) | Channel Use
170 | 5850-5855 | -- | Reserved.
172 | 5855-5865 | 33 | Service Ch. 2
174 | 5865-5875 | 33 | Service Ch.
175 | 5875-5885 | 23 | Service Ch.3
176 | 5885-5895 | 33 | Service Ch.
178 | 5895-5905 | 33/44.8 | Control Ch.
180 | 5905-5885 | 23 | Service Ch
181 | 5895-5915 | 23 | Service Ch3
182 | 5905-5915 | 23 | Service Ch
184 | 5915-5925 | 33/40 | Service Ch4

## Slide 7: DSRCS - Channel Allocation Contd.
1. An RSU may employ an antenna with a height exceeding 8 m but not exceeding 15 m, provided the EIRP specified in the table above is reduced by a factor of 20 log(Ht/8) in dB where Ht is the height of the radiation center of the antenna in meters above the roadway bed surface. The EIRP is measured as the maximum EIRP toward the horizon or horizontal, whichever is greater, of the gain associated with the main or center of the transmission beam. The RSU antenna height shall not exceed 15 m above the roadway bed surface.
2. Channel 172 is designated for public safety applications involving safety of life and property.
Channel Nos. 174/176 may be combined to create a 20 MHz channel, designated Channel No. 175. Channels 180/182 may be combined to create a 20 MHz channel, designated Channel No. 181.
4. Channel 184 is designated for public safety applications involving safety of life and property. Only entities meeting the requirements of § 90.373(a) can operate on this channel.

## Slide 8: Proposal for 802.15.4p in DSRC Band

## Slide 9: Proposal
Use the bottom “reserved” 5 MHz of the current US FCC Part 95 DSRC band for wireless rail transit communications
Include in 802.11.4p.

## Slide 10: Typical Deployment
Two types of device
  Wayside Base Station (WBS)
  On-board Unit (OBU)
WBS transmits regular 802.15.4 beacon.
OBU hunts for beacons, uses beacon to maintain sync
Wayside Base Station (WBS) Antenna
On-Board Unit (OBU)
8 m (up to 15m) height above rail
Rail vehicle antenna 4-5 m above rail

## Slide 11: Base Stations
Transmit regular beacon with unique ID, track / signal status
Time slotted communications, same radio frequency but unique time slots per 802.15.4e

## Slide 12: Proposal: Channelization
For the reserved 5 MHz of spectrum, divide into channels with 100 kHz centers
49 channels total
First channel at 5850.1 MHz
Last channel center at 5854.9 MHz
Contiguous channels may be aggregated
Channels 1 and 49 are guard channels and may not be used.

## Slide 13: Channel Centers
Channel # | Channel Center Frequency
1 (guard channel) | 5850.1
2 | 5850.2
3 | 5850.3
4 | 5850.4
5 | 5850.5
6 | 5850.6
7 | 5850.7
8 | 5850.8
9 | 5850.9
10 | 5851.0
11 | 5851.1
12 | 5851.2
13 | 5851.3
14 | 5851.4
15 | 5851.5
16 | 5851.6
17 | 5851.7
18 | 5851.8
19 | 5851.9
20 | 5852.0
Channel # | Channel Center Frequency
21 | 5852.1
22 | 5852.2
23 | 5852.3
24 | 5852.4
25 | 5852.5
26 | 5852.6
27 | 5852.7
28 | 5852.8
29 | 5852.9
30 | 5853.0
31 | 5853.1
32 | 5853.2
33 | 5853.3
34 | 5853.4
35 | 5853.5
36 | 5853.6
37 | 5853.7
38 | 5853.8
39 | 5853.9
40 | 5854.0
Channel # | Channel Center Frequency
41 | 5854.1
42 | 5854.2
43 | 5854.3
44 | 5854.4
45 | 5854.5
46 | 5854.6
47 | 5854.7
48 | 5854.8
49 (guard channel) | 5854.9

## Slide 14: Frequency Control
All mobile devices to derive their operating frequency from base station reference
WBS frequency reference probably needs to be 0.1 PPM to maximize receiver performance

## Slide 15: Required Link Margin
Using Longley Rice ITS model, with antenna height vehicle at 5m and base station at 8 m (up to 15 m)
100 kHz bandwidth, 50 kbps, OQPSK modulation
+30 dBm at antenna, 10 dBi gain antenna, 4 dB noise figure, 10E-4 BER
Doppler is approximately 2 kHz
Typical WC fading at 20 dB
At 1 km, path loss including fade statistics is 117 dB, providing 21 dB margin over minimum required
802.15.4 already sufficient to support this link margin.

## Slide 16: Modulation Modes
All modulation modes currently supported or proposed for 802.15.4 shall be allowed subject to local regulatory requirements

## Slide 17: Rules and Rulemaking

## Slide 18: History of DSRC
In 1997, ITS America petitioned FCC to allocate 75 MHz of spectrum in the 5.9 GHz band for Intelligent Transportation Systems (ITS), in particular for the Dedicated Short Range Communications (DSRC).
The Transportation Equity Act for the 21st Century ("TEA-21") of 1998, directs FCC with DOT to consider spectrum needs for ITS (and DSRC)
In October 1999, FCC allocated the 5.9 GHz band for DSRC-based ITS applications and adopted basic technical rules for DSRC operations.
In December 2003, FCC adopted a Report and Order establishing licensing and service rules for the DSRC Service in the ITS Radio Service in the 5.850-5.925 GHz band.

## Slide 19: DSRCS - Introduction
Equipment in the DSRC Service comprises On-Board Units (OBUs) and Roadside Units (RSUs).
An OBU is a transceiver that is normally mounted in or on a vehicle. In some cases, it may be a portable unit.
Vehicle OBUs and portable units are licensed under Part 95 of the Rules.

## Slide 20: DSRCS – Introduction Contd.
An RSU is a transceiver mounted along a road or pedestrian passageway, or even on a vehicle which is stationary when operating.
An RSU broadcasts data to OBUs or exchanges data with OBUs in its communications zone. RSUs operate under Part 90 of the Rules.

## Slide 21: ASTM E2213–03 DSRC Standard/ IEEE 802.11p
Current Rule 90 requires: RUs operating in the DSRC band shall comply with the technical standard ASTM E2213–03, “Standard Specification for Telecommunications and Information Exchange Between Roadside and Vehicle Systems—5 GHz Band Dedicated Short Range Communications (DSRC) Medium Access Control (MAC) and Physical Layer (PHY) Specifications” published September 2003.
IEEE 802.11p, an amendment to the IEEE 802.11 standard, was approved in 2010. It adds wireless access in vehicular environments (WAVE). It defines enhancements to 802.11 to support ITS applications. This includes data exchange between high-speed vehicles and between the vehicles and the roadside infrastructure in the DSRC band.
IEEE 1609 is a higher layer standard based on the IEEE 802.11p.

## Slide 22: IEEE 802.11p
802.11p will be the basis for DSRC.
It will be a U.S. DOT project based on the ISO Communications, Air-interface, Long and Medium range (CALM) architecture standard, looking at vehicle-based communication networks, particularly for applications such as toll collection, vehicle safety services, and commerce transactions via cars.
The vision is a nationwide network that enables communications between vehicles and roadside access points or other vehicles. This work builds on its predecessor ASTM E2213-03.
Parts 90 and 95 need to be updated to include IEEE 802.11p. It may be an opportunity to include IEEE 802.15.4p as well.

## Slide 23: Licensing - Eligibility
The following entities are eligible to operate RSUs in the DSRC:
Any territory, possession, state, city, county, town or similar governmental entity
Any public safety or industrial/business entity meeting the eligibility requirements of CFR 90.33 or 90.35.

## Slide 24: Licensing – Co-Primary Users
There is also:
A co-primary Federal Government radiolocation allocation (for use by high-powered military services) in the 5.850-5.925 GHz band
A co-primary fixed satellite (earth-to-space) allocation
Amateur service has a secondary allocation in the band.
Industrial, Scientific and Medical (ISM) equipment can also operate in the 5.850-5.875 MHz portion of the band.

## Slide 25: Licensing – Numbers and Exclusivity
    FCC issues an unlimited number of non-exclusive geographic-area licenses to eligible entities authorizing operation on 70 MHz of co-primary spectrum, excluding the reserve channel.
    Governmental applicants will be issued a geographic area license based on the geo-political area encompassing the legal jurisdiction of the entity. All other applicants will be issued a geographic area license for their proposed area of operation.
    This spectrum is not subject to any aggregation limit, so each licensee uses channels in accordance with the ASTM-DSRC Standard.

## Slide 26: Licensing - Registration
Licensees must register RSU sites, channels, and other relevant data on the Universal Licensing System (ULS). ULS will refer RSU registrations through NTIA that are within 75 km of any existing Government radar sites listed in Section 90.371(b).

## Slide 27: Next Steps
Explore possibility of getting 5850-5855 MHz Reserve channel for exclusive PTC system deployment (possibly nation-wide)
Explore possibility of changing the rule to allow using IEEE 802.15.4p with different channelization and other parameters
Check industry support to supply products in this band ( 802.15.4 and others)

## Slide 28: References

## Slide 29: References
    (Jones, 2005) “DSRC - Linking the Vehicle and the Road”
    (FC, 2004) W. Fisher and B. Cash, “IEEE 802.11p Draft Review”
    (Weigle, 2008) “Standards: WAVE / DSRC / 802.11p”
    (Notor, 2011) “ITS Spectrum in the 5.9 GHz Band“
    http://www.fcc.gov/, September 2012