## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Merged MAC proposal summary
Date Submitted: [Sept 18 2012]
Source: See slide 2 for contributors list and affiliation
Company []
Address []
Voice: [+1.408.395.7207], FAX: [None],
E-Mail: [ben @ blindcreek.com]
Re: Support 4tv PHY development
Abstract: Summary of the combined MAC proposal for 802.15.4m
Purpose: Report progress of merging proposals and present to the task group
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Contributors
Name | Affiliation |  | Name | Affiliation
Chin-Sean Sum | NICT |  | Youngae Jeon | ETRI
Ming-Tuo Zhou | NICT |  | Sangjae Lee | ETRI
Zhou Lan | NICT |  | Sangsung Choi | ETRI
Fumihide Kojima | NICT |  | Soo-Young Chang | SYCA
Liru Lu | NICT |  | Kunal Shah | Silver Spring Networks
Funada Ryuhei | NICT |  |  | 
Hiroshi Harada | NICT |  |  | 
Benjamin Rolfe | BCA |  |  | 
This proposal represents the combined efforts of a many contributors!

## Slide 3: Progress Report
July 2012, San Diego
  4 MAC proposals presented
  Some overlapping functions with common goals and approachs
  Many unique features
  Task Group leadership asked proposers to collaborate and attempt to merge
  The challenge was accepted!
July, August, Sept 2012
  Collaboration via email circulation, teleconference
  Agreement on all areas overlapping functions
  Combination of all basic concepts and objectives
  Detailed outline of proposal draft circulated and many contributions received
  A lot of detailed technical work completed!
Sept 2012, Indian Wells
  A detailed proposal document created (doc #)
  Presentation of result to Task Group 4m
Detailed proposal document: 15-12-0512
https://mentor.ieee.org/802.15/dcn/12/15-12-0512-00-004m-tg4m-merged-mac-proposal.docx

## Slide 4: Overview of the proposal
Builds with existing MAC building blocks
TVWS channel enabling
  Information elements to enable TVWS specific information exchange to support TVWS channel access (topology independent)
Functional extensions to enhance low energy operation
Enhanced support for cluster-tree network topologies (TVWS Multichannel Cluster Tree PAN)
Extended support for direct device-to-device data transfer in beacon enabled PANs
  peer-to-peer (not through PAN coordinator)
  Support for multicast
Low Energy enhancements for TVWS operation
Support for dynamic band, channel and PHY operating parameter changes
Support for TVWS PHY capabilities exchange
Support for ranging (localization)
Support for general probe/response
Additions to MAC commands, MLME, MCPS to support additional functions

## Slide 5: General Approach
Use existing, extensible MAC mechanisms
  Information elements
    TVWS Channel Access Enabling
    PHY parameter change (adopted from 15.4j, 15.4k)
    TVWS Power saving mode support
    TVWS device capabilities exchange/advertisement
    Ranging support
    TMCTP superframe specification
  Use enhanced beacon and multipurpose frames (4e)
  New command frames
  New TVWS specific access procedures
  Extend base superframe for
    More flexible peer-to-peer communication, remove restrictions on GTS usage
    Support for multi channel cluster tree topology in TVWS
  Add to existing MAC SAP

## Slide 6: Enabling TVWS Channel Access

## Slide 7: Enabling TVWS Channel Access
Supports beacon PAN and non-beacon modes
Enables separation of PAN coordinator from channel availability data source roles and supports combing network control with data source
Supports scenarios for multiple regulatory domains
MLME IEs for TVWS enabling
  TVWS device identification
  TVWS device location IE
  TVWS channel information query request/response IE
  TVWS channel information source description IE
  Channel Timing Management IE
  Channel map verification

## Slide 8: Dynamic band, channel PHY parameter change
Use procedure, base IEs defined in 802.15.4j draft
  Coordinating with TG4j, TG4k
Beacon PAN – coordinator initiated switch
  Add notification IE to (enhanced) beacon
  Flexible control provided to NHL
Supports non-beacon PAN (ad-hoc)
  Use MP frame to propagate change notification
  Can be directed or broadcast
MLME IEs Dynamic band, channel and/or PHY parameter change
  PHY Parameter Change IE
  TVWS Power Saving IE
  Description of a specific TVWS PHY operating mode
  IE used to exchange TVWS PHY specific device capabilities

## Slide 9: TVWS Multichannel Cluster Tree PAN (TMCTP)
Extended cluster tree network
Supports clustering on multiple channels
Enables synchronous mult-hop, multi-level transfer between clusters
Super-PAN coordinator (SPC)
  Has TVWS database access (internet)
  Controls head of cluster tree
  Provides timing to child PAN coordinators on multiple/dedicated channel for each and synchronous transfer between clusters
Mult-channel support for clusters
  Reduces interference/collision between cluster PANs
  Extends effective network range
Provides for Control of latency

## Slide 10: TVWS Multichannel Cluster Tree PAN (TMCTP)
Based on existing (simple) superframe
Adds Beacon Only Period after CFP
  Dedicated Beacon Slot (DBS), composed of one more base slots in BOP
  Beacon scheduling between clusters
  DBS can have dedicated channel per cluster
Use enhanced beacon with TMCTP SF description IE

## Slide 11: TVWS Power Saving
Scalable and symmetrical power saving model
Initiating Device:
Transmits polling frames w/TVWSPS IE
Listens
Repeats until timeout or hears a response
Responding device:
Scheduled listening periods, can sleep in between
Responds with rendezvous time

## Slide 12: Direct Device to device
Support for neighbor discovery in PAN
  Request/response command frames
  MLME primitives
Supports multiple transfer methods:
  Direct transfer “push” data transfer
  Poll-mode to “pull” data transfer
  Broadcast mode transfer
  Multicast transfer

## Slide 13: Support for ranging
MLME IEs
IEs Support for ranging
  Ranging request IE
  Ranging response IE
Provides for initiation of ranging and exchange of ranging measurement
Supports ranging on data, multi-purpose or beacon frame transmission
Presence of Ranging Request IE triggers ranging data exchange
Works with proposed PHY mechanism to support ranging

## Slide 14: New command frames
DBS request
DBS response
Neighbor discovery request
Neighbor discovery response
Probe

## Slide 15: MLME
Add to existing primitives
  MLME-BEACON-NOTIFY (new parameters for TVWSLE)
  MLME-POLL (minor for direct neighbor poll)
  Primitives for ranging calibration (remove UWB from title)
New primitives
  TMCTP DBS allocation primitives
    MLME-DBS.request
    MLME-DBS.indication
    MLME-DBS.response
    MLME-DBS.confirm
  Neighbor Discovery
    MLME-NBR.confirm
    MLME-NBR.request

## Slide 16: MCPS
MCPS-DATA.request (add parameter to use ranging IE)
MCPS-DATA.indication (add parameters for TVWSLE)
MAC PIB attributes

## Slide 17: Informative Annex
Add TVWS ranging to existing ranging annex
Add new annex for TVWS operational recommendations