## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposed Text for Annex Q]
Date Submitted: [20 September, 2012]
Source: [Steve Jillings] Company [Semtech]
Address [200 Flynn Rd, Camarillo, CA, 91320]
Voice:[805-498-21111], E-Mail:[sjillings@semtech.com]
Re: []
Abstract: [Draft Text for Annex Q]
Purpose: [To assist with comment resolution for LB83]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Annex Q
The maximum PPDU size that a LECIM PHY shall be able to receive is 2047 octets. To facilitate the multi-year battery life operation expected for envisaged LECIM applications and given the low OTA chip rate provisioned by the PHY in terms of allowable spreading factor (215 chip per symbol for the DSSS PHY and 25 in the case of the FSK PHY) it is recommended that small PPDU frame sizes are used.
As an example, the on-air time for an un-fragmented 2047 octet frame at a symbol rate of 12.5 kb/s will require a minimum of 1.3 seconds total air time to be transmitted or received. If the same frame has a spreading factor of 8 applied to each symbol the over the OTA broadcast time will exceed 10 seconds.
This increase in transmission and reception time will have a significant impact upon the battery longevity of a LECIM device, even allowing for low duty cycle operation.
It should also be noted that the increased transmission time may lead to regulatory duty cycle limitations, especially for the case of network coordinator.