## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Views of PAC operation and requirements]
Date Submitted: [2 Oct., 2012]
Source: [Eldad Zeira]
Company: [InterDigital Communications LLC]
Address:
E-Mail: [Eldad.Zeira@InterDigital.com]
Re: [Discussion of 15.8 requirements]
Abstract: [This document presents operational constraints and derived potential requirements for the TGD]
Purpose: [To be discussed and adopted by 802.15.8 PAC]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PAC topology
Single device type (unlike e.g. 15.4 “controller” mode)
Any device could act as bridge to infrastructure but none has to
  Infrastructure access itself not specified by 802.15
Infrastructure availability: intermittent (in time) and sporadic (in devices)
  Smart phones are an example of ubiquitous access but ubiquity is not a general property of PAC deployments
Access enables security without necessity of provisioning in the field
Multi-hop relaying is required (and is a requirement)

## Slide 3: PAC interoperability
Many 802.15.4 amendments include multiple modes
Vendors select which mode(s) to implement
Deployment is often in “closed systems”: same coordinator for all end devices
Social use cases in 802.15.8-PAC imply that “universal interoperability” is desirable.
Important “side” benefit: Universal interoperability helps with infrastructure access

## Slide 4: PAC security and user’s identity
User’s Data:
  Confidentiality required for most applications
    E.g. at the level provided by cellular carriers
  Data integrity required for some applications (e.g. emergency notifications)
User’s identity:
  User’s ID defined in terms of an application (e.g. a game handle)
  Multiple (per application) identities possible
  Prevent disclosure of user’s application identity over the air or to 3’rd parties (other than the application provider)
  System must prevent impersonation

## Slide 5: How could it work?
PDs may be provisioned with shared secrets that allow them to form SOME level of connectivity, e.g. by group
  e.g. establish a secured relayed link to infrastructure
PDs attempt to connect to application server where a user can establish his or her identity
PDs obtain own as well as desired peer temporary ID’s for discovery
Identity information needs to be cryptographically secure
PDs also receive keys for data encryption, if needed
ID’s, keys etc. retained through absence of infrastructure (for some time)
ID is used for discovery

## Slide 6: Additional Requirements
All PDs shall support (at least one) common communication mode
The discovery identity (DID) of a PD is derived from higher layers
PD relaying groups could be provisioned
A PD could have multiple DID at the same time
PDs may be pre-configured with DID e.g. for the purpose of relaying
How to handle discovery and peering in the absence of higher layers DID is out of scope for 802.15.8-PAC (and could be provisioned and subject to user’s control)

## Slide 7: Thank You!