## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Views of the communication type, discovery and infrastructure
Date Submitted: November 05, 2012
Source: Jinyoung Chun, Suhwook Kim, HanGyu Cho
Company: LG Electronics
Address: jiny.chun@lge.com
Re: Consider the discovery procedure according to the applications
Abstract: We discuss the discovery procedure according to the applications
Purpose: Discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Overview
Communication type and discovery procedure
  PAC has lots of application matrix (15-12-0350-04-0008) and we can categorize it to several communication types.
  Then we can define the discovery procedures depending on the communication types.
View of Infrastructure-related issues
  We may need to get some information from infrastructure
  So I clarify what PAC does
    What information is used
    How PAC devices get the information

## Slide 3: Communication type and procedure
Type 1: One-way communication
  Applications: one-way advertisement, Emergency alert, etc
  Source device broadcasts it’s information to the vicinity devices. They don’t need to response to the source device.
Type 2: Anonymous group communication
  Applications: two-way communication with vicinity users such as personal selling, social gaming, etc.
  Source device finds anonymous vicinity devices to communicate with them. And they response with their information to the source device.
Type 3: Friend communication
  Applications: two-way communication with the known users
  Source device finds the known device(s) in the vicinity with it’s ID; e.g. device ID, application ID. And the target device(s) response to the source device.
Communication procedures can be different according to communication types.

## Slide 4
Communication type | Discovery (Device and Service) | Peering (link setup)
Broadcast communication | Find what: whole vicinity devices OR devices to allow advertisement services  May no need to discovery target devices. Find how: Active scanning (broadcast own information such as advertisement type, data formats, data region) | Broadcast without response (may) no need to setup a link between devices
Anonymous Group communication | Find what: devices with the same application group  Need to know the application. But there are thousands applications. So we may categorize them to several types. Find how: Passive scanning(?) OR Active scanning (broadcast own information such as application type, own application ID, data formats, data region and wait Response with vicinity’s application ID) | Make multiple unicast group(1:1 link) OR multicast group(1:n link)
Friend communication | Find what: devices with the pre-known ID  may keep the ID after communication type 2 Find how: Passive scanning OR active scanning (broadcast own information such as own application ID, target application ID, data formats, data region and wait Response with vicinity’s application ID) | Make multiple unicast group(1:1 link) OR multicast group(1:n link)

## Slide 5: Consideration points
Definitions
  What is Application type?
  : We can define application type by categorizing applications
  : e.g. emergency, advertisement, chatting, gaming, data sharing, navigation, etc.
  What is Application ID? : user unique ID + application
  : e.g. phone number /device MAC address + facebook/ navigation
Others
  In broadcast communication, how we can avoid interference with other links without discovery and link setup?

## Slide 6: View of Infrastructure-related issues
Necessity
  May need some information from high layers through infrastructure.
  For example, sync information(if we decide to support it), MAC address, application/service type, etc
Scope in this spec
  It has to be defined what information is used. But it’s premature to specify it in TGD.
  How PAC devices can get the information from infrastructure is out of scope.