## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [SFD Proposal for LECIM DSSS PHY]
Date Submitted: [Novemeber, 2012]
Source: [Xiang Wang1, Jie Shen1, Yang Yang1, Tao Xing1,2 ]
Company: [Wuxi SensingNet Industrialization Research Institute1 , SIMIT2]
Address [No.18, Zhenze Rd, Wuxi]
Voice:[+86-0510-81156888], FAX: [+86-0510-81156888]
E- Mail:[wilsonwangxiang@gmail.com]
Re: []
Abstract: [Resolution to Letter Ballot Comments]
Purpose: [To be considered TG4k]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comments
Comment 377
  SFD pattern should associate with preamble pattern, is SFD 0xE7 best for all preamble patterns? The SFD can be change according to preamble style, to enhance the performance

## Slide 3: Preamble and SFD in current Draft
19.1.1
The 2 and 4 octet preambles are as follows:
2 octet preamble = [0011 1111 0101 1001]
4 octet preamble = [1010 1010 1010 1010 1010 1010 1010 1011]
The SFD field, if present, indicates the beginning of the frame.
SFD = [1110 0111]

## Slide 4: Consideration
Keep SFD length as 1 octet
Different SFD pattern to each preamble pattern (2 octets and 4 octets)
Detect SFD pattern in receiver can be commissioned or changed according received preamble;
Good auto-correlation properties
• Low cross-correlation against preamble

## Slide 5: Proposed SFD to 2 octet preamble
SFD = [0,0,1,1,1,0,0,0]
abs(correlation value) | 0 | 2 | 4 | 6
Draft SFD | 12 | 9 | 10 | 1
Proposed SFD | 4 | 25 | 3 | 0

## Slide 6: Proposed SFD to 4 octet preamble
SFD = [1,0,0,0,0,1,0,0]
abs(correlation value) | 0 | 2 | 4
Draft SFD | 51 | 11 | 2
Proposed SFD | 51 | 13 | 0