## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: DSSS PHY Proposal for IEEE802.15.4N
Date Submitted: Jan 10, 2012
Source: Wei-Xia Zou, BUPT; Liang Li, Vinno; Guang-Long Du, BUPT ;
Suite 202, Building D, No.2 Xinxi Lu, Beijing, China,
Voice: 1-949-813-7909, FAX: 1-949-813-7909,
E-Mail: liangli@vinnotech.com
Abstract: Tech Proposal for TG4n(MBAN) Task Group
Purpose: Outline accomplishments from the March 2012 meeting and planned tasks for this meeting.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: General View
One PHY Definition and similar to sub-GHz ones in IEEE802.15.4C/4G
The designed Tx/Rx mainly applied for in-door hospital/clinic/senior house environment.
The Tx/Rx adopting this PHY may detect interference and switch to free band adaptively

## Slide 3: Proposal Definition
Data Rate: 250Kb/s and 500 Kb/s
Band Width: 2MHz
Operation Frequency Bands: 608-630MHz, 407-425MHz
  Fc=408 + 2k, k= 0, ….., 8
  Fc=609 + 2k, k= 0, ….., 10

## Slide 4: Bandwidth, Data Rate and Chip Rate
Chip rate is 1Mchip/s for 2MHz bandwidth.
Tow DSSS table, (16,4) and (8,4) for 250kbps and 500kbps.
The 16-ary symbol consists of 16 continues chips for (16,4) DSSS table and 8 continues chips for (8,4) DSSS table. (which are same to DSSS tables used in 15.4C and 15.4g)
The 16-ary symbol rate is 62.5ksym/s and 125ksym/s. Hence the data rate is log216×62.5=250kb/s and log216×125=500kb/s.

## Slide 5: Coefficient Summary
Frequency Band (MHz) | Bandwidth | Chip Rate (kchip/s) | Modulation | Symbols | DSSS table | Bit Rate (kb/s) | Symbol Rate (ksymbol/s)
407-425 | 2MHz | 1000 | QPSK | 16-ary | (16,4) | 250 | 62.5
 |  |  |  |  | (8,4) | 500 | 125
608-630 | 2MHz | 1000 | QPSK | 16-ary | (16,4) | 250 | 62.5
 |  |  |  |  | (8,4) | 500 | 125

## Slide 6: Modulation and Spreading Functions
Modulation and Spreading Functions
O-QPSK chip offsets

## Slide 7
Data Symbol (decimal) | Data Symbol (binary) (b0 b1 b2 b3) | Chip Values for (16,4) DSSS (c0 c1 … c14 c15) | Chip Values for (8,4) DSSS (c0 c1 … c6 c7)
0 | 0 0 0 0 | 0 0 1 1 1 1 1 0 0 0 1 0 0 1 0 1 | 0 0 0 0 0 0 0 1
1 | 1 0 0 0 | 0 1 0 0 1 1 1 1 1 0 0 0 1 0 0 1 | 1 1 0 1 0 0 0 0
2 | 0 1 0 0 | 0 1 0 1 0 0 1 1 1 1 1 0 0 0 1 0 | 0 1 1 0 1 0 0 0
3 | 1 1 0 0 | 1 0 0 1 0 1 0 0 1 1 1 1 1 0 0 0 | 1 0 1 1 1 0 0 1
4 | 0 0 1 0 | 0 0 1 0 0 1 0 1 0 0 1 1 1 1 1 0 | 1 1 1 0 0 1 0 1
5 | 1 0 1 0 | 1 0 0 0 1 0 0 1 0 1 0 0 1 1 1 1 | 0 0 1 1 0 1 0 0
6 | 0 1 1 0 | 1 1 1 0 0 0 1 0 0 1 0 1 0 0 1 1 | 1 0 0 0 1 1 0 0
7 | 1 1 1 0 | 1 1 1 1 1 0 0 0 1 0 0 1 0 1 0 0 | 0 1 0 1 1 1 0 1
8 | 0 0 0 1 | 0 1 1 0 1 0 1 1 0 1 1 1 0 0 0 0 | 1 0 1 0 0 0 1 0
9 | 1 0 0 1 | 0 0 0 1 1 0 1 0 1 1 0 1 1 1 0 0 | 0 1 1 1 0 0 1 1
10 | 0 1 0 1 | 0 0 0 0 0 1 1 0 1 0 1 1 0 1 1 1 | 1 1 0 0 1 0 1 1
11 | 1 1 0 1 | 1 1 0 0 0 0 0 1 1 0 1 0 1 1 0 1 | 0 0 0 1 1 0 1 0
12 | 0 0 1 1 | 0 1 1 1 0 0 0 0 0 1 1 0 1 0 1 1 | 0 1 0 0 0 1 1 0
13 | 1 0 1 1 | 1 1 0 1 1 1 0 0 0 0 0 1 1 0 1 0 | 1 0 0 1 0 1 1 1
14 | 0 1 1 1 | 1 0 1 1 0 1 1 1 0 0 0 0 0 1 1 0 | 0 0 1 0 1 1 1 1
15 | 1 1 1 1 | 1 0 1 0 1 1 0 1 1 1 0 0 0 0 0 1 | 1 1 1 1 1 1 1 0
Symbol-to-chip mapping for O-QPSK

## Slide 8: PHY-frame format
PHY frame format
PHR field format

## Slide 9: PHY frame generate diagram

## Slide 10: PSD Limitation
PSD Limitation among Channels.
Transmit center frequency tolerance is still ±40ppm.
Bandwidth | Frequency | Relative limit | Absolute limit
2MHz | ¦f-fc¦>1MHz | -20dB | -20dBm

## Slide 11: Pulse-Shape Filter
The raised cosine pulse shape with roll-off factor of r=0.8 is used to represent each baseband chip
This pulse shape filter is enough to meet the PSD and minimum receiver jamming resistance.
See the PSD figure in the next slide.
The future work is to confirm its ability to anti-TV and other inference

## Slide 12: PSD of TX-signal
PSD of transmission signal (Burg's estimation method.)
PSD limit
Same PSD for both (16,4)-DSSS signal and (8,4)-DSSS signal.

## Slide 13: Source Coding
FEC or other source coding may be necessary.
The further research is on the way

## Slide 14: Receiver Design
Receiver Sensitivity: <-85dBm for (16,4) DSSS table and <-82dBm for (8,4) DSSS table (with a noise figure of 10 dB and an implementation loss of 6 dB).
Minimum Receiver Jamming Resistance Requirement
Rx details on the way.
Adjacent channel rejection | Alternate channel rejection
0dB | 36dB

## Slide 15: Noise and Interference Models
Noise Model
  Flat-fading for 2MHz band channel both in 400MHz and 600MHz band;
  Noise model is AWGN channel model.
Interference Models
  CMMB (China Mobile Multimedia Broadcasting) is the mainly interference signal in the 608-630MHz band.
  The channel for CMMB signal is illustrated in following figure (3 channel in 606-630MHz)

## Slide 16: Noise and Interference Models
Interference Models
  Bandwidth for CMMB signal is 8MHz
  BPSK, QPSK and16QAM modulation, OFDM technology with 4096 sub-carrier (3076 been used)
  The math model is as the following equation:
  r(t)=x(t)+Am×[h*xC(t)]+n
r(t): received signal;
x(t): transmitted signal (after fading);
xC(t): CMMB interference signal in unit power;
Am: amplitude of CMMB interference signal;
h: low-path filter with 2MHz bandwidth;
n: the gauss noise.
*: denote convolution.
Right figure: Power Spectrum Density (PSD) of CMMB signal (in QPSK modulation scheme).

## Slide 17: Noise and Interference Models
Interference scenario
SIR calculation result with different distance between 4n devices
the 4n device is assumed in 19m high, or floor 5 ~ floor 6.
In the figure:
signal power: CMMB – 60dBm, 4n – 0dBm;
d1: distance between 4n transmitter and 4n receiver;
d2: distance between 4n devices and the CMMB base station;
hm: the height of 4n devices for ground;
hs: the height of CMMB base station;

## Slide 18: Simulation in Interference Environment
Simulation system model is as the following figure.
Cross-correlation demodulator have 16 correlator where each one denotes a modulated symbol.
Other coefficients:
CMMB modulation scheme: QPSK
Frame length: 256 byte;
Carrier frequency offset: random variable between ±40ppm.
Matched filter order: 10-order fir filter;
Roll-off factor: 0.8;
Correlator length in demodulator: 16.

## Slide 19: Simulation in Interference Environment
The PER vs. SNR simulation result is illustrated in the right figure.
(16,4) means when (16,4) DSSS table has been used (250kbps);
(8,4) means when (8,4) DSSS table has been used (500kbps).

## Slide 20: Simulation in Interference Environment
The interference math model is as:
IC=Am×[h*xC(t)]
So the interference power is estimated as
Picmmb=1kW×f(d)×Br≈1kW×d-2×0.25=54-20log10(d) dBm
Where
f(d) ≈d-2 is path loss factor, and d is the distance to CMMB base station (m);
Br=2MHz/8MHz=0.25 is relatively bandwidth factor;
So the amplitude of interference signal is
Am=Picmmb1/2

## Slide 21: Simulation in Interference Environment
The following figures illustrates PER vs SNR in constant interference signals (SIR).
(16,4) DSSS table (250kbps)
(8,4) DSSS table (500kbps)

## Slide 22: Transmission Model in Hospital Environment
The path-loss model is:
L=La+Lb
Here, La is free space path loss
La=32.45+20logf+10γlogd , (dB)
where γ is channel fading parameter, in the equation, γ=2.0;
And, Lb is penetration loss
Lb=nLp+N1L1+N2L2, (dB)
where :
Lp : penetration loss of human body;
L1 : penetration loss of concrete wall;
L2 : penetration loss of wooden door.
and n, N1, N2 is the number of human body, concrete wall and wooden door correspondingly.

## Slide 23: Transmission Model in Hospital Environment
The parameters Lp, L1, L2 is listed in the following table.
 | Lp | L1 (with thickness of 200mm) | L2 (with thickness of 42mm)
410MHz | 14dB | 10dB | 3dB
610MHz | 13.5dB | 9dB | 2.3dB
Path loss of 400MHz and 600MHz band
  Right figure: Path loss in 400MHz and 600MHz band.
  NLOS: Path loss after penetrate 1 concrete wall and 1 people

## Slide 24: Simulation in Hospital Environment
The PER simulation result is illustrated in the right figure.
TBD

## Slide 25: Conclusion
This proposal includes one dual-data rate PHY structure.
Introduce the major interference CMBB model
Initial Simulation of PER vs SNR + CMBB interference
Introduce the path models in hospital environment
More Simulation are on the way.