## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Technical proposal for wearable 15.4n device
Date Submitted: November 8, 2012
Source:
Kenichi Mori (individual), Hirokazu Tanaka (individual), Shinsuke Hara (QOL-SN)
ken1.morius@gmail.com, hi.tanaka@m.ieice.org, shinsukehara0122@gmail.com
Kaoru Yokoo (Individual)
kaoru.yokoo.ieee@gmail.com
Abstract: Technical proposal for wearable 15.4n device
Purpose: Lower power consumption modulation scheme and needed interface to connect with already installed in hospitals and clinics.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Key points for 15.4n devices
Based on the previous discussion on applications [1] and Chinese regulation [2], the following features are demanded for some healthcare applications
Usage in hospitals and clinics (especially for patients)
Low-cost
Wearable
Low mutual interference among devices
Easy communication with already existing healthcare instruments

## Slide 3: Technical requirements
Followings have to be considered to actualize demands written in the previous slide
We have to prepare as many channels as we can to support patients in the same area and timing
Simpler circuit, cheaper device can be actualized
Battery operation is needed Lower power consumption is preferable
Side lobe must be filtered sharply
Frequency agility is needed to avoid interference from/to legacy systems

## Slide 4: Technical proposal
Modulation schemes with constant envelope Filtered FSK - Simpler circuit (PLL modulation and non-linear PA can be used) - Lower power operation Note: FSK and OQPSK are also a modulation scheme with constant envelope but side lobes are not filtered sharply
Support IEEE11073 [3]

## Slide 5: Spectrum comparison (example)
Common parameters
Data rate = 200 kbps
Modulation index = 0.5
Parameter only for Filtered FSK; Gaussian filtered, BT=0.5
Red colored line; FSK
Black colored line; OQPSK
Blue colored line; Filtered FSK
Filtered FSK has much better side lobe attenuation than other two
PSD [dB]
Frequency [Hz]

## Slide 6: Summary
Filtered FSK and/or O-QPSK are preferable for wearable devices used for some healthcare applications in hospitals and clinics Filter type for filtered FSK is TBD
IEEE11703 should be supported to communicate with already installed healthcare instruments in hospitals and clinics
Band plan is TBD

## Slide 7: References
[1] 12/0539r0
[2] 12/0105r0
[3] 12/0413r0/004j

## Slide 8
Annex

## Slide 9
Frequency Band [MHz] (BW) | Modulation | Bit Rate [kb/s] | Channel Spacing [kHz] | Number of Channels
174 – 216 (42MHz) | Filtered FSK | 200 | 400 | 105
407-425 (18MHz) | Filtered FSK | 200 | 400 | 45
608-630 (22MHz) | Filtered FSK | 200 | 400 | 55
One example
In a case without considering channel overlapping