## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Conceptual proposal of autonomously distributed wireless system based on dynamic multi-layer control for fair satisfaction of QoE]
Date Submitted: [12 November, 2012]
Source: [Masahiro Uno] Company [ATR ]
Address [2-2-2 Hikaridai Seika, Kyoto 619-0288 Japan]
Voice:[+81-774-95-1511], FAX: [+81-774-95-1508], E-Mail:[uno@atr.jp]
Re: []
Abstract: [This presentation proposed new concept of a dynamic radio resource controlled wireless system based on Quality of Experience (QoE) targeting for medical and disaster situations. ]
Purpose: [For discussion.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Conceptual proposal of autonomously distributed wireless system based on dynamic multi-layer control for fair satisfaction of QoE
Authors:

## Slide 3: Motivation
Self Organized Wireless System for Medical and Disaster situations
  Public protection and disaster relief (PPDR)
  For Efficient medical works (Kyoto Univ. Hospital & ATR)
Various Applications with Easy-to-Setup, Enough Quality
  from Text to Video under limited radio resources
  Dynamic Resource Assignment / Topology control based on Quality of Experience (QoE) of all users

## Slide 4: Use Case of Medical / Disaster Situation
Rescue
Medical Treatment
Cross-border operation
interoperability
interoperability
sensors
Comm. tools
sensors
Self-Organized
Network
Information gathering
& distribution

## Slide 5: Kyoto University Hospital
Founded in 1901
Over 30 department (internal medicine, surgical, obstetrics, pediatrics, ophthalmologic, etc.)
2,700 medical workers and 2,600 patients/day
Research & practice of advanced medical care (organ transplantation, iPS cells, etc.)
Huge wireless medical information system throughout a hospital is employed
Notes: ・32,000 patients/year
・アニュアルレポートより引用 http://www.kuhp.kyoto-u.ac.jp/~annual/H22/siryou/ichinichi.pdf

## Slide 6: Medical information system in hospital
BT-ID
(for location)
BT-AP (for data exchange)
DB
Electronic medical record
Bluetooth AP network connected with WiFi
Laptop PC for nurses
WiFi (IEEE 802.11b/g)
Nurse
Bluetooth Barcode Reader
Patient
Medicine
WiFi AP

## Slide 7: Medical information system in the hospital
Medical device network
system (experimental)
WiFi WLAN system
Outpatients navigation
system
Prescription check system
650 WiFi access points
1,500 Bluetooth barcode readers
600 Bluetooth access points (BT-AP)
1,100 Bluetooth identification beacon
(BT-ID)
2,700 Bluetooth navigation tablets
1,000 Laptop PC
Database
Medical devices
Notes: medical thermometer

## Slide 8: Problems in actual operation
Nurses complain about...
Connectivity of their Laptop PCs by WiFi, especially around 8 A.M.
Service coverage at certain places (for example, behind a large pillar).
These would come from...
Interference between devices operated in the same 2.4 GHz ISM band. Not only hospital equipment (microwave ovens, etc.), but also private devices (mobile routers, portable game machines, etc.) are used.
Blind area due to unsuitable placement for access points (behind some objects, etc.).
Notes: morning medical check
*After switching WiFi operation from IEEE 802.11g (2.4 GHz) to 802.11n (5 GHz), connectivity might have been improved somehow.

## Slide 9: Measurement detail
70 m
30 m
6 m
7 m
BT-AP
BT-ID
Microwave oven
WiFi AP

## Slide 10: Measurement results: WiFi
2400 2410 2420 2430 2440 2450 2460 2470 2480 2490
Frequency [MHz]
50 ms
Hospital WiFi service is provided on channel 1, 6, and 11
Other private devices operated on other channels would cause interference to existing WiFi devices.
Notes: ks8f1000_2012.03.02.10.09.25.546.png

## Slide 11: Measurement results: WiFi and Bluetooth
2400 2410 2420 2430 2440 2450 2460 2470 2480 2490
Frequency [MHz]
10 ms
-50
-55
-60
-65
-70
-75
-80
-85
-90
Power Spectrum Density [dBm]
WiFi and Bluetooth packets would cause collisions

## Slide 12: Measurement Results: Microwave Oven
2400 2410 2420 2430 2440 2450 2460 2470 2480 2490
Frequency [MHz]
50 ms
-80
-85
-90
-95
-100
Power Spectrum Density [dBm]
Noise from microwave oven is measured
Nearby wireless devices would not be able to communicate when microwave oven is being operated

## Slide 13: Problems and Solutions Proposed
From the measurement results:
It’s hard to build and operate large scale wireless networks of autonomously operated devices.
These networks need to be self-organized and dynamically reconfigurable in the real situation (huge disaster time, etc.).
Solutions proposed
Self-organized wireless system for flexible and maintenance-free utilization in medical and disaster area
Spectrum sensing of whole band for searching vacant radio resources
Radio resource assignment and network topology management controlling bandwidth and interference between wireless systems based on quality of experience (QoE) of each applications

## Slide 14: Concept of our Proposed System
The parameters of QoE f(x): data rate, latency, BER,
priority, subjective assessment (i.e., mean opinion score)
Shares limited Radio Resources with Various Applications
Controls dynamically based on QoE

## Slide 15: Concept of system
antenna control
Other System
resource assign
QoE
estimation
QoE
estimation
network reconfiguration
sensing environment
topology optimization
Proposed System
resource assign