## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposed Resolution to CID 371 about phyMaxFrameDuration]
Date Submitted: [November, 2012]
Source: [Xiang Wang1, Jie Shen1, Yang Yang1, Heqing Huang1, Tao Xing1,2 ]
Company: [Wuxi SensingNet Industrialization Research Institute1 , SIMIT2]
Address [No.18, Zhenze Rd, Wuxi]
Voice:[+86-0510-81156888], FAX: [+86-0510-81156888]
E- Mail:[wilsonwangxiang@gmail.com]
Re: []
Abstract: [Resolution to Letter Ballot Comments]
Purpose: [To be considered TG4k]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comments
Comment 377
  Wrong equation, eg. miss SFD duration, phyLECIMDSSSPSDUSize shoud multipe with phyLECIMDSSSPSDUSpreadingFactor not phyLECIMDSSSSHRSpeadingFactor, phyLECIMDSSSSHRSpreadingFactor is already 2^X-1 value
Proposed Change
  Correct it.

## Slide 3: Text in current Draft
For the LECIM DSSS PHY, the attribute phyMaxFrameDuration is given by:
phyMaxFrameDuration =
[(phyLECIMDSSSPreambleSize *phyLECIMDSSSPreambleRepetition)+ K +
phyLECIMDSSSPSDUSize *8 *2phyLECIMDSSSSHRSpreadingFactor)]* 
(phyLECIMDSSSPPDUModulation*1000)

## Slide 4: Change
phyMaxFrameDuration =
[(phyLECIMDSSSPreambleSize*phyLECIMDSSSPreambleRepetition+M)*
phyLECIMDSSSSHRSpreadingFactor+
phyLECIMDSSSPSDUSize *2*8 * phyLECIMDSSSPSDUSpreadingFactor]*
1000*(N+1)
M means SFD length in bits,
if phyLECIMDSSSSFDPresent = True, M =8; else, M = 0;
N changes according phyLECIMDSSSPPDUModulation,
if phyLECIMDSSSPPDUModulation= O-QPSK, N=1; else, N=0;

## Slide 5: Problem
For Std15.4, a superframe duration is defined as BI, and
BI = aBaseSuperframeDuration*2macBeaconOrder
aBaseSuperframeDuration = aBaseSlotDuration*aNumSuperframeSlots = 60*16
0=<macBeaconOrder<=14
Which means
BI <= 60*16*2^14
and for current phyMaxFrameDuration, if phyLECIMDSSSPreambleSize = 32,

## Slide 6: Problem
For current phyMaxFrameDuration,
eg.
phyLECIMDSSSPreambleSize = 32, phyLECIMDSSSPreambleRepetition = 8,
phyLECIMDSSSSFDPresent = True, phyLECIMDSSSSHRSpreadingFactor =2^16-1,
phyLECIMDSSSPSDUSize = 32, phyLECIMDSSSPSDUSpreadingFactor= 2^14-1 and
phyLECIMDSSSPPDUModulation = BPSK
phyMaxFrameDuration = 2.5689336*10^10, much larger than BI, make it uncompatible.

## Slide 7: Proposed Resolution
For the LECIM DSSS PHY, the symbol rate is defined as the bit rate of the SHR.
phyMaxFrameDuration = phySHRDuration + phyPSDUDuration;
phySHRDuration = phyLECIMDSSSPreambleSize*phyLECIMDSSSPreambleRepetition+M;
M means SFD length in bits,
if phyLECIMDSSSSFDPresent = True, M =8; else, M = 0;
phyPSDUDuration = ceiling(phyLECIMDSSSPSDUSize *2*8 * phyLECIMDSSSPSDUSpreadingFactor/phyLECIMDSSSSHRSpreadingFactor);