## Slide 1
Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks(WPANs)
Submission Title: Solutions proposed for TBDs of the Merged TVWS-OFDM PHY
Date Submitted: November 2012
Source: Cheol-ho Shin , Byoung Hak kim, Seung Sik Lee and Sangsung Choi (ETRI), Soo-Young Chang (SYCA)
Contact: chshin@etri.re.kr
Voice: +82 42 860 6831, E-Mail: chshin@etri.re.kr
Re: Call for proposals
Abstract: This presentation provides solutions proposed for TBDs of the Merged TVWS-OFDM PHY.
Purpose: To propose solutions for TBDs of the Merged TVWS-OFDM PHY
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Contents
TBDs of TVWS-OFDM PHY
Solution proposed for frequency domain LTF
Solution proposed for STF power boosting
Baseband waveform of TVWS-OFDM packet
Conclusion

## Slide 3: TBDs of TVWS-OFDM PHY
STF power boosting (20.2.1.1.4)
  Power boosting shall be applied to the STF OFDM symbols in order to aid preamble detection, The boost should be a multiplication by TBD, which is approximately TBD dB.
Frequency domain LTF (20.2.1.2.1)
  Table 136 shows the frequency domain representation of the LTF.
  Table 136 (TBD).

## Slide 4: Solution proposed for frequency domain LTF
Slide 4
Frequency domain LTF
Tone #: -64 -33 Value : 0 0 0 0 0 0 0 0 0 0 1 1 -1 1 -1 1 1 1 1 1 -1 -1 -1 1 1 -1 1 -1 1 1 1 1
Tone #: -32 -1 Value: 1 1 -1 -1 1 1 -1 1 -1 1 -1 -1 -1 -1 -1 1 1 -1 -1 1 -1 1 -1 1 1 1 -1 -1 -1 -1 1 -1
Tone #: 0 31 Value: 0 -1 -1 1 1 -1 1 1 -1 -1 1 1 -1 1 -1 -1 1 1 1 1 1 -1 -1 1 1 -1 1 -1 1 1 1 -1
Tone #: 32 63 Value: 1 1 -1 -1 1 1 -1 1 -1 1 -1 -1 -1 -1 -1 1 1 -1 -1 1 -1 1 -1 0 0 0 0 0 0 0 0 0

## Slide 5: Solution proposed for STF power boosting
Slide 5
STF power boosting
  Propose the STF power boosting of 2.

## Slide 6: Baseband waveform of TVWS-OFDM packet
Slide 6
Number of OFDM Symbols:
- OFDM symbol is composed of 160
samples
- STF: 1 – 4, 2 in this figure and
STF power boosting of 2 is
assumed
- LTF: 2
- PLCP header: 1
- Payload: Variable
with proposed solutions

## Slide 7: Conclusion
Slide 7
Solutions proposed for TBDs of the Merged TVWS-OFDM PHY
  The STF power boosting of 2
  Frequency domain LTF
Peak magnitudes and mean powers among STF, LTF and payload compared, considering the proposed solutions.
- If the STF power boosting of 1.5 is assumed, the mean power of STF is 0.8438
The results in the above table show the proposed solutions are suitable for a design of TVWS-OFDM PHY.
 | Peak magnitude |  | Mean power
 | real | image | 
STF | 1.5517 | 1.5517 | 1.5000
LTF | 1.5102 | 1.4726 | 0.8457
Payload | 4.2426 (Theoretically, 11.3) | 2.6553 (Theoretically, 11.3) | 0.8441