## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: TG4m OFDM PHY Updates for ranging
Date Submitted: November 11, 2012
Source: Soo-Young Chang (SYCA) and Mi-Kyung Oh (ETRI)
Voice: +1 530 574 2741, E-mail: sychang@ecs.csus.edu
Re: [802.15 TG4m]
Abstract: Merged TG4m OFDM PHY was submitted in September 2012. This document is to provide updates for an issue raised in ranging area.
Purpose: To update the 802.15 TG4m group regarding merged TG4m OFDM PHY
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: TG4m OFDM PHY Updates for Ranging
Soo-Young Chang and Mi-Kyung Oh

## Slide 3: ONE ISSUE FOR RANGING (1)
20.2.1.3 PHR  Insert ranging bit in PHR
Figure 118 is to be replaced by the following table.
* 15-12-0575-00-004m-preliminary-draft-for-tg4m
Figure 118—PHY header fields for TVWS-OFDM
Bit string index | 0-4 | 5 | 6-7 | 8-18 | 19-27 | 28-43 | 44-49
Bit mapping | R4-R0 | RNG | RA1-RA0 | L10-L0 | S8-S0 | H15-H0 | T5-T0
Field name | Reserved | Ranging | Rate | Frame length | Scrambling seed | HCS | Tail

## Slide 4: ONE ISSUE FOR RANGING (1)
20.2.1.3 PHR (continued) Insert ranging bit in PHR
At the third paragraph in 20.2.1.3, insert the following text. "The Ranging (RNG) field is set to indicate that this particular frame is intended for ranging." as follows:
“The PHR occupies one OFDM symbol. The PHR shall be transmitted using the lowest supported modulation and coding scheme (MCS) level, as described in Table 137. It is sent to the convolutional encoder starting from the leftmost bit in Figure 131 to the rightmost bit.
The Ranging (RNG) field is set to indicate that this particular frame is intended for ranging.
The Rate field (RA1-RA0) specifies the data rate of the payload and is equal to the numerical value of the MCS for the mandatory mode and the numerical value of the MCS minus three for the optional 4 times overclock modes, as described in 20.2.2, expressed in binary format. The list of data rates for TVWS-OFDM can be found in 20.2.2.”
* 15-12-0575-00-004m-preliminary-draft-for-tg4m

## Slide 5: SUMMARY
One issue for ranging bit
  This ranging issue already discussed in September 2012.
  Recommended modification is suggested in this document per discussion/agreement in September 2012 meeting.
All the issues can be cleared in TG4m OFDM PHY area if suggestions/recommendations in this document and another document, doc. 15-12-0620-00, are accepted.