## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed solutions for TBDs of ETRI MAC Proposal in TG4m Draft 575r0
Date Submitted: November, 2012
Source: Youngae Jeon, Sangjae Lee, and Sangsung Choi (ETRI), Soo-Young Chang (SYCA)
Contact: yajeon@etri.re.kr
Voice: +82 42 860 6497, E-Mail: yajeon@etri.re.kr
Re: [802.15 TG4m]
Abstract: This document provides proposed solutions for TBDs of ETRI MAC Proposal in TG4m Draft 575r0.
Purpose: To resolve TBDs for TG4m Draft 575r0
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: TMCTP related clauses which contain TBDs in P802.15.4m/D0
4.5.1 Superframe Structure (p6) – 1TBD
5.1.14 Starting and maintaining TVWS Multichannel Cluster Tree PANs (TMCTP) (p16) – 2TBDs
5.3.14 DBS request command frame (p35) – 1TBD
5.3.15 DBS response command frame (p35) – 1TBD
6.2.23.1 MLME-DBS.request (p46) – 1TBD
6.2.23.2 MLME-DBS.indication (p47) – 1TBD
6.2.23.3 MLME-DBS.response (p48) – 2TBDs
6.2.23.4 MLME-DBS.confirm (p49) – 1TBD
* 15-12-0575-00-004m-preliminary-draft-for-tg4m

## Slide 3: 4.5.1 Superframe Structure (p6) (before)
4.5.1.1 Superframe Usage for TVWS
4.5.1.5.1 TVWS Multichannel Cluster Tree PAN (TMCTP) Superframe
  This standard allows ~~~ can be found in 5.1.1.1a.
4.5.1.5.2 Generalized GTS Usage
  In a TVWS PAN allocated GTS may be configured for direct peer-to-peer communication. When a frame is transmitted in a GTS with a valid destination address, implicit addressing based on the GTS direction parameter is not used.
  Add overview paragraph for GTS features to support TVWS operation

## Slide 4: 4.5.1 Superframe Structure (p6) (after)
4.5.1.1 Superframe Usage for TVWS
4.5.1.5 TVWS Multichannel Cluster Tree PAN (TMCTP) Superframe
  This standard allows ~~~ can be found in 5.1.1.1a.
4.5.1.5.2 Generalized GTS Usage
  In a TVWS PAN allocated GTS may be configured for direct peer-to-peer communication. When a frame is transmitted in a GTS with a valid destination address, implicit addressing based on the GTS direction parameter is not used.
  Add overiew paragraph for GTS features to support TVWS operation
Discussion
  Additional GTS description is unnecessary. Since TMCTP adds only BOP in basic superframe structure, there is no change to GTS.

## Slide 5: 5.1.14 Starting and maintaining TVWS Multichannel Cluster Tree PANs (TMCTP) (p16) (before)
In step B the SPC transmits an enhanced beacon containing a TMCTP Extended Superframe Specificiation IE (xref). Upon successful reception of the beacon from the SPC, the child PAN coordinator may request a DBS allocation sending a DBS request (xref) to the SPC. Upon receiving the DBS request, the SPC will allocate a DBS slot and channel, and generate a DBS response to report the slot and channel allocated (the request is successful in this example).

## Slide 6: 5.1.14 Starting and maintaining TVWS Multichannel Cluster Tree PANs (TMCTP) (p16) (after)
In step B the SPC transmits an enhanced beacon containing a TMCTP Extended Superframe Specificiation IE (5.2.4.35). Upon successful reception of the beacon from the SPC, the child PAN coordinator may request a DBS allocation sending a DBS request (5.1.14) to the SPC. Upon receiving the DBS request, the SPC will allocate a DBS slot and channel, and generate a DBS response (5.1.15) to report the slot and channel allocated (the request is successful in this example).

## Slide 7: 5.3.14 DBS request command frame (p35)
5.3.14.1 MHR Fields (before)
  (TBD)
5.3.14.1 MHR Fields (after)
  Destination Addressing Mode field and Source Addressing Mode field shall be set to indicate short addressing.
  Frame Pending field shall set to zero, and AR field shall set to one. Frame Version field shall set to (TBD).
  Destination PAN Identifier field shall contain the value of macPANId. Destination Address field shall contain the address from the beacon frame that was transmitted by the coordinator to which the DBS request command is being sent. Source PAN Identifier field shall contain the value of macPANId Source Address field shall contain the value of macShortAddress.

## Slide 8: 5.3.15 DBS response command frame (p35)
5.3.15.1 MHR Fields (before)
  (TBD)
5.3.15.1 MHR Fields (after)
  Destination Addressing Mode field and Source Addressing Mode field shall be set to indicate short addressing.
  Frame Pending field shall set to zero, and AR field shall set to one. Frame Version field shall set to (TBD).
  The Destination PAN Identifier field shall contain the value of macPANId. The Destination Address field shall contain the short address of the device requesting. The Source PAN Identifier field shall contain the value of macPANId. Source Address field shall contain the value of macShortAddress.

## Slide 9: 6.2.23.1 MLME-DBS.request (p46) Table 14—MLME-DBS.request Parameters (before)
Name | Type | Valid range | Description
RequesterCoordAddr | Device Short address | 0x0000‐0xffff | The short device address of the (original) source requester PAN coordinator.
RequestType | Enumeration | ALLOCATION, DEALLOCATION | If the request is for allo‐cation or deallocation of TMCTP DBS.
DBSLength | Integer | See [xref] | Number of BOP slots being requested for the DBS.
NumberOfDescendents | PHY Channel ID | See 8.1.2 | Value to set the The Number of the Descendant field in the DBS request: indicates the actual or expected number of descendant PAN coordinators. Set as zero if the PAN coordinator is not clear about how many descendants it will have.
SecurityLevel | As defined in Table 48 |  | 
KeyIdMode |  |  | 
KeySource |  |  | 
KeyIndex |  |  | 

## Slide 10: 6.2.23.1 MLME-DBS.request (p46) Table 14—MLME-DBS.request Parameters (after)
Name | Type | Valid range | Description
RequesterCoordAddr | Device Short address | 0x0000‐0xffff | The short device address of the (original) source requester PAN coordinator.
RequestType | Enumeration | ALLOCATION, DEALLOCATION | If the request is for allo‐cation or deallocation of TMCTP DBS.
DBSLength | Integer | 0x00‐0xff | Number of BOP slots being requested for the DBS.
NumberOfDescendents | Integer | 0x00‐0xff | The actual or expected number of descendant PAN coordinators. Set as zero if the PAN coordinator is not clear about how many descendants it will have.
SecurityLevel | As defined in Table 48 |  | 
KeyIdMode |  |  | 
KeySource |  |  | 
KeyIndex |  |  | 

## Slide 11: 6.2.23.2 MLME-DBS.indication (p47) Table 15—MLME-DBS.indication Parameters (before)
Name | Type | Valid range | Description
CoordAddress | Device Short address | 0x0000‐0xffff | The short address of the Coordinator that sent TMCTP DBS Request
RequesterCoordAddr | Device Short address | 0x0000‐0xffff | The short device address of the (original) source requester PAN coordinator.
DBSLength | Integer | See [xref] | Value of the DBSLength field of the the received TMCTP DBS Request
RequestType | Enumeration | ALLOCATION, DEALLOCATION | If the request is for allocation or deallocation of TMCTP DBS.
NumberOfDescendents | PHY Channel ID | See 8.1.2 | Value to set the The Number of the Descendant field in the DBS request: indicates the actual or expected number of descendant PAN coordinators. Set as zero if the PAN coordinator is not clear about how many descendants it will have.
SecurityLevel | As defined in Table 48 |  | 
KeyIdMode |  |  | 
KeySource |  |  | 
KeyIndex |  |  | 

## Slide 12: 6.2.23.2 MLME-DBS.indication (p47) Table 15—MLME-DBS.indication Parameters (after)
Name | Type | Valid range | Description
CoordAddress | Device Short address | 0x0000‐0xffff | The short address of the Coordinator that sent TMCTP DBS Request
RequesterCoordAddr | Device Short address | 0x0000‐0xffff | The short device address of the (original) source requester PAN coordinator.
RequestType | Enumeration | ALLOCATION, DEALLOCATION | If the request is for allocation or deallocation of TMCTP DBS.
DBSLength | Integer | 0x00‐0xff | Value of the DBSLength field of the received TMCTP DBS Request
NumberOfDescendents | integer | 0x00‐0xff | The actual or expected number of descendant PAN coordinators. Set as zero if the PAN coordinator is not clear about how many descendants it will have.
SecurityLevel | As defined in Table 48 |  | 
KeyIdMode |  |  | 
KeySource |  |  | 
KeyIndex |  |  | 

## Slide 13: 6.2.23.3 MLME-DBS.response (p48) Table 16—MLME-DBS.response Parameters (before)
Name | Type | Valid range | Description
CoordAddress | Device Short address | 0x0000‐0xffff | The short address of the Coordinator that sent TMCTP DBS Request
RequesterCoordAddr | Device Short address | 0x0000‐0xffff | The short device address of the (original) source requester PAN coordinator.
DBSStartingSlot | Integer | See [xref] | The first slot of the allocated DBS in the BOP
DBSLength | Integer | See [xref] | The size, in BOP slots, of the allocated DBS.
ChannelNumber | PHY Channel ID | See 8.1.2 | The channel number that the coordinator intends to use for all future communications
ChannelPage | Integer | See 8.1.2 | The channel page that the coordinator intends to use for all future communications.
StartingChNum | PHY Channel ID | See 8.1.2 | The lowest channel number, which is assigned by the parent PAN coordinator
EndingChNum | PHY Channel ID | See 8.1.2 | The highest channel number, which is assigned by the parent PAN coordinator

## Slide 14: 6.2.23.3 MLME-DBS.response (p48) Table 16—MLME-DBS.response Parameters (after)
Name | Type | Valid range | Description
CoordAddress | Device Short address | 0x0000‐0xffff | The short address of the Coordinator that sent TMCTP DBS Request
RequesterCoordAddr | Device Short address | 0x0000‐0xffff | The short device address of the (original) source requester PAN coordinator.
DBSStartingSlot | Integer | 0x0000‐0xffff | The first slot of the allocated DBS in the BOP
DBSLength | Integer | 0x00‐0xff | The size, in BOP slots, of the allocated DBS.
ChannelNumber | PHY Channel ID | See 8.1.2 | The channel number that the coordinator intends to use for all future communications
ChannelPage | Integer | See 8.1.2 | The channel page that the coordinator intends to use for all future communications.
StartingChNum | PHY Channel ID | See 8.1.2 | The lowest channel number, which is assigned by the parent PAN coordinator
EndingChNum | PHY Channel ID | See 8.1.2 | The highest channel number, which is assigned by the parent PAN coordinator

## Slide 15: 6.2.23.3 MLME-DBS.response (p48) Table 16—MLME-DBS.response Parameters (after)
Name | Type | Valid range | Description
SecurityLevel | As defined in Table 48 |  | 
KeyIdMode |  |  | 
KeySource |  |  | 
KeyIndex |  |  | 
Table 16 (continued)

## Slide 16: 6.2.23.4 MLME-DBS.confirm (p49) Table 17—MLME-DBS.confirm Parameters (before)
Name | Type | Valid range | Description
RequesterCoordAddr | Device Short address | 0x0000‐0xffff | The short device address of the (original) source requester PAN coordinator.
DBSStartingSlot | Integer | See [xref] | The first slot of the allocated DBS in the BOP
ChannelNumber | PHY Channel ID | See 8.1.2 | The channel number that the coordinator intends to use for all future communications
ChannelPage | Integer | See 8.1.2 | The channel page that the coordinator intends to use for all future communications.
StartingChNum | PHY Channel ID | See 8.1.2 | The lowest channel number, which is assigned by the parent PAN coordinator
EndingChNum | PHY Channel ID | See 8.1.2 | The highest channel number, which is assigned by the parent PAN coordinator

## Slide 17: 6.2.23.4 MLME-DBS.confirm (p49) Table 17—MLME-DBS.confirm Parameters (before)
Name | Type | Valid range | Description
Status | Enumeration | SUCCESS, (TBD), NO_ACK, DENIED, UNAVAILABLE_KEY, UNSUPPORTED_SECURITY, INVALID_PARAMETER | The status of the attempt of the allocation of a DBS and a channel.
Table 16 (continued)

## Slide 18: 6.2.23.4 MLME-DBS.confirm (p49) Table 17—MLME-DBS.confirm Parameters (after)
Name | Type | Valid range | Description
RequesterCoordAddr | Device Short address | 0x0000‐0xffff | The short device address of the (original) source requester PAN coordinator.
DBSStartingSlot | Integer | 0x0000‐0xffff | The first slot of the allocated DBS in the BOP
ChannelNumber | PHY Channel ID | See 8.1.2 | The channel number that the coordinator intends to use for all future communications
ChannelPage | Integer | See 8.1.2 | The channel page that the coordinator intends to use for all future communications.
StartingChNum | PHY Channel ID | See 8.1.2 | The lowest channel number, which is assigned by the parent PAN coordinator
EndingChNum | PHY Channel ID | See 8.1.2 | The highest channel number, which is assigned by the parent PAN coordinator

## Slide 19: 6.2.23.4 MLME-DBS.confirm (p49) Table 17—MLME-DBS.confirm Parameters (after)
Name | Type | Valid range | Description
Status | Enumeration | SUCCESS, (TBD), NO_ACK, DENIED, UNAVAILABLE_KEY, UNSUPPORTED_SECURITY, INVALID_PARAMETER | The status of the attempt of the allocation of a DBS and a channel.
Table 16 (continued)