## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Merged Comments to TGD (Draft and Clean)]
Date Submitted: [15 November 2012]
Source: [Seung-Hoon Park] Company [Samsung Electronics]
Address [416, Maetan-3Dong, Yeongtong-Gu, Suwon-Si, Gyeonggi-Do, 443-742, Korea]
Voice:[+82-10-9349-9845], FAX: [+82-31-279-0813], E-Mail:[shannon.park@samsung.com]
Re: [.]
Abstract: [Merged comments to revise TGD draft document (based on DCN385-06) and TGD clean document (based on DCN568-00)]
Purpose: [To summary and compare comments to TGD draft and clean document]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Merged Comments to TGD
November 12, 2012
Seung-Hoon Park

## Slide 3: Comments to Agreed Texts to 6.3 Discovery
Commenter | Comments
Shannon Park | Modify texts in 6.3 as follows: “Energy-efficient discovery”  “Energy-efficient discovery including (e.g. low duty cycle)” “Support high PD density” “Support high PD density and high peer discovery traffic” Comments: a PD may have several peer IDs when using several applications.

## Slide 4: Comments to Disagreed Texts
Not yet gathered

## Slide 5: New Comments to 5.4 Operating modes
Commenter | Comments
Eldad Zeira | Add new sub-clause 5.4 “Operating modes” Add new texts into 5.4 as follows: “IEEE 802.15.8 All PDs shall support at least one common communication mode.”
PAC group | Proposers can suggest their own common communication mode. Only proposals for common communication mode will be compared by performance metric and evaluation criteria. Proposals Possible operating modes -

## Slide 6: New Comments to 6.3 Discovery
Commenter | Comments
PAC group (11.14) summarized by Marco Hernandez | Add new texts into 6.3 as follows: “Discovery IDs For the purpose of discovery of PAC peers, the discovery signal contains a frame of data that proposers may use for the following identifiers: Device ID. This is a unique identifier for compliant PDs. Example: device MAC address. Application ID. This identifies a specific application or set of applications enable in a PD by a PAC peer. Example: social networking, emergency, gaming, advertising, etc. Application type ID is included as well. Note that it is up to proposers to present how to support identification of applications. Example: Application type ID plus application ID.

## Slide 7: New Comments to 6.3 Discovery
Commenter | Comments
PAC group (11.14) summarized by Marco Hernandez | Application specific user ID. This is the user ID linked to a specific application. Note that we only reserve a group of bits for this identifier that will be used by an application to place a user name. Group ID. This identifier is used to form selected groups of peers. Peer or peer ID is defined as the application specific user ID. Note that it is up to the proposer how to use and implement these identifiers or to use part of them."

## Slide 8: New Comments to 6.3 Discovery
Commenter | Comments
Jinyoung Chun | Modify Marco’s summary as follows: Application type ID. This identifies set of applications enable in a PD by a PAC peer. Example: social networking, emergency, gaming, advertising, etc. Application ID. This identifies a specific application or set of applications enable in a PD by a PAC peer. Example: social networking, emergency, gaming, advertising, etc. Application type ID can be is included as well. Note that it is up to proposers to present how to support identification of applications. Example: Application type ID plus application ID.

## Slide 9: New Comments to 2.2 Definition
Commenter | Comments
PAC group (11.15) Discussion | Add new texts into 2.2 as follows: “ - Device ID: e.g. MAC address . This is a unique identifier for a compliant PD. - Device group ID: . This is a unique identifier for a group of compliant PDs. - Application type ID: . This identifies a class of specific applications enabled in a PD. . e.g. SNS, gaming, etc. - Application-specific ID: . This identifies a specific application enabled in a PD. . e.g. Facebook, Twitter, Space Invaders, etc. - Application-specific user ID: . This is the user account ID linked to a specific application. . e.g. account@facebook - Application-specific group ID: . This identifies a group of selected Application-specific users. - Peer is equal to Application-specific user ID. “

## Slide 10: New Comments to 6.3 Discovery
Commenter | Comments
Eldad Zeira | Modify Marco’s summary as follows: For the purpose of discovery of PAC peers, the discovery signal contains a frame of data that proposers may use for the conveys information that may reflect one or more of the following identifiers:IDs such as Device ID, Device Group ID, Application type ID, Application-specific ID, Application-specific user ID, Application-specific group ID: … Note that it is up to the proposer implementer how to use and implement these identifiers or to use part of them.“ Add new texts into 6.3 as follows: “A PD may use multiple discovery identities at the same time.”

## Slide 11: New Comments to 6.3 Discovery
Commenter | Comments
Shannon Park | Add new texts into 6.3 as follows: “IEEE 802.15.8 mayshall support that a peer ID is discovered to only other peers who is in the same application-specific ID/group ID or the designated application-specific ID/group ID.” “IEEE 802.15.8 mayshall support privacy that a PD is not tracked when a user manipulate not to broadcast the peer identity of the peer.” “IEEE 802.15.8 may shall provide support proximity-based presence functionality that a PD shall recognizes another peer entering in the proximity as well as the peer going out of the proximity.” “IEEE 802.15.8 may shall provide support state-based presence functionality that a PD shall recognize another peer activation as well as the peer deactivation. support that a user recognizes the activation status of peers.”

## Slide 12: New Comments to 6.16 Requirements for high layer and infrastructure interaction
Commenter | Comments
Eldad Zeira | Add new texts into 6.16 as follows: “A discovery identity of a PD is derived from higher layers. Discovery identity may be pre-configured e.g. for the purpose of relaying. How to handle discovery and peering in the absence of higher layers, infrastructure access or sufficient pre-configuration information is out of scope for 802.15.8-PAC.”

## Slide 13: New Comments to 7.4 Error Rate
Commenter | Comments
Marco Hernandez | Add new texts into 7.4 as follows: "Transmission range from a PD to another PD of at least 500 200 meters shall be supported for the lowest link bit rate in proposed frequency band, excluding 2.4GHz, 5GHz, or the UWB band, which has a value of 10 m. At this transmission range, the packet error rate (PER) shall be less than or equal to 10% for a 128256 octet payload packet size with a link success probability of 95% over all channel conditions as specified in the channel model document per frequency band. Straw poll : 256 vs 512 : 256 won A link success probability of 95% is defined as the PER averaged over the channels that result in the 95% best performance at a given Eb/N0 for a channel model, i.e., the PER performance due to the worst 5% channels at a given Eb/N0 should not be included in the average PER calculation."

## Slide 14: New Comments to 9.3 Simulation scenarios and parameters
Commenter | Comments
Marco Hernandez | The channel model document specifies the following channel model conditions (path loss , small scale fading and scenarios): - Indoor office, outdoor to indoor and pedestrian, vehicular for the 900 MHz band - Outdoor to indoor and pedestrian, vehicular, typical urban for 2.4 GHz band - Model A, B, C, D, E for 5 GHz band. 802.15.4a UWB channel models for UWB band. * comments: licensed bands required e.g. 700MHz for public safety, 1.9GHz, 2.3 GHz, etc.

## Slide 15: New Comments to 9.3 Simulation scenarios and parameters
Commenter | Comments
Shannon Park | Add new sub-clauses into 9.3 as follows: 9.3.1 Link-level simulation (PHY) 9.3.2 System-level simulation (MAC) 9.3.2.1 scenarios & parameters for unpeered PDs (or just PDs) : for discovery phase 9.3.2.2 scenarios & parameters for peered PDs (or PD links) : for communication phase (including unicast, multicast, broadcast) comments For comparison convenience, reference system (e.g. simple CSMA or ALOHA) is required when showing results. (in case of system-level simulation) Suggestion of simulation parameters : for the generality, so I suggest 2.4GHz ISM band and general Wi-Fi parameters.

## Slide 16: Items to be agreed
Common communication mode : All
Regulation : Suh-Wook Kim
Simulation scenarios & parameters for MAC : Shannon & Jin
Definition of latency (discovery, data) : Jiny & Ryu
  Needs clear model of discovery
Channel model for licensed bands
  700MHz : Shannon & Marco
  Refer to 16m EMD (Evaluation Methodology Doc.) : Chan-ho & Marco
  Others?: 16p (M2M) :Shannon
Security (Authentication & key management) : Jun-beom
States of the PD : Eldad
Synchronization : Shannon & Kwak
Relative positioning : J.Kim