## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)‏
Submission Title: [Proposal for TBDs in TVWS-NB-OFDM draft document]
Date Submitted: [November 14, 2012]
Source: [Ryuhei Funada, Hiroshi Harada]
Company [NICT]
Address [3-4, Hikarino-oka, Yokosuka, 239-0847 Japan.]
Voice: [+81-46-847-5092], FAX: [+81-46-847-5440], E-Mail: [funada@nict.go.jp]
Re: [Proposal of TVWS-NB-OFDM for IEEE 802.15.4m Document]
Abstract: [This document proposes additions and modifications of description of the TVWS-NB-OFDM section in the preliminary draft 15-12-0575-00-4m.]
Purpose: []
Notice: [This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.]
Release: [The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.]

## Slide 2: Summary
This document proposes additions and modifications of description of the TVWS-NB-OFDM section in the TG4m preliminary draft 15-12-0575-00-4m.
  20.3.1.4 PSDU field
  20.3.2 System parameters for TVBS-NB-OFDM (Table 142)
  20.3.3.1 Reference modulator diagram
  20.3.3.2.2 Inner encoding
  20.3.3.2.3 Pad bit Insertion
  20.3.5.1 Operating frequency range

## Slide 3: 20.3.1.4, 20.3.2 and 20.3.5.1
20.3.1.4 PSDU field
  The PSDU field carries the data of the PPDU.
20.3.2 System parameters for TVBS-NB-OFDM
20.3.5.1 Operating frequency range
  Removed
Parameter | Mode #1 | Mode #2
STF duration (TSTF) | 1008 (252 x4) us | 
LTF duration (TLTF) | 1008 (504x2) us | 
Table 142 (Continued)
Notes: 20.3.1.4, Description is missing, so the sentence, ‘The PSDU field carries the data of the PPDU’ is addded.
20.3.2 System parameters for TVBS-NB-OFDM, Some of parameters, STF and LTF duration, is TBD in Table 142,
The values we propose are 1008 us, which are determined according to the Preamble part description.

## Slide 4: 20.3.3.1 Reference modulator diagram
The reference modulator diagram is shown in Figure zzz.
Notes: The Reference modulator diagram, missing description are proposed as a same manner of 802.15.4g standard document.

## Slide 5: 20.3.3.2.2 Inner encoding (1/2)
A recursive and systematic convolutional encoder of coding rate R = 1/2, 2/3, 3/4, 7/8 encodes the RS encoded data bits, 6 tail bits, and pad bits. The convolutional encoder shall use the generator polynomials g0 = 171 and g1 = 133, of rate R = 1/2, with feedback connection of g0 as shown in Figure 129.
Notes: What you see here is a modification of Figure of systematic convolutional coder, in which tail bit inserter are added. This is the modification point. Next slide shows tail bit pattern.

## Slide 6: 20.3.3.2.2 Inner encoding (2/2)
The value of the tail bits are dependent on the memory state shown in Figure 129 and shall be set as shown in Table xxx.
Table xxx—Tail bit pattern for the recursive systematic encoder
Memory state (M0–M5) | Tail bits (T0–T5) | Memory state (M0–M5) | Tail bits (T0–T5) | Memory state (M0–M5) | Tail bits (T0–T5) | Memory state (M0–M5) | Tail bits (T0–T5)
000000 | 000000 | 010000 | 100001 | 100000 | 111011 | 110000 | 011010
000001 | 111001 | 010001 | 011000 | 100001 | 000010 | 110001 | 100011
000010 | 001011 | 010010 | 101010 | 100010 | 110000 | 110010 | 010001
000011 | 110010 | 010011 | 010011 | 100011 | 001001 | 110011 | 101000
000100 | 010110 | 010100 | 110111 | 100100 | 101101 | 110100 | 001100
000101 | 101111 | 010101 | 001110 | 100101 | 010100 | 110101 | 110101
000110 | 011101 | 010110 | 111100 | 100110 | 100110 | 110110 | 000111
000111 | 100100 | 010111 | 000101 | 100111 | 011111 | 110111 | 111110
001000 | 101100 | 011000 | 001101 | 101000 | 010111 | 111000 | 110110
001001 | 010101 | 011001 | 110100 | 101001 | 101110 | 111001 | 001111
001010 | 100111 | 011010 | 000110 | 101010 | 011100 | 111010 | 111101
001011 | 011110 | 011011 | 111111 | 101011 | 100101 | 111011 | 000100
001100 | 111010 | 011100 | 011011 | 101100 | 000001 | 111100 | 100000
001101 | 000011 | 011101 | 100010 | 101101 | 111000 | 111101 | 011001
001110 | 110001 | 011110 | 010000 | 101110 | 001010 | 111110 | 101011
001111 | 001000 | 011111 | 101001 | 101111 | 110011 | 111111 | 010010
Notes: The tail bit pattern are added in the draft as a same manner of 802.15.4g standard document as shown in this slide.

## Slide 7: 20.3.3.2.3 Pad bit Insertion
The number of pad bits input to the convolutional encoder, NPAD, shall be computed with to the following equation:
NRS = ceiling (LPSDU /(188*8))
LRS= LPSDU+NRS×16*8
NSYS = ceiling ((LRS +6)/ NDBPS))
NDATA= NSYS* NDBPS
NPAD= NDATA - 8*LRS+6
LPSDU is the number of PSDU bits, which is equal to the content of the Frame Length field in Figure 128, and NDBPS is shown in Table 142.
The function ceiling (.) is a function that returns the smallest integer value greater than or equal to its argument value. The pad bits are set to “zeros”.
Notes: Pad bit insertion section is also an missing part. To use RS code as an outer code, the computation is different from the system using only convolutional code. That’s why.