## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Discovery Latency]
Date Submitted: [2012-11-15]
Source: [RYU Cheol, Sunggeun Jin]
Company: [ETRI, Korea]
Address: [ryuch@etri.re.kr, sgjin@etri.re.kr]
Re: [Draft of TG8 Technical Guidance Document]
Abstract: [Discovery latency is dependent on discovery targets and schemes.]
Purpose: [To discuss the definition of discovery latency]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1

## Slide 2: Wi-Fi P2P Service Discovery
Wi-Fi P2P
Active Device Discovery
Passive Discovery
Service Discovery Request
Service Discovery Agent
( e.g. UPnP Daemon)
P2P Device
P2P Device
Group Formation
Service Discovery Response

## Slide 3: Examples of Discoveries
Peer Discovery by Peer ID
  Query: “Are there peers who logged on twitter with the account ‘bob.johnson’?”
  Response: Device ID
Peer Discovery by Application
  Query: “Are there peers who have ftp server?”
  Response: Device ID
Peer Discovery by Application Type
  Query: “Are there peers who are participating in a social network service and want to be known to neighbors in the proximity?”
  Response: Device ID (, Application ID)

## Slide 4: Discovery schemes
Passive scheme
  Broadcasting-based discovery
Active scheme
  Query-based discovery
Post-association scheme
  Infrastructure-based discovery

## Slide 5: Passive Scheme
A PD broadcasts the following IDs periodically on a common channel;
  Device ID
  Device Group IDs
  Application Type IDs
  Application IDs (?)
  Application User IDs (?)
A PD has to listen on a common channel.

## Slide 6: Active Scheme
A PD can query with questions;
  Device ID (*)?
  Application Type ID (Storage Service)?
  Application ID (Samba)?
  Application User ID (‘bob.johnson’)?
A PD can receive replies in a certain time;
  Device ID, Device Group ID, Application Type ID

## Slide 7: Post-association scheme
After link setup, a PD can query relative long questions. (Bluetooth)
After group formation, a PD can talk via legacy service discovery protocols.

## Slide 8: Proposal
Discovery latency is dependent on discovery targets and schemes, so we can not specify a certain period at this moment.