## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Overview of IEEE 802.16m channel models]
Date Submitted: [9 January 2013]
Source: Chanho Yoon, Seungkwon Cho, Sungkyung Kim, Soojung Jung, Hyungjin Kim, and Sungcheol Chang
Company [ETRI]
Address [] Voice:[], FAX: [],
E-Mail:[chyoon@etri.re.kr]
Re: [In Response to Technical Guidance Document contributions for overview of 2.5GHz licensed band channel models]
Abstract: [Channel models for IEEE 802.16m]
Purpose: [For overview of reference channel models for proposals evaluation to TG8]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Overview of IEEE 802.16m EMD channel models

## Slide 3: Table of Contents
Introduction
  Purpose
  Test Scenarios
  Highlights
System level channel models
  Pass loss models (mandatory)
  Pass loss models (optional)
Link level channel models
  Power delay profile (PDP) for baseline test scenario (mandatory)
  Power delay profile (PDP) for Cluster-Delay-Line models (optional)

## Slide 4: Introduction

## Slide 5: Introduction
Purpose
  To provide sufficient details for evaluating the system proposals to IEEE 802.16m
  Targeting the IMT-Advanced standard
  Provide MIMO channel models as key enabling technology for 802.16m and IMT-Advanced
  Suggested:
    1) Mandatory & optional system level channel models
    2) Mandatory & optional link level channel models

## Slide 6: Introduction
Test scenarios
Scenario/Parameters | Baseline configuration TDD and FDD | NGMN configuration TDD and FDD | Urban Macrocell TDD and FDD
Requirement | Mandatory | Optional | Optional
Site-to-site distance | 1.5km | 0.5km | 1km
Carrier frequency | 2.5GHz | 2.5GHz | 2.5GHz
Operating bandwidth | 10MHz for TDD / 10MHz per UL and DL for FDD | 10MHz for TDD / 10MHz per UL and DL for FDD | 10MHz for TDD / 10MHz per UL and DL for FDD
BS height | 32m | 32m | 32m
BS Tx Power per sector | 46 dBm (4 0W) | 46 dBm (40 W) | 46 dBm (40 W)
MS Tx Power | 23 dBm (200 mW) | 23 dBm (200 mW) | 23 dBm (200 mW)
MS height | 1.5m | 1.5m | 1.5m
Penetration loss | 10 dB | 20 dB | 10 dB
Path loss model | 130.19+37.6*log10(R) (R in km) | 130.19+37.6*log10(R) (R in km) | 35.2+35*log10(d)+26* log10(f/2), (d in meters)
Lognormal shadowing standard deviation | 8dB | 8dB | 8dB

## Slide 7: Introduction
Test scenarios
Scenario/Parameters | Baseline configuration TDD and FDD | NGMN configuration TDD and FDD | Urban Macrocell TDD and FDD
Correlation distance for shadowing | 50m | 50m | 50m
Mobility | 0-120 km/hr | 0-120 km/hr | 0-120 km/hr
Channel mix | ITU Pedestrian B 3 km/hr – 60% ITU Vehicular A 30 km/hr – 30% ITU Vehicular A 120 km/hr – 10% | Low mobility: 3 km/hr UL: typical urban, DL: SCM-C Mixed mobility: ITU Pedestrian B 3 km/hr – 60% ITU Vehicular A 30 km/hr – 30% ITU Vehicular A 120 km/hr – 10% | 3 km/hr – 60% 30 km/hr – 30% 120 km/hr – 10%
Spatial channel model | ITU with spatial correlation | Low mobility: 3 km/hr SCM Mixed mobility: ITU with spatial correlation | 10MHz for TDD / 10MHz per UL and DL for FDD
Error Vector Magnitude (EVM) | 30 dB | N/A | 30 dB

## Slide 8: Introduction
Highlights in system-level channel modeling
  Stochastic models
  Spatial channel modeling
  Mix of different speeds and channel scenarios
  Pass loss, shadowing, cell radius, BS transmission power, antenna pattern, height, MS transmission power, height, gain factor, and etc. are included

## Slide 9: Introduction
Highlights in link-level channel modeling
  Stochastic models
  Incorporated double-directional (reciprocal) impulse response
    Angle of departure (AoD)
    Angle of arrival (AoA)
    Spatial correlation matrix (per tap)
    Consideration of polarization
  Incorporated MIMO matrix channel response
    Antenna patters at transmitter and receiver
    Antenna pattern for horizontal and vertical polarization
    Considered elevation and azimuth
    Spatial correlation matrix (per tap)
  Generation of spatial channels (including MIMO channel)
    1) Correlation based method
    2) Ray based method

## Slide 10: System level channel model

## Slide 11: Pass loss models (mandatory)
1) Carrier frequency
  2.5GHz
2) Uniform height of buildings
  R in km, f in MHz, hBS in meters
3) 15m above rooftop baseline configuration path loss
  R in km
4) lognormal shadowing standard deviation
  8dB

## Slide 12: Pass loss models (optional)
1) Urban Macrocell (f[GHz]: 2 < f < 6)
  BS height: 32m, MS height: 1.5m
2) Suburban Macrocell
  BS height: 32m, MS height: 1.5m
3) Urban Microcell
  BS: height: 12.5m, MS height: 1.5m
  Refer to [1]

## Slide 13: Pass loss models (optional)
5) Indoor Small Office
  Refer to [2]
6) Indoor Hot Spot
  LOS (20m < d < 60m, hBS = hMS = 1~2.5m)
  NLOS (20m < d < 80m, hBS = hMS = 1~2.5m)

## Slide 14: Pass loss models (optional)
7) Outdoor to Indoor
  Refer to [2]
8) Open Rural Macrocell
  Refer to [2]

## Slide 15: Link level channel model

## Slide 16: Baseline test scenario (Mandatory)
Case 1) Uncorrelated antennas at both BS and MS
Case 2) Uncorrelated antennas at MS, correlated antennas at BS
  Spatial correlation calculation
    Derived from 20 sub-paths resulting Laplacian PDF
    Antenna spatial correlation coefficients

## Slide 17: PDP for baseline test scenarios (Mandatory)
Modified ITU baseline channel models
  ITU pedestrian B (6-taps => 24-taps)
  ITU vehicular A (6-taps => 24-taps)
Realization of a time-varying spatial channel
  Correlation based method: antenna correlation for each tap is computed first according the per-tap mean AoA/AoD, per-tap power angular profile, and antenna configuration parameters.
Considered for a 10MHz system bandwidth
  TDD: 10MHz
  FDD: 10MHz for both UL and DL

## Slide 18: PDP for baseline test scenarios (Mandatory)
Modified ITU baseline channel models

## Slide 19: PDP for baseline test scenarios (Mandatory)
Angle parameters

## Slide 20: PDP for baseline test scenarios (Mandatory)
Spatial correlation matrix calculation (correlation based method)
  Derived from 20 sub-paths resulting Laplacian PDF
  Angular spread of 3 degrees
  Inter-element spacing of 4 wavelengths
  Angular offsets of the k-th (k=1,2,..20) sub-path are determined by

## Slide 21: PDP for baseline test scenarios (Mandatory)
Spatial correlation matrix calculation
  Step1) Derivation of antenna spatial correlation at the BS and MS between the p-th and q-th antenna as:
  Step2) Denoting the spatial correlation matrix at BS and MS as RBS,n and RMS,n, the per-tap spatial correlation is determined as
  is a 2x2 matrix if cross-polarized antennas are used at BS and MS

## Slide 22: PDP for baseline test scenarios (Mandatory)
Spatial correlation matrix calculation
  Step3) Generate NxM i.i.d. channels that satisfies Jake’s Doppler spectrum where N is the number of RX antennas and M is the number of TX antennas
  Step4) compute the correlated channel at each tap as

## Slide 23: Cluster-Delay-Line models (optional)
1) Urban Macrocell
2) Suburban Macrocell
3) Urban Microcell
4) Suburban Microcell
5) Indoor Small Office
6) Indoor Hot Spot
7) Outdoor to Indoor
8) Open Rural Macrocell

## Slide 24: Cluster-Delay-Line models
CDL concept
  Referred as conventional tap delayed line models of power delay profile with the addition of
    1) Per-tap AoA, AoD information
    2) Per-tap angular spread (power angular profile) information
  A group of multi-path (taps) components form a cluster
  Each cluster (tap) have 20 equal-power rays with fixed offset angles
    Thus, the ray power is 1/20 of the mean tap power (i.e. -13dB)
  A cluster can be divided into three sub-clusters

## Slide 25: Cluster-Delay-Line models
Urban Macrocell
  XPR = 5dB

## Slide 26: Cluster-Delay-Line models
Urban Macrocell
  XPR = 5dB

## Slide 27: Cluster-Delay-Line models
Bad Urban Macrocell
  XPR = 5dB

## Slide 28: Cluster-Delay-Line models
Suburban Macrocell
  XPR = 5.5dB

## Slide 29: Cluster-Delay-Line models
Urban Microcell
  LOS (Ricean K-factor is 3.3dB)
  XPR = 9.5dB

## Slide 30: Cluster-Delay-Line models
Urban Microcell
  NLOS
  XPR = 7.5dB

## Slide 31: Cluster-Delay-Line models
Bad Urban Microcell
  NLOS
  XPR = 7.5dB

## Slide 32: Cluster-Delay-Line models
Indoor Small Office
  NLOS
  XPR = 10dB

## Slide 33: Cluster-Delay-Line models
Indoor Hotspot
  LOS
  XPR = 11dB

## Slide 34: Cluster-Delay-Line models
Indoor Hotspot
  NLOS, XPR = 11dB

## Slide 35: Cluster-Delay-Line models
Rural Macrocell
  LOS, XPR = 7dB
  Ricean K-factor is 13.7dB

## Slide 36: Cluster-Delay-Line models
Rural Macrocell
  NLOS, XPR = 7dB

## Slide 37: References
[1] IEEE 802.16m-08/004r2
[2] IST-WINNER II Deliverable D1.1.1 v1.0 “WINNER II Interim Channel Models”, December 2006

## Slide 38: Thank You
Any Questions?