## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Security protocol of IEEE 802.15.9 and its implication]
Date Submitted: [Jan, 2013]
Source: [Junbeom Hur, Sungrae Cho]
Company [Chung-Ang University, Korea]
E-Mail:[jbhur@cau.ac.kr, srcho@cau.ac.kr]
Re: [This is the original document]
Abstract: [This documents presents the key management protocol of IEEE 802.15.9 and considers its possibility to utilize it with IEEE 802.15.8]
Purpose: [To improve security protocols of IEEE 802.15.8]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Security protocol of IEEE 802.15.9
& its implication
Junbeom Hur, Sungrae Cho
Chung-Ang University

## Slide 3: Contents
IEEE 802.15.9 Introduction
Description of Key Management Protocol (KMP)
Implication & Discussion

## Slide 4: IEEE 802.15.9 Introduction
Defines a recommended practice for the transport of Key Management Protocol(KMP) for WPANs
Defines a message exchange framework based on information element(IE) as a transport method for KMP datagrams and guidelines for the use of some existing KMPs with the IEEE 802.15.4 and IEEE 802.15.7
  IETF’s HIP (Host Identity Protocol)
  IKEv2 (Internet Key Exchange version 2)
  PANA
  IEEE Std 802.1x
Does not create a new KMP

## Slide 5: Why IEEE 802.15.9 ?
IEEE 802.15.4 and IEEE 802.15.7 have always supported datagram security
However, they have not provided a mechanism for establishing the keys
This results in weak keys, which is a common avenue for attacking the system
Adding KMP support is critical to a proper security framework

## Slide 6: Description
The Key Management Transport is encapsulated in payload IEs.
As key management payload may exceed the MPDU, a frame chaining method (using Forced ACKs) will provide the needed fragmentation support

## Slide 7: KMP IE Format
ID = Varies by standard (i.e. 802.15.4 or 802.15.7)
Length = KMP fragment + 1; maximum value varies by standard
IE Content
  Control Field – 1 byte
  Chaining Flag – 1 bit
    0 = last/only one
  1 = yes chaining
  Multipurpose ID/Chaining count – 7 bits
  First packet provides Multipurpose ID
  ID range 98 – 126, 97 & 127 reserved
  ID = 98 for KMP
  Chain count (1 – 96 to disambiguate count from ID)
  1 = 1st fragment
  2 = 2nd fragment
  96 = last possible fragment
  KMP fragment
  First KMP fragment
  KMP type – 1 byte
  KMP payload fragment
  Additional KMP fragments
  KMP payload fragment
KMP type
1 802.1X
2 HIP
3 IKEv2
4 PANA
5 SAE

## Slide 8: KMP Transport Mechanism
Handle triggers to/from KMP higher layer
  Pass through for KMP payloads
  Triggers from MAC events to KMP
PHY Services
MAC Services
Data MCPS
Information Element Shim
Other IE processes
KMP
DATA higher layer
Key Request
Keys
Data Traffic
IE frames

## Slide 9: Discussion
What about 802.15.8?
Can we adopt existing KMPs like 802.15.9?
  Considering infrastructureless architecture
    Communication architecture
    Security architecture
Should we consider higher layer security?
  KMP in 802.15.9 is deployed above the MAC layer