## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks(WPANs)
Submission Title: Overview of 15.4m
Date Submitted: January 14, 2013
Source: Sangsung Choi (ETRI) and Soo-Young Chang (SYCA)
Contact: Sangsung Choi (ETRI)
Voice: +82 42 860 6831, E-Mail: sschoi@etri.re.kr
Re: TG4m overview presentation for joint meeting with 802.19
Abstract: TG4m overview and status in Jan. 2013
Purpose: To introduce the overview and status of 802.15.4m.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Overview of 15.4m
Sangsung Choi
15.4m Chair

## Slide 3: OVERVIEW OF 15.4m
Overview of 15.4m Group
  The IEEE 802.15 Task Group 4m (TG4m) is chartered
    to specify a physical layer for 802.15.4 and
    to enhance and add functionality to the existing standard 802.15.4-2006 MAC
  meeting TV white space regulatory requirements.
Scope of Standard
  This amendment specifies
    a physical layer for 802.15.4 meeting TV white space regulatory requirements in as many regulatory domains as practical and
    also any necessary Media Access Control (MAC) changes needed to support this physical layer.
  The amendment enables operation in the VHF/UHF TV broadcast bands between 54 MHz and 862 MHz,
    supporting typical data rates in the 40 kbits per second to 2000 kbits per second range, to realize optimal and power efficient device command and control applications.
Purpose of standard
  The purpose of this amendment is to allow 802.15.4 wireless networks to take advantage of the TV white space spectrum for use in large scale device command and control applications.

## Slide 4: CURRENT STATUS
The 1st meeting for SG4TV was held at LA in January 2011.
  Thee meetings were held for providing PAR & 5C.
TG4m 4TV was approved in September 2011.
  The 1st meeting was held in Okinawa.
  Technical Guidance Document (TGD) discussed and finalized
  Three meetings in Nov. 2011 at Atlanta, Jan. 2012 at Jacksonville, and Mar. 2012 in Hawaii
Call for Preliminary Proposals and Call for Final Proposals
  The Calls closed on May 6, 2012 and on July 9, 2012 respectively with 4 final PHY Proposals & 4 final MAC Proposals
Proposals merged into five areas in Sep. 2012
  Five documents adopted as baseline documents for standard drafting
First drafting done by editors in Nov. 2012
The final draft for TG4m comment resolution is being done by editors in Jan. 2013

## Slide 5: SEVEN PROPOSALS INITIALLY PROPOSED
PHY area
MAC area
No | DoC # | Title | Presenter (Affiliation)
1 | 15-12-0332-03 | ETRI OFDM PHY Proposal for TG4m | Cheol-ho Shin (ETRI)
2 | 15-12-0334-02 | ETRI FSK PHY Proposal for TG4m | Mi-Kyung Oh (ETRI)
3 | 15-12-0336-00 | Full Proposal on PHY for IEEE 802.15.4m | Hiroshi Harada (NICT)
4 | 15-12-0338-00 | PHY Proposal to TG4m | Cristina Seibert (SSN)
No | DoC # | Title | Presenter (Affiliation)
1 | 15-12-0328-01 | Proposed Approach for MAC changes for TVWS | Benjamin A. Rolfe (BCA)
2 | 15-12-0333-01 | IEEE802.15.4m MAC Proposal: TVWS Multi-Channel Utilization (TMCU) | Youngae Jeon (ETRI)
3 | 15-12-0335-01 | MAC proposal for supporting the TVBD network | Seong-Soon Joo (ETRI)
4 | 15-12-0336-00 | Full Proposal on PHY for IEEE 802.15.4m | Hiroshi Harada (NICT)

## Slide 6: FIVE MERGED PROPOSALS
Five merged proposals after merger efforts
  In five areas: FSK-PHY, OFDM-PHY, NB OFDM-PHY, MAC, and Ranging
These five documents were adopted as baseline documents for standard drafting.
The latest version of draft: 15-12-0575-01-004m Primary Draft for TG4m
No | DoC # | Title | Presenter (Affiliation)
1 | 15-12-0483-00-004m | tvws-fsk-merged-proposal-draft | Cristina Seibert (SSN)
2 | 15-12-0481-01-004m | ofdm-phy-merged-proposal-for-tg4m | Soo-Young Chang (SYCA)
3 | 15-12-0511-01-004m | tvws-nb-ofdm-merged-proposal-to-tg4m | Hiroshi Harada (NICT)
4 | 15-12-0513-00-004m | merged-mac-proposal-summary | Benjamin A. Rolfe (BCA)
5 | 15-12-0473-01-004m | suggested-baseline-for-optional-tg4m-ranging | Mi-Kyung Oh (ETRI)

## Slide 7: SUMMARY OF MERGED PROPOSALS, FSK
System parameters
Freq. Band | Parameter | Mode #1 | Mode #2 | Mode #3 | Mode #4 | Mode #5
All available TVWS bands | Data rate (kbps) | 50 | 100 | 200 | 300 | 400
 | Modulation level | 2-level | 2-level | 2-level | 2-level | 4-level
 | Modulation index h | 0.5 or 1.0 | 0.5 or 1.0 | 0.5 or 1.0 | 0.5 | 0.33
 | Channel spacing (kHz) | 100 if h=0.5 200 if h=1.0 | 200 if h=0.5 400 if h=1.0 | 400 if h=0.5 600 if h=1.0 | 600 | 600

## Slide 8: SUMMARY OF MERGED PROPOSALS, OFDM
System parameters
Description | Mandatory mode | Optional mode (4 times overclock mode)
Nominal bandwidth (kHz) | 1064.5 | 4258
Channel spacing (kHz) | 1250 | 4*1250
Subcarrier spacing (kHz) | 1250/128 | 4*1250/128
DFT Size | 128 | 128
Number of pilot tones | 8 | 8
Number of data tones | 100 | 100
BPSK ½ rate (kbps) | 390.625: MCS0 Mode | 1562.5: MCS3 Mode
QPSK ½ rate (kbps) | 781.250: MCS1 Mode | 3125: MCS4 Mode
16-QAM ½ rate (kbps) | 1562.5: MCS2 Mode | 6250: MCS5 Mode

## Slide 9: SUMMARY OF MERGED PROPOSALS, NB-OFDM
System parameters
Description | Mode #1, Mode #2
Nominal bandwidth (kHz) | 389.95
Subcarrier spacing (kHz) | 0.99206 (125kHz/126)
Number of pilot tones | 32
Number of data tones | 352
Effective symbol duration (us) (TFFT) | 1008
Guard interval (TGP) | 1/32 (31.5us) as mandatory 1/16 (63us) as optional 1/8 (126us) as optional
Symbol interval (us) | 1039.5 as mandatory 1071.0 as optional 1134.0 as optional (TFFT+TGP)

## Slide 10: SUMMARY OF MERGED PROPOSALS, MAC
TVWS channel enabling
  Information elements to enable TVWS specific information exchange to support TVWS channel access (topology independent)
Functional extensions to enhance low energy operation
Enhanced support for cluster-tree network topologies (TVWS Multichannel Cluster Tree PAN)
Extended support for direct device-to-device data transfer in beacon enabled PANs
  peer-to-peer (not through PAN coordinator)
  Support for multicast
Low Energy enhancements for TVWS operation
Support for dynamic band, channel and PHY operating parameter changes
Support for TVWS PHY capabilities exchange
Support for ranging (localization)
Support for general probe/response
Additions to MAC commands, MLME, MCPS to support additional functions

## Slide 11: SUMMARY OF MERGED PROPOSALS, RANGING
Support for ranging is optional.
Ranging procedure for TG4m
  Basically two-way ranging (TWR) as in 15.4a
A TVWS WPAN PHY that supports ranging shall support a ranging counter.
For ranging counter operation
  RMARKER
    Boundary between SHR & PHR for both FSK/OFDM PHYs
  Ranging bit
    Use one of reserved bits in PHR
  ToA estimation
    Use SHR for both FSK/OFDM PHYs
Informative Annex for FSK/OFDM PHY based ranging is being added to the standard for guideline.

## Slide 12: FUTURE PLAN AND TIMELINE
Drafting
  Preliminary draft with TBDs November 2012
  Complete draft document January 2013
  Final draft for WG Letter Ballot March 2013
  Letter Ballot Comment resolution May 2013
Balloting
  1st Recirculation & Comment Resolutions July 2013
  2nd Recirculation & Comment Resolutions September 2013
  3rd Recirculation & Comment Resolution November 2013
  1st SB Recirculation & Comment Resolutions January 2014
  2nd SB Recirculation March 2014
RevCom Approval
  EC approval July 2014