## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Coexistent technical proposal for wearable 15.4n device
Date Submitted: January 14, 2013
Source:
Kenichi Mori (individual), Shinsuke Hara (QoL-SN), Kaoru Yokoo (Individual)
ken1.morius@gmail.com, shinsukehara0122@gmail.com, kaoru.yokoo.ieee@gmail.com
Masahiro Kuroda (QoL-SN,NICT)
marsh@nict.go.jp
Abstract: Coexistent technical proposal for wearable 15.4n device
Purpose: Lower power consumption modulation scheme consistent with OQPSK Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Our proposal
In addition to “15-12-0588-02-004n-technical-proposal-for-wearable-15-4n-device” we discussed at the last meeting, we propose a harmonization in modulation schemes with OQPSK.

## Slide 3: GFSK coexistence with OQPSK
GFSK is common in IEEE802.15.6 and 15.4g
GFSK is very power-efficient, because it has a constant envelop nature
Transmission power limit of 10mW should be applied to not only DSSS OQPSK PHY but also GFSK PHY, which allows to support on-body/off-body wireless communications (bed-side monitoring) as well as on-body/on-body and on-body/in-body wireless communications
Parameterize the use of BT, such as BT=0.3 or =0.5

## Slide 4: Our GFSK proposal
Our GFSK supports 200kbps-data transmission rate per 500kHz channel spacing
200kbps is affordable for medical devices to retrieve data from human body including high-demanding 12-lead ECG (16bits, 1ms)
Ideal PSD of GFSK
Simulation condition
Same modulation scheme as
IEEE802.15.4g
Modulation index = 0.5
BT of Gaussian filter = 0.5
Note: An example of BT=0.5 in the Gaussian low pass filter.
500kHz
-46dBr

## Slide 5: Our GFSK proposal (cont.)
Our band plan is shown as below
a) Good coexistence with OQPSK
b) Large number of channels (see annex)
c) Channel overlapping by 0.5 channel bandwidth if needed
- relax ACLR spec that gives impact to an out-band system - easy to find unoccupied frequency band
d) Support up to 400kbps by 2 channels aggregation
freq.
OQPSK
2MHz mode
OQPSK
2MHz mode
OQPSK
2MHz mode
OFDM
(DTV)
500kHz
freq.
a,b
c
frequency boundary between 4n and another system
Half shift can relax leakage power spec to an out-band systems
c
d

## Slide 6: Band Plan
Frequency Band [MHz] (BW) | Modulation | Bit Rate [kb/s] | Channel Spacing [kHz] | Number of Channels
174 – 216 (42MHz) | Filtered FSK | 200 | 400 | 105
407-425 (18MHz) | Filtered FSK | 200 | 400 | 45
608-630 (22MHz) | Filtered FSK | 200 | 400 | 55
In a case without considering channel overlapping

## Slide 7: Summary
Filtered FSK and/or O-QPSK are preferable for wearable devices used for healthcare applications in hospitals and clinics and filter type is proposed
Band plan is proposed