## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Considerations of parameters for IEEE 802.15.4q
Date Submitted: Jan 15, 2013
Source: Kiran Bynam, Jinesh.P.Nair, Youngsoo Kim [Samsung Electronics]
E-Mail: kiran.bynam@samsung.com
Abstract: This document describes authors view of some technical parameters dependig on applications discussed in SG4q
Purpose: This document describes authors view of some technical parameters dependig on applications discussed in SG4q
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Conideration of Parameters to ULP
Kiran Bynam

## Slide 3: Objective
Review of application Matrix
To comment on the Range and data rates required for TG4q
To calculate the sensitivity based on channel models and spectrum chosen
On Power consumption in view of the coin cell batteries

## Slide 4: Application Matrix
Application domain | Data rate | Range | Number of nodes
Health (gluco meters, single node ECG sensor, patient monitoring) | upto 200 kbps | 10 m | 10
Health(ECG, EEG) | Upto 1 Mbps | 5 m | 15
Home Automation | Upto 100 Kbps | 15 -30 m | 10
Inventory management | Upto 320 Kbps | 100 m | 1000
Industrial monitoring | Upto 100 kbps | 100 m | 1000
Telecom service | Upto 1 Mbps | 15 m | 1

## Slide 5: Comments on Data rate and Range
Data Rate
  All applications require below 300 kbps data rate
  Only EEG application in health care requires upto 1 Mbps
Range
  Typical range required for the given application is 15-30 m
  Only Industrial and Inventory management applications require higher Range

## Slide 6: Other Considerations for Low Power
Transmit Power is an important concern for ULP
  it would not be apt on increase transmit power level above 7 dBm ( 5 mW)
  For 7 dBm transmit Power (PA + Pre-Processing) would be 10 mW (50 % PA loss)

## Slide 7: Path Loss Component
Frequency of operation (MHz) | Distance (m) | environment | Path Loss (dB)
2400 | 10 | Indoor | 69.6
2400 | 30 | Indoor | 83.9
900 | 10 | Indoor | 61.52
900 | 30 | Indoor | 75.84
2400 | 10 | Outdoor LOS | 59.89
2400 | 30 | Outdoor LOS | 69.3
900 | 10 | Outdoor LOS | 51.41
900 | 30 | Outdoor LOS | 68
Ref erences:
ITU-R P.1411-6 “Propagation methods for the planning of short range outdoor radiocommunication systems and radio local area networks in the frequency range 300 MHz to 100 GHz” 02/2012
ITU-R P.1238-7 “Propagation data and prediction methods for the planning of indoor radiocommunication systems and radio local area networks in the frequency range 900 MHz to 100 GHz” 02/2012

## Slide 8: Received Power and SNR Margin
2400 MHz
Noise at 5 MHz Bandwidth = -107 dBm
Noise Figure = 15 dB
TotalNoise = -92 dBm
Rx Power at Receiver = 7 dBm – 84 dB = -77 dBm (15 dB Margin for SNR)
900 MHz
Noise at 5 MHz Bandwidth = -107 dBm
Noise Figure = 15 dB
TotalNoise = -92 dBm
Rx Power at Receiver = 7 dBm – 76 dB = - 69dBm (23 dB Margin for SNR)

## Slide 9: PHY Power Consumption
As this is primarily a PHY amendment, only active Power should be considered
Active Power in Rx differs from state to state
Active Power in Tx is dependent on EIRP
Active Power for Rx for each state should be less than 15 mW
  Power consumption with 0 bytes payload length
  Power consumption with 20 bytes payload length
  All Receiver Power should be measured at Rx Sensitivity
Active Power for Tx for a given EIRP < 15 mW
  Power consumption for all data rates @ 7 dBm transmit Power

## Slide 10: Review of Applications
Application domain | Data rate | Range | Number of nodes
Health (gluco meters, single node ECG sensor, patient monitoring) | upto 20 kbps | 10 m | 10
Health(ECG, EEG) | Upto 1 Mbps | 5 m | 15
Home Automation | Upto 10 Kbps | 15 -30 m | 10
Inventory management | Upto 320 Kbps | 100 m | 1000
Industrial monitoring | Upto 100 kbps | 100 m | 1000
Telecom service | Upto 1 Mbps | 15 m | 1

## Slide 11: Summary
Request the group for considering the below parameters
  Minimum Transmit Power of 7 dBm
  Minimum Range required is 30 m
  Data rates scalable from 250 kbps to 1 Mbps
  Criteria for Power consumption is discussed